## Slide 1: Roanoke River, Tinker Creek, and Wolf Creek TMDL Study
A water quality study for watersheds in the City of Roanoke, Roanoke County, and Botetourt County
Aerin Doughty
TMDL Coordinator
April 10, 2024

## Slide 2: Our goals for today…
Share DEQ’s water quality improvement process
  Provide information on the streams of interest
  Define Total Maximum Daily Loads (TMDL)
  Discuss stressor identification process
  Explore next steps and opportunities for engagement
Receive community feedback – we want to hear from you!

## Slide 3: Agenda
Background and TMDL Development
  Virginia Stream Condition Index
  Impairments
  TMDL
Benthic Stressor Analysis Overview - Dr. R. Brent
  Monitoring/Data
  Approach
  Conclusions
Wrap-up and Next Steps by DEQ Staff
  Public Comment Period
  Community Engagement vs. TMDL Advisory Group
  Study/Modeling/Implementation
Questions

## Slide 4: Virginia’s Water Quality Process

## Slide 5: Background: Clean Water Act
The Clean Water Act requires that all waters meet water quality standards that promote healthy water use.
To meet the goals of the Clean Water Act, Virginia established water quality standards.

## Slide 6: Virginia’s Water Quality Standards
Water quality standards protect these six designated uses:
  aquatic life
  wildlife
  fishing
  shellfish
  swimming
  drinking water

## Slide 8: Why Benthic Macroinvertebrates?
Biological Indicators
Vary in their sensitivity to or tolerance of pollution
  Known pollution tolerance values (0-10)
  Respond to changes in water quality
Widespread, found in all aquatic environments
Limited mobility; spend 1-3 years in the water as larvae or nymphs
Biological monitoring gives a longer-term picture of water quality

## Slide 9: Aquatic life impairments are visible and quantifiable.

## Slide 10: Virginia Stream Condition Index (VSCI)
Benthic macroinvertebrates are collected, sorted, and identified
Each sample produces a score that is driven primarily by the types and diversity of organisms found
Pollution sensitivity affects the score

## Slide 11: Virginia Stream Condition Index (cont.)
VSCI scores tell us that there is an impairment but not what the pollutant is…

## Slide 13: Roanoke River Biomonitoring Data Station: 4AROA198.08
Low VSCI scores are driven by % Mayflies, % Stoneflies and Caddisflies, and % Scrapers
Sample Year
VSCI
2020
2021
2022
2023

## Slide 14: Tinker Creek Biomonitoring Data Station: 4ATKR000.69
2022
2021
2020
2019
2015
2016
2017
2018
Low VSCI scores are driven by % Mayflies, % Stoneflies and Caddisflies, and % Scrapers
VSCI
2023
Sample Year

## Slide 15: Wolf Creek Biomonitoring Data Station: 4AWOR000.34
2022
2021
2020
2019
2015
2016
2017
2018
Low VSCI scores are driven by % Mayflies, % Stoneflies and Caddisflies, and % Scrapers
VSCI
2023
Sample Year

## Slide 16: What is a TMDL?
A Total Maximum Daily Load (TMDL) is the maximum amount of a pollutant that a waterbody can receive and still meet water quality standards.
A TMDL includes:
  Identifying sources of pollution causing impairments
    Aquatic Life Impairment
  Modeling their path to the stream
  Determining the reductions needed from each source to meet the standard

## Slide 17: TMDL? A kind of “Pollution Diet”
Pollutant load in the stream currently
Pollutant load the stream can accept and meet WQS
TMDL Endpoint

## Slide 18: TMDL? A kind of “Pollution Diet”
Pollutant load in the stream currently
Pollutant load the stream can accept and meet WQS
TMDL Endpoint
Water pollution is described by its source. There are two source types,
Point Sources and Non-Point Sources.
Pollution from a point source comes from a direct discharge (ie. effluent discharged to river through an overflow or pipe). Pollution from a non-point source comes from indirect contributions such as stormwater runoff, wind erosion, groundwater seepage, etc.
Pollution Load is the total pollutant from both sources being transported downstream by river flows.

## Slide 19: What pollutants may be leading to aquatic life impairments in the Roanoke River, Tinker Creek, and Wolf Creek?

## Slide 20: Benthic Stressor Analysis
Goal – identify the pollutant(s) responsible for causing the benthic impairment
Process – EPA’s CADDIS approach (Causal Analysis/Diagnosis Decision Information System)
  Identify potential causes
  Analyze lines of evidence
  Determine the probable cause(s)
Like a medical diagnosis

## Slide 21: Potential Causes and Available Data
Available Data Included
  Nearly 400 different water quality parameters
  67 stations
  > 20 years (2000 – 2023)
  > 72,000 data points
  Additional data from
    Western Viriginia Water Authority
    Biological Monitoring, Inc.
    Brown and Caldwell
    Federal Energy Regulatory Commission
    US Geological Survey
General List of Potential Causes
Large Dataset

## Slide 22: Lines of Evidence
For each potential cause, up to 18 different lines of evidence were evaluated
Example Lines of Evidence

## Slide 23: Scoring Lines of Evidence
Each potential cause is then scored for each line of evidence on a -3 to +3 scale

## Slide 24: Example Scoring
Non-Stressors
Possible Stressors
Probable Stressors
Scores for each stream and potential cause are summed
  >0 = non-stressors
  1-3 = possible stressors
  >3 = probable stressors

## Slide 25: CADDIS Overview

## Slide 26: Results
Probable Stressors
  Wolf Creek
    Sediment
  Tinker Creek
    Sediment
    Sediment PCBs
  Roanoke River (202.20)
    Sediment
    Phosphorus
  Roanoke River (198.08)
    Phosphorus
    Nitrogen
    Niagara Dam
Non-Stressors
Possible Stressors
Probable Stressors

## Slide 27: Some Supporting Lines of Evidence – Sediment (Wolf, Tinker, Upper Roanoke)
Total habitat assessment scores
Statistically lower than the reference
Medium probability range for stressor effects

## Slide 28: Some Supporting Lines of Evidence – Sediment (Wolf, Tinker, Upper Roanoke)
Individual habitat metrics

## Slide 29: Some Supporting Lines of Evidence – Sediment (Wolf, Tinker, Upper Roanoke)
Functional feeding group analysis – increase in collectors and filterers

## Slide 30: Some Supporting Lines of Evidence – Nutrients (Roanoke)
Functional feeding group analysis – increase in scrapers

## Slide 31: Some Supporting Lines of Evidence – Nutrients (Roanoke)
Statistically significant regressions between nutrient levels and benthic scores across Roanoke River sites

## Slide 32: Some Supporting Lines of Evidence – Nutrients (Roanoke)
Excess algae growth that increases moving downstream

## Slide 33: Some Supporting Lines of Evidence – Nutrients (Roanoke)
Biological condition gradient attribute analysis showed nutrients as the highest ranked stressor

## Slide 34: Some Supporting Lines of Evidence – Nutrients (Roanoke)
High nitrogen levels – statistically significantly higher than the reference and in the high probability range for stressor effects

## Slide 35: The Controlling Nutrient – Phosphorus or Nitrogen?
Algal growth is typically controlled by the limiting nutrient
Because both phosphorus and nitrogen were identified as probable stressors, both will be carried into the model development phase
At a later point, phosphorus or nitrogen could be removed based on subsequent modeling
Rationale
  CADDIS scores were in the probable stressor range
  Currently don’t have definitive nutrient limitation evidence
  Nutrient limitation may vary spatially and temporally
  Phosphorus controls alone may be inadequate for controlling algae

## Slide 36: Impact of the Niagara Dam
Station 4AROA198.08 is only approximately a mile downstream from the Niagara Dam
Dams are known to cause physical, chemical, and ecological changes that result in immediate downstream benthic impairment
In addition, the dam is likely exacerbating the nutrient impairment by:
  increasing nutrient retention
  reducing the frequency of scouring event and allowing algal communities to proliferate
However, TMDL program is designed to address pollutants only

## Slide 37: Benthic Stressor Analysis Summary
Stream | Probable Stressors | TMDL Target
Wolf Creek | Sediment | Sediment
Tinker Creek | Sediment Sediment PCBs | Sediment
Roanoke River | Phosphorus Nitrogen Sediment Niagara Dam | Phosphorus Nitrogen
Red strikethrough = TMDL already developed
Blue strikethrough = TMDL can only be developed for pollutants

## Slide 38: What happens next…
EPA and SWCB Approval
Completed Benthic Stressor Analysis
First Public Meeting
Final Public Meeting
Public Comment Period
Public Comment Period
April 10, 2024
30 Days
*****May 10th, 2024*****
https://www.deq.virginia.gov/our-programs/water/water-quality/tmdl-development/tmdls-under-development
Opportunity for you to participate
TMDL Development/
Community Engagement Meetings/TAG Meetings

## Slide 39: Community Engagement Meeting or TMDL Advisory Group?
Community Engagement Meetings
  Open to the public
  Anyone in attendance can participate & advise DEQ on TMDL development
TMDL Advisory Group (TAG)
  Set-up upon request
  Replaces community engagement meetings
  Formal panel with approved membership that advises DEQ on TMDL development
    Cross-section of stakeholders
    Members commit to attend multiple meetings
  Open to the public but non-members may only attend as observers

## Slide 40: TMDL Development: The Study Continues
Identity Point Sources
  Permitted discharges
  Construction Permits
Identify Non-point Sources
  Land Use
  Natural hydrologic properties of the area

## Slide 41: TMDL Development: The Model & Reductions
Watershed
Inputs
Computer Model
Model Outputs
Adjust
Calibration
Parameters
Match Observed Data?
No
Yes
Meet TMDL Endpoints?
Yes
Revise Pollutant Reduction
Scenarios Until We Meet
TMDL Endpoints
No
TMDL
Complete

## Slide 42: TMDL Development: The Equation of the Pollution Load
WLA
LA
MOS
TMDL
Wasteload Allocation
Permitted/Point Sources
Load Allocation
Non-point Sources
Margin of Safety
Extra load to account for uncertainty
Total Maximum Daily Load

## Slide 43: What happens next…
EPA and SWCB Approval
Completed Benthic Stressor Analysis
First Public Meeting
Final Public Meeting
Public Comment Period
Public Comment Period
April 10, 2024
30 Days
Opportunity for you to participate
TMDL Development/
Community Engagement Meetings/TAG Meetings

## Slide 44: For comments: aerin.doughty@deq.virginia.gov or 901 Russell Drive Salem, VA 24153 The 30-day public comment period ends May 10 To learn more about TMDLs, visit DEQ’s website: https://www.deq.virginia.gov/our-programs/water/water-quality/tmdl-development To view the Stressor Analysis Document: https://www.deq.virginia.gov/our-programs/water/water-quality/tmdl-development/ tmdls-under-development
Comments, Thoughts, & Questions