## Slide 1: Wolf Creek Watershed Clean Up Study
Initial Public Meeting
Landon Jenkins
TMDL Coordinator, SWRO Regional Office
October 16, 2024

## Slide 2: Goals for our meeting
Share what we know about Wolf creek: Summarize monitoring data, discuss pollutants
Describe process we will use to identify and address pollution in the streams
Describe how you can get involved in this process
Answer your questions about this effort

## Slide 4: Why a study?
Water quality standards designate six uses for surface waters in Virginia. These include:
  Aquatic life
  Fish consumption
  Public water supplies (where applicable)
  Recreation (swimming)
  Shellfishing
  Wildlife
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 5: Aquatic Life Designated Use What does this mean?
All waters should support “the propagation and growth of a balanced, indigenous population of aquatic life”
Benthic impairments, result from violations of the general standard narrative that “waters should be free from substances that are harmful to aquatic life”
Monitor benthic macroinvertebrates (the bugs on the stream bottom) to determine if the standard is met

## Slide 7: Why should we care about bugs?
Consume algae and organic matter  nutrient cycling
Aquatic food chain
Our “canary in the coal mine”
Chemical monitoring = a snapshot in time
  Long lived
  Relatively immobile

## Slide 8: Determining a biological impairment
DEQ biological monitoring data (spring and fall)
VA Stream Condition Index is our barometer
  Diversity, pollution tolerance, feeding group
  Target score of ≥60

## Slide 9: Sensitive to pollution: Mayflies
Photo: Jan Hamrsky: lifeinfreshwater.net
Sensitive to pollution: Mayflies

## Slide 10: Caddisflies
Photo: Jan Hamrsky: lifeinfreshwater.net
Sensitive to pollution: Caddisflies

## Slide 11: Net spinning caddisfly
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 12: Moderately Sensitive: Dragonflies
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 13: Insensitive to Pollution: Blackflies
Photo: Jan Hamrsky: lifeinfreshwater.net

## Slide 14: Virginia Stream Condition Index
60
40
20
Photos: Jan Hamrsky: lifeinfreshwater.net

## Slide 15: Wolf Creek Benthic Monitoring Stations
Notes: Extrapolation, assumes due to no land changes the lower segment will also be impaired

## Slide 16: Impairment Units And Impairment Map
Stream Name | NWBD | Impaired Assessment Units | Cause Group Code | First listed | Length (miles) | Impairment Description
Wolf Creek | TH16 | VAS-O06R_WLF01A98 | O06R-01-BEN | 2002 | 3.33 | Lower mainstem from Town Creek confluence through the Great Knobs, downstream to upper Rt. 75 bridge
Wolf Creek | TH16 | VAS-O06R_WLF03A06 | O06R-01-BEN | 2006 | 2.93 | From upper Rt. 75 bridge near Abingdon downstream to lower Rt. 75 bridge near Green Spring
Wolf Creek | TH16 | VAS-O06R_WLF02B06 | O06R-01-BEN | 2006 | 0.41 | From VDOT bridge number 6035 near Green Spring downstream to South Holston Lake backwaters

## Slide 17: Temporal Trends in Benthic Data For Wolf Creek

## Slide 18: The Benthic Stressor Analysis
The Virginia Department of Environmental Quality (VDEQ) contracted Wetland Studies and Solutions, Inc. and James Madison University (JMU) to conduct a stressor identification analysis for benthic impairments in Wolf Creek in Washington County, VA. Wolf Creek drains most of the Town of Abingdon, Virginia, flows south, and empties into South Holston Lake

## Slide 19: Biological Impairments Determining the Cause…
How the benthic stressor analysis works
  Evaluation of monitoring data
  Comparison with healthy reference watershed data and stressor thresholds
  Weight of evidence approach-evaluates all data
  Identification of most likely stressor(s)
Photo: Jan Hamsky; www.lifeinfreshwater.net
Notes: Weight of Evidence approach evaluates all available information on potential candidate stressors by listing potential candidate stressors identified from the listing information, monitoring data, scientific literature and historic information

## Slide 20: Candidate Stressors
Suspended solids
Deposited sediment
Dissolved oxygen
Phosphorus
Nitrogen
Ammonia
Total dissolved ions
Dissolved chloride
Dissolved sulfate
Dissolved sodium
Dissolved potassium
Dissolved metals
Temperature
Conductivity
pH
Organic matter
Sediment metals
Sediment toxics
Pesticides
Polycyclic Aromatic Hydrocarbons (PAHs)
Polychlorinated Biphenyls (PCBs)

## Slide 21: CADDIS
In this step, James Madison University (JMU) used the Causal Analysis/Diagnosis Decision Information System (CADDIS) (USEPA, 2018a).
The CADDIS approach provides guidance on evaluating various lines of evidence to determine the cause of biological impairments

## Slide 22: CADDIS APROACH

## Slide 23: Evidence Of Sediment As A Stressor With an Increase in Filterers
Notes: This shift in functional feeding group points to an increase in suspended sediment and organic matter. As particulate matter in the water column increases, more food is available for filtering organisms and that feeding niche expands

## Slide 24: Habitat Measurements

## Slide 25: What is a TMDL?
A Total Maximum Daily Load is the maximum amount of a pollutant that a waterbody can receive and still meet water quality standards.

## Slide 26: How do we develop a TMDL? What’s the magic number…
Identify sources of sediment
Model their path to the stream
Determine reductions needed from each source to restore aquatic life
Cropland:
10 tons/yr
Pasture: 12 tons/yr
Residential:
4 tons/yr
Forest:
1 ton/yr
Diagram: Adapted from the Center for TMDL and Watershed Studies at Virginia Tech
Urban:
8 tons/yr
Cropland:
30% reduction
Pasture: 40% reduction
Residential:
50% reduction
Forest:
0% reduction
TMDL
Sediment load = 19 tons/yr
Urban:
75% reduction
Impaired stream
Sediment load = 37 tons/yr
Point sources:
2 tons/yr
Point sources:
0% reduction

## Slide 27: This Is More Than Just Numbers
Primary objective is to address pollution in our waterways
TMDL study is the first step
Followed by an implementation plan
Implementation through partnerships with local organizations
Photo: Jan Hamsky; www.lifeinfreshwater.net

## Slide 28: How can you get involved? We need to hear from you!!!
Participate in Community Engagement Meetings
  Represents the local community
  Provides feedback on
    Land use
    Pollutant sources
    Key stakeholders and community meetings

## Slide 29: Join us for the first Community Engagement Meeting! Mid-Late January Time Preference??? Location Preference???
What’s Next?

## Slide 30: Questions & Comments
30-day public comment period (October 16-November 15)
Send comments to:
Landon Jenkins
355 A Deadmore St SW
Abingdon, VA 24210
landon.jenkins@deq.virginia.gov