## Slide 1: Module 2
Managing Runoff

## Slide 2: Table of Contents
2a. Stormwater Pollution Prevention Plan –
Administering a Stormwater Program
2b. Stormwater Management Plan –
Managing Runoff
2c. 17 Non-Proprietary Post-Construction BMPs
2d. Environmental/Stormwater Site Design –
Managing Runoff
2. | TABLE OF CONTENTS | Pg. 1
Notes: All content in 2a and d is covered completely in these two online courses.
We will do a mini quality/quantity review in 2b and do a QP, then cover 2c in its entirety here.
Describe contents to be covered while emphasizing overall learning objectives:
(click) 2a. Stormwater Pollution Prevention Plan
Recall the required components of a stormwater pollution prevention plan (SWPPP)
Explain how runoff characteristics can change as landcover conditions change
(click) 2b. Stormwater management plan (from online course)
Generalize the goal of the Part II B water quality technical criteria
Generalize the goal of the Part II B water quantity criteria
(click) 2c. 15 non-proprietary BMPs
Identify how each of the 15 non-proprietary BMPs removes pollutants from stormwater runoff
(click) 2d. Environmental site design

## Slide 3: Module 2b.
Stormwater Management Plan – Managing Runoff Online Course
Notes: We will cover a bit more VRRM spreadsheet info here and do a QP to review online course content.

## Slide 4: VRRM Spreadsheets
Two different spreadsheets
  New Development
  Re-Development
See table on pg. 15 for different development scenarios
2b. | STORMWATER MANAGEMENT PLAN| Pg. 15
Notes: VRRM: Virginia Ruoff Reduction Method
IN REFRENCE TO PLAN REVIEW PROCESS OF WHICH A PROGRAM-ADMIN NEEDS TO KNOW ABOUT!
ReDevelopment is called “development on prior developed lands”
Predevelopment refers to existing land conditions at the time the plan is submitted to the VSMP authority.
The table on page 13 lays out the different development scenarios.
Maximum amount of discussion on water quality

## Slide 5: QuickPoll
Notes: Which of the following can have a negative impact on water quality?
Correct answer: A, B, D

## Slide 6: QuickPoll
Select all that apply. Which of the following can have a negative impact on water quality?
Removal of vegetation
Addition of roads
Expansion of buffer areas
Soil compaction from site grading
Notes: Correct answer: A, B, D

## Slide 7: Water Quantity Criteria
Flood protection
Channel protection
2b. | STORMWATER MANAGEMENT PLAN| Pg. 16-18
Notes: Pages 17-19 discusses water quantity and the technical criteria for channel/flood protection and sheet flow.
Also covered in the online course. Review it for yourself there.
(Photo credit: Channel protection – DEQ, Flooding: Wendy North, https://commons.wikimedia.org/wiki/File:Flooded_stream_rushing_over_Dance_Lane_-_geograph.org.uk_-_907516.jpg)
Greater volumes of runoff and higher flow rates (even in small storms) can create:
• Altered stream flows (affect water conditions and habitat for fish)
• Channel erosion, widening, and downcutting (degrade stream habitat and produce substantial increases in sediment)
• Flooding and floodplain expansion
• Entrenched streams cutoff from the floodplain

## Slide 8: Q&A
VRRM
2b. | STORMWATER MANAGEMENT PLAN
Landcover and runoff
Water quality criteria
Water quantity criteria
Notes: (Pause for Q&A session) from online course content and brief review
Does anyone have questions about:
The link between the different types of landcover and the amount of stormwater runoff that results from each
The water quality criteria which aims to reduce the amount of sediment that leaves a developed site because sediment carries phosphorus and other nutrients which can be harmful when too many nutrients and other pollutants get into our waterways
The use of the Virginia Runoff Reduction Method to assess compliance with the water quality criteria of 0.41 lbs/acre/year of phosphorus
The water quantity criteria which address channel protection by looking at what type of flow is coming off a site and where it is discharging and flood protection by assessing current conditions of the downstream conveyance system
Add your questions into the question box and the moderator will read them.

## Slide 9: Module 2c.
17 Non-Proprietary Post-Construction BMPs (P-BMPs)
Notes: Emphaisse these practices are in response to the land disturbing activity.
These facilities treat stormwater from the site before send

## Slide 10: P-BMPs
Reduce phosphorus loads (water quality)
  All remove pollutants from stormwater runoff
  Some also provide runoff reduction
2c. | P-BMPs| Pg. 19
Notes: Announce page number since we’ve skipped around
EXAMPLE: Sand Filter (Quality) attached to a 50/10 Basin (Quantity)

## Slide 11: P-BMPs
2c. | P-BMPs
Ch. 8
VSWHB
Notes: The stormwater regulations only allow for the use of the non-proprietary BMPs and manufactured treatment devices listed on the Virginia Stormwater BMP Clearinghouse and Virginia Stormwater Management Handbook to achieve the water quality criteria.
Stormwater management facilities being used for water quantity alone do not have to be listed on the Clearinghouse, but these practices are discussed in P-SUP-07 of the VSWHB..

## Slide 12: P-BMPs – Pollution Control
3 primary mechanisms to control pollution:
  Infiltration
  Settling
  Vegetative uptake or filtering
2c. | P-BMPs| Pg. 19-20
Notes: Stormwater BMPs use three primary mechanisms to control pollution: (Discussed more on following slides)
Infiltration
Settling
Vegetative uptake or filtering

## Slide 13: Infiltration
Water soaks through the basin into subsoil
Sediment and pollutants stay in basin
2c. | P-BMPs| Pg. 19
Notes: Infiltration: Practices that use infiltration to remove pollutants collect stormwater runoff in a basin. The water gradually soaks through the basin and into the subsoil. After all the runoff is infiltrated, sediment and pollutants stay within the basin.
Permeable pavement, infiltration practices, bioretention systems, and dry swales use infiltration as a pollution control mechanism.
(Photo credit: Rice Creek Watershed District, http://www.ricecreek.org/)

## Slide 14: Settling
Runoff collects in a basin
Heavy solids and pollutants settle
Cleaner runoff is discharged
2c. | P-BMPs| Pg. 19
Notes: Settling: Another way stormwater BMPs remove pollutants is by collecting runoff in a basin and temporarily holding the water. While the runoff is contained, heavy solids and pollutants settle to the bottom of the basin while the cleaner runoff is discharged through the outlet.
Constructed wetlands, wet swales, extended detention basins and wet ponds use settling as a pollution control mechanism.
(Photo credit: Stormwater Maintenance LLC)

## Slide 15: Vegetative Uptake or Filtering
Pollutants filtered by contact with plants, root uptake, or consumption by microbes
2c. | P-BMPs| Pg. 20
Notes: Vegetative uptake or filtering: The third way to remove pollutants from runoff is by allowing it to flow through a vegetated area. Pollutants can be filtered out by physical contact with plants - causing sediment to settle out, plant root uptake, or consumption by microbes.
Vegetative filter strips, grass channels, vegetated roofs, bioretention, and filtering practices use vegetative uptake or filtering as a pollution control mechanism.
(Photo credit: DEQ)

## Slide 16: Flood and Erosion Control
2c. | P-BMPs| Pg. 20
Reduce runoff
Rainwater harvesting, permeable pavement, infiltration
Detain water and slowly release
Extended detention basins, wet ponds, constructed wetlands
Notes: Flood and erosion control
BMPs can also be used to achieve the water quantity criteria be reducing the amount of runoff that leaves a site or detaining the water and slowly releasing it. Rainwater harvesting, permeable pavement, and infiltration are examples of runoff reduction practices. Extended detention basins, wet ponds, and constructed wetlands are examples of detention practices.

## Slide 17: Numbering and Nomenclature
P-BAS-02
First letter represents
the type of BMP:
Post-Construction (P)
Number represents
the specific BMP per grouping
Three letters represent the primary function of the BMP:
Basins​ (BAS)
Conveyance (CNV)​
Filtration and Infiltration (FIL)
Support Components (SUP)
Flip to pg.21 in the PG
Notes: OVERVIEW OF P-BMPS
OTHER VARIATIONS OF SAME FORMAT BUT FOR CONSTRUCITON BMPS (C-BMPS)
COME BACK TO THIS MODULE ON YOUR OWN. Read about each P-BMP and highlight important specific information.

## Slide 18: P-BAS-01: Constructed Wetlands
2c. | P-BMPs| Pg. 22
Notes: Constructed wetlands, sometimes called stormwater wetlands, are shallow depressions that receive stormwater inputs for water quality treatment. Wetlands are typically less than one-foot deep and possess variable micro-topography to promote dense and diverse wetland cover.
(Photo credit: Seuss, Flickr)

## Slide 19: P-BAS-02: Wet Pond
2c. | P-BMPs| Pg. 23
Notes: Wet ponds consist of a permanent pool of standing water that promotes a better environment for gravitational settling, biological uptake, and microbial activity.
Runoff from each new storm enters the pond and partially displaces water from previous storms. The pool also acts as a barrier to re-suspension of sediments and other pollutants deposited during prior storms.
When sized properly, wet ponds have a residence time that ranges from many days to several weeks, which allows numerous pollutant removal mechanisms to operate. Wet ponds can also provide extended detention above the permanent pool to help meet channel protection requirements.
(Photo credit: Stormwater Maintenance LLC)

## Slide 20: P-BAS-03: Extended Detention Pond
2c. | P-BMPs| Pg. 24
Notes: An extended detention pond relies on 24 to 36 hour detention of stormwater runoff after each rain event. An under-sized outlet structure restricts stormwater flow so it backs up and is stored within the basin. The temporary ponding enables particulate pollutants to settle out and reduces the maximum peak discharge to the downstream channel, thereby reducing the effective shear stress on banks of the receiving stream.
(Photo credit: DEQ)

## Slide 21: P-BAS-04: Rainwater Harvesting
Intercept, divert, store and release rainfall for future re-use
2c. | P-BMPs| Pg. 25
Notes: Rainwater harvesting systems intercept, divert, store, and release rainfall for future use. The term rainwater harvesting is used in this specification, but it is also known as a cistern or rainwater harvesting system.
Rainwater that falls on a rooftop is collected and conveyed into an above- or below-ground storage tank where it can be used for non-potable water uses and on-site stormwater disposal/infiltration. Non-potable uses may include flushing of toilets and urinals inside buildings, landscape irrigation, exterior washing (e.g. car washes, building facades, sidewalks, street sweepers, fire trucks, etc.), and fire suppression (sprinkler) systems.
In many instances, rainwater harvesting can be combined with a secondary (down-gradient) runoff reduction practice to enhance runoff volume reduction rates and/or provide treatment of overflow from the rainwater harvesting system.

## Slide 22: P-CNV-01: Grass Channels
2c. | P-BMPs| Pg. 26
Notes: A grass channel is a stable, vegetated swale that is used as part of a stormwater conveyance system. Grass channels reduce stormwater runoff and pollutants by slowing the flow and providing the opportunity for infiltration.
Grass channels can be used to treat runoff from the managed turf areas of turf-intensive land uses, such as sports fields and golf courses, and drainage areas with combined impervious and turf cover (e.g., roads and yards).
(Photo credit: Upper left – Fairfax County, Upper right – Montgomery County, MD, Lower left – Maryland DOT, Lower right – Stormwater Maintenance LLC)

## Slide 23: P-CNV-02: Dry Swales
2c. | P-BMPs| Pg. 27
Notes: Dry swales are essentially bioretention cells that are shallower, configured as linear channels, and covered with turf or other surface material (other than mulch and ornamental plants). They are a soil filter system that temporarily stores and then filters the desired treatment volume.
(Photo credit: Montgomery County Planning Commission)

## Slide 24: P-CNV-03: Wet Swales
2c. | P-BMPs| Pg. 28
Notes: Wet swales can provide runoff filtering and treatment within the conveyance system and are a cross between a wetland and a swale. These linear wetland cells often intercept shallow groundwater to maintain a wetland plant community. The saturated soil and wetland vegetation provide an ideal environment for gravitational settling, biological uptake, and microbial activity.
(Photo credit: Lake County Illinois Stormwater Management Commission)

## Slide 25: P-CNV-04: Regenerative Conveyance Channels
2c. | P-BMPs| Pg. 29
Notes: Treat and convey stormwater through a combination of sand, wood chips, native vegetation, riffles (with either cobble rocks or boulders), and shallow pools.
Designed to convey water while minimizing the effects of erosion
Designed to treat and convey water through a series of shallow pools

## Slide 26: P-FIL-01: Rooftop (Impervious Area) Disconnection
Simple disconnection
Disconnection leading to another P-BMP
2c. | P-BMPs| Pg. 30
Notes: This strategy involves managing runoff close to its source by intercepting, infiltrating, filtering, treating, or reusing it as it moves from the impervious surface to the drainage system. Two kinds of disconnection are allowed:
Simple disconnection whereby rooftops and/or on-lot residential impervious surfaces are directed to pervious areas; and
Disconnection leading to an alternative runoff reduction practice(s) adjacent to the roof such as:
  Soil compost amended filter path
  Infiltration by micro-infiltration practice
  Filtration by rain gardens or micro-bioretention
  Storage and reuse with a cistern
  Storage and release into a stormwater planter
(Photo credit: Low Impact Development Center)

## Slide 27: P-FIL-02: Vegetated Roofs
2c. | P-BMPs| Pg. 31
Intensive
Extensive
Notes: Vegetated roofs are alternative roof surfaces that typically consist of waterproofing and drainage materials and an engineered growing media that is designed to support plant growth. Vegetated roofs capture and temporarily store stormwater runoff in the growing media before it is conveyed into the storm drain system. A portion of the captured stormwater evaporates or is taken up by plants, which helps reduce runoff volumes, peak runoff rates, and pollutant loads on development sites.
There are two different types of vegetated roof systems:
  Intensive vegetated roofs have a deep growing media layer that ranges from 6 inches to 4 feet thick, which is planted with a wide variety of plants, including trees; and
  Extensive systems that typically have much shallower growing media (2 to 6 inches) and is planted with carefully selected drought tolerant vegetation.
(Photo credit: Left – Chris Burekner, Flickr, Right – Chesapeake Bay Program)

## Slide 28: P-FIL-03: Permeable Pavement
2c. | P-BMPs| Pg. 32
Porous Concrete
Pervious Asphalt
Permeable Interlocking Concrete Pavers
Notes: Permeable pavement is an alternative to asphalt or concrete that allows stormwater to filter through openings in the surface into an underlying stone reservoir, where it is temporarily stored and/or infiltrated.
A variety of permeable pavement surfaces are available, including
  porous concrete,
  pervious asphalt, and
  permeable interlocking concrete pavers.
While the specific design may vary, all permeable pavements have a similar structure, consisting of a surface pavement layer, an underlying stone aggregate reservoir layer and a filter layer or fabric installed on the bottom.
(Photo credit: Upper left – DEQ, Upper right – NEMO Uconn, Lower left – DEQ, Lower right – BMP Spec #7)

## Slide 29: P-FIL-04: Infiltration
Infiltration trench
Infiltration basin
2c. | P-BMPs| Pg. 33
Notes: Infiltration practices use temporary surface or underground storage to allow incoming stormwater runoff to go into underlying soils. Runoff first passes through multiple pretreatment mechanisms to trap sediment and organic matter before it reaches the practice. As the stormwater penetrates the underlying soil, chemical and physical adsorption processes remove pollutants.
Infiltration practices have the greatest runoff reduction capability of any stormwater practice and are suitable for use in residential and other urban areas where measured soil permeability rates exceed 1/2 inch per hour.
(Photo credit: BMP spec #8)

## Slide 30: P-FIL-05: Bioretention Basins
2c. | P-BMPs| Pg. 34
Urban Bioretention
Micro-Bioretention/Rain Garden
Bioretention
Notes: A bioretention facility is a depressed area that uses a custom soil mix and plants to reduce stormwater runoff and filter pollutants – much like a forested ecosystem. The primary component of a bioretention practice is the filter bed, which has a mixture of sand, soil, and organic material as the filtering media with a surface mulch layer.
(Photo credit: Upper – VA Department of General Services, Lower left – CSN, Lower Right – Chesapeake Bay Program)

## Slide 31: P-FIL-06: Filtering Practices
2c. | P-BMPs| Pg. 35
Perimeter Sand Filter
Underground Sand Filter
Surface Sand Filter with Turf Cover
Surface Sand Filter
Notes: Stormwater filters are a useful practice to treat stormwater runoff from small, highly impervious sites. Stormwater filters capture, temporarily store, and treat stormwater runoff by passing it through an engineered filter media, collecting the filtered water in an underdrain, and then returning it back to the storm drainage system. The filter consists of two chambers. The first chamber is devoted to settling, and the second serves as a filter bed consisting of sand or organic filter media.
(Photo credit: Center for Watershed Protection)

## Slide 32: P-FIL-07: Sheet Flow to Vegetated Filter Strip or Conserved Open Space
Vegetated filter strip
Conserved open space
2c. | P-BMPs| Pg. 36
Notes: Filter strips are vegetated areas that treat sheet flow delivered from adjacent impervious and managed turf areas by slowing runoff velocities and allowing sediment and attached pollutants to settle and/or be filtered by the vegetation. The two design variants are conserved open space and vegetated filter strips

## Slide 33: P-FIL-08: Soil Compost Amendments
2c. | P-BMPs| Pg. 37
Area being prepared for compost amendments
Re-seeded area with recently applied soil compost amendments
Notes: Soil compost amendments are applied to compacted soil after construction to restore its porosity. Soil amendments can reduce the generation of runoff from compacted urban lawns and may also be used to enhance the runoff reduction performance of downspout disconnections, grass channels, and filter strips.
(Photo credit: Upper picture – Center for Watershed Protection, Lower picture – Fairfax County)

## Slide 34: P-FIL-09: Tree Planting
2c. | P-BMPs| Pg. 38
Notes: Tree plantings as a pollution-reduction practice pertain to new, individually planted trees on developed land. Credited area only accounts for precipitation that falls on the tree canopy area. Additionally, this measure does not require a specific soil media be used.
Trees cannot receive credit as a best management practice (BMP) when:
Planted to replace those removed in land disturbance
Planted to meet planning requirements
Financed through local, state, and federal programs
Planted to meet water quality requirements through the VRRM (as forest, part of other BMPs, etc.)

## Slide 35: QuickPoll
Notes: Select all that apply. How does a grass channel provide stormwater management?
Infiltration
Settling
Vegetative uptake or filtering
Correct Answer: All
A. grass channels provide minimal infiltration on their own, but that can be improved with the addition of compost (**note to participants to add this to the PG)
B. Settling occurs in a grass channel and that can be improved with the addition of check dams which act as speed bumps to slow down the water
C. Filtering occurs by the grass

## Slide 36: QuickPoll
Select all that apply. How does a grass channel provide stormwater management?
Infiltration
Settling
Vegetative uptake or filtering
Notes: Correct Answer: All
A. grass channels provide minimal infiltration on there own, but that can be improved with the addition of compost (**note to participants to add this to the PG)
B. Settling occurs in a grass channel and that can be improved with the addition of check dams which act as speed bumps to slow down the water
C. Filtering occurs by the grass

## Slide 37: Q&A
2d. Environmental Site Design
2a. SWPPP
2. | MANAGING RUNOFF
2b. SWM plan
2c. P-BMPs
Answers to Knowledge Check Questions are in the APPENDIX
Notes: All content in 2a and d is covered completely in online courses. Cover a bit more VRRM spreadsheet info in 2b, then 2c in its entirety here.

## Slide 38: Photo Credits:
Atlanta Regional Commission: slide 9
Center for Watershed Protection: slide 43 (upper), 51
Chesapeake Bay Program: slide 12-13, 44 (right), 45, 48 (lower right)
Chesapeake Stormwater Network: slide 48 (lower left)
Chris Brueckner, Flickr: slide 34, 44 (left)
DEQ: slide 25, 38, 46 (upper left, bottom left and right), 54
Fairfax County: slide 42 (upper left), 43 (lower)
Federal Interagency SWRG: slide 15
Lake County Illinois Stormwater Management Commission: slide 50
Low Impact Development Center: slide 40
Maryland DOT: slide 42 (lower left)
Montgomery County, MD: slide 42 (upper right), 49
CT NEMO: slide 46 (upper right)
Pixnio: slide 18
PublicDomainPictures.NET: slide 17
Rice Creek Watershed District: slide 36
Seuss, Flickr: Slide 52
Stormwater Maintenance LLC: slide 37, 42 (lower right), 53
Utah Department of Environmental Quality: slide 14
VA DGS: Slide 48 (upper)
Wendy North, Wiki Commons: slide 25
W.L Tarbert , Wiki Commons: slide 56

## Slide 39: Knowledge Check Questions
Which two plans in the SWPPP must be approved?
  Erosion and sediment control plan and stormwater management plan
Does the stormwater management plan address runoff during construction or after?
  Post-construction stormwater runoff
2. | KNOWLEDGE CHECK QUESTIONS| Pg. 37
Notes: You may want to give participants a couple of minutes to answer these on their own first and then go through as a group.
Which two plans in the SWPPP must be approved?
Erosion and sediment control plan and stormwater management plan must be approved
Does the stormwater management plan address runoff during construction or after?
The stormwater management plan address post-construction stormwater runoff

## Slide 40: Knowledge Check Questions
What impact does impervious cover have on water quality?
  The volume and velocity of stormwater runoff increases as natural vegetation is replaced with roads, buildings, parking areas and other impervious surfaces. The increase in stormwater runoff leads to an increase in pollutants, such as sediment and phosphorus that are carried to waterways, which has a negative effect on water quality.
What is the target pollutant in the water quality criteria?
  Phosphorus
2. | KNOWLEDGE CHECK QUESTIONS| Pg. 37
Notes: What impact does impervious cover have on water quality?
The volume and velocity of stormwater runoff increases as natural vegetation is replaced with roads, buildings, parking areas and other impervious surfaces. The increase in stormwater runoff leads to an increase in pollutants, such as sediment and phosphorus that are carried to waterways, which has a negative effect on water quality.
What is the target pollutant in the water quality criteria?
Phosphorus

## Slide 41: Knowledge Check Questions
What is the lower limit of the range of imperviousness that can result in stream degradation?
  10%
The SWM regulation ensures water quantity is considered in stormwater management planning to protect against which two destructive forces?
  Channel erosion and flooding
2. | KNOWLEDGE CHECK QUESTIONS| Pg. 37
Notes: What is the upper limit of the range of imperviousness that can result in stream degradation?
10%
The SWM regulation ensures water quantity is considered in stormwater management planning to protect against which two destructive forces?
Channel erosion and flooding

## Slide 42: Knowledge Check Questions
Discuss how the rate of runoff changes after development.
  The rate of runoff increases after development because of the replacement of vegetation with impervious surfaces. A larger volume of water will travel more quickly through a stream channel, potentially causing erosion and flooding.
What are the three primary mechanisms BMPs use to control pollution?
  Infiltration, settling and vegetative uptake and filtering
2. | KNOWLEDGE CHECK QUESTIONS| Pg. 37
Notes: Discuss how the rate of runoff changes after development.
The rate of runoff increases after development because of the replacement of vegetation with impervious surfaces. A larger volume of water will travel more quickly through a stream channel, potentially causing erosion and flooding.
What are the three primary mechanisms BMPs use to control pollution?
Infiltration, settling and vegetative uptake and filtering