## Slide 1: Module 3
Administering an Erosion and Stormwater Management Program
Administering a SWM Program Online Course

## Slide 2: Table of Contents
3a. Locality Programs
3b. Local Ordinances for Chesapeake Bay Preservation Act LDAs
3c. Standards and Specifications
3d. Reports and Record Keeping
3e. Program Reviews
3. | TABLE OF CONTENTS | Pg. 1
Notes: We will cover a bit of additional info in 3a but all other sections are covered in their entirety in the online course
At the end of this module, you will be able to:
  List the basic requirements of a stormwater management program and a locality’s stormwater management ordinance
  Summarize the enforcement elements that are minimally required and those that are optional within a stormwater program and locality’s stormwater ordinance
  State the maximum civil penalty that can be issued for violations
  Recall examples of violations that can be included in a locality’s schedule of civil penalties
  Describe the conditions under which a locality is authorized to adopt a more stringent ordinance
  Recall the conditions under which a locality VSMP authority may prohibit a DEQ approved BMP or require more stringent conditions
  Summarize the annual standards and specifications requirements and identify the entities that are or may be regulated under them

## Slide 3: Module 3a.
Locality Programs
Notes: Localities that operate a regulated Municipal Separate Storm Sewer System (MS4) must adopt and administer a Virginia Erosion and Stormwater Management Program (VESMP).
Non-MS4 localities may choose to administer a VESMP or Virginia Erosion and Sediment Control Program (VESCP), where DEQ serves as the Virginia Stormwater Management Program (VSMP) authority

## Slide 4: Locality Program Requirements
3a. | LOCALITY PROGRAM| Pg. 3
Notes: MUST VS MAY! --> Lawyer Speak!!!!!!!

## Slide 5: Program Requirements
The ordinance must:
  Remain consistent with the VESM Regulation
  Require approval for land disturbance
  Include program requirements for:
    Plan review
    Inspections
    Enforcement
3a. | LOCALITY PROGRAM| Pg. 4
Notes: Ordinance content requirements were not in the online course
The VESMP must be established by an ordinance that includes:
Ordinances, policies, and technical materials consistent with the VESM Regulation
Requirements for land disturbance approvals
Program requirements for
  plan review,
  periodic inspections including the installation of stormwater management measures, and
  Enforcement (enforcement procedures and civil penalties as discussed in the online course and shortly here)

## Slide 6: Program Requirements
The ordinance must also include:
  Program administration fees for LDAs
  Provisions for the long-term responsibility (and maintenance) of stormwater management control devices
  Requirements for coordination with flood insurance, flood plain management, and other programs requiring compliance before authorizing the start of construction
3a. | LOCALITY PROGRAM| Pg. 4
Notes: (Continued)
Provisions charging applicants a reasonable fee to defray the cost of program administration for land-disturbing activities that do not require permit coverage
Provide provisions for the long-term responsibility for and maintenance of stormwater management control devices and other techniques for the management of the quality and quantity of stormwater runoff
Coordinate with flood insurance, flood plain management, and other programs requiring compliance before authority the start of construction

## Slide 7: Enforcement
Inspection Report
Completed for each inspection
Includes a deadline for any needed repairs or noted issues
Provided to operator
Notice to Comply
Permittee fails to comply
Served electronically, registered or certified mail or at the site
Specifies how to comply and a deadline
3a. | LOCALITY PROGRAM| Pg. 5
Notes: Inspection report info is added for clarity
A notice to comply can be used if it is determined by the locality VESMP authority or DEQ that there is a failure to comply with the permit conditions (in this instance, graduating up from an IR).
Notice must be served upon the owner, permittee, or person conducting the LDA by delivery via registered or certified mail or at the development.
The notice must specify:
the measures needed to comply with the permit conditions and
the time within which such measures shall be completed.

## Slide 8: Enforcement
Upon failure to comply within the time specified, the following actions may be taken:
VESMP authority
or DEQ
3a. | LOCALITY PROGRAM| Pg. 6
Stop Work Order
(or Emergency)
Penalties
Notes: Upon failure to comply within the time specified, the following actions may be taken:
Stop work order may be issued by the locality VESMP authority;
The Board/DEQ or the VSMP authority may take enforcement action.

## Slide 9: Enforcement
Stop work order
  Land-disturbing activities must stop until:
    Violation of the permit has ceased
    Approved plan and required permits are obtained
    Specified corrective measures have
    been completed
3a. | LOCALITY PROGRAM| Pg. 6
Notes: If a permittee fails to comply with a notice within the time specified, the locality VESMP authority or DEQ may issue a stop work order requiring the permittee or person conducting the LDA without a required permit to cease all land-disturbing activities. The stop work order is in effect until the violation of the permit has stopped, or an approved plan and required permits are obtained, and specified corrective measures have been completed.
(Delivery options are the same as NTCs, previously discussed)

## Slide 10: Enforcement
Emergency stop work order
  Alleged non-compliance:
    Causing, or
    Presents an imminent and substantial danger of causing harmful erosion of lands or sediment deposition in state waters or otherwise substantially impacts water quality
EMERGENCY
3a. | LOCALITY PROGRAM| Pg. 6
Notes: If the locality VESMP authority or DEQ finds that any alleged non-compliance is:
Causing or
Presents an imminent and substantial danger of causing harmful erosion of lands or sediment deposition in state waters or otherwise substantially impacting water quality
Instructor provides example

## Slide 11: Enforcement
Civil penalties may be imposed for:
No CGP coverage
No SWPPP, incomplete SWPPP, SWPPP not available
No approved ESC or SWM plan
Failure to install or maintain BMPs
Operational deficiencies
Failure to conduct required inspections
Incomplete, improper, or missing inspections
*Not limited to these violations
3a. | LOCALITY PROGRAM| Pg. 8
Discharges not in compliance with CGP
Notes: Violations for which a penalty may be imposed include, but are not limited to:
No state permit,
No SWPPP,
Incomplete SWPPP,
SWPPP not available for review,
Engaging in a regulated LDA without an approved plan,
Failure to install stormwater BMPs or erosion and sediment controls,
Failure to properly maintain Stormwater BMPs or erosion and sediment controls,
Operational deficiencies,
Failure to conduct required onsite qualified personnel inspections,
Incomplete, improper, or missed onsite inspections, or
Discharges not in compliance with the CGP.

## Slide 12: Enforcement
Injunctive relief
  DEQ or a locality VESMP authority may bring a civil action requesting the court to compel compliance
3a. | LOCALITY PROGRAM| Pg. 10
Notes: DEQ or VESMP authority may bring an action requesting the court to compel compliance with the Act, rule, Regulation, ordinance, approved standard and specification, order, or permit condition.
We will not cover the criminal misdemeanor/felonies on pages 9-11. You can review yourself.

## Slide 13: Enforcement
Hearings
  Permit applicant, permittee, or person subject to the CGP requirements aggrieved by any action of DEQ taken without a formal hearing, may demand, in writing, a formal hearing
    Must follow APA process
3a. | LOCALITY PROGRAM| Pg. 13
Notes: The locality VESMP authority and DEQ must ensure that any permit applicant, permittee, or person subject to state permit requirements under the Act aggrieved by any action of the VESMP authority taken without a formal hearing, or by inaction of the VESMP authority, shall have the right to a hearing
(VESMP authority and hearings is discussed under the Emergency SWO)

## Slide 14: QuickPoll
Notes: When may a local authority adopt a more stringent ordinance than the state?
Local referendum calls for it
Addresses specific pollution concern – correct
Discourage bids by certain contractors
The locality may not

## Slide 15: QuickPoll - Ordinances
When may a local authority adopt a more stringent ordinance than the state?
Local referendum calls for it
To address a specific pollution concern
Discourage bids by certain contractors
The locality may not

## Slide 16: Q&A
CBPA
Stand. & Specs.
Record keeping
Program Reviews
Locality Programs
Notes: We only covered content here in 3a. The other four sections are covered in their entirety in the online course.
(Pause for Q&A session)
Does anyone have questions
Add your questions into the question box and the moderator will read them.

## Slide 17: Knowledge Check Questions
A locality VSMP must be at least as stringent as what state permit?
  Construction GP
What plans must a locality’s ordinance require to be submitted and approved?
  ESC plan and SWM plan
3. | KNOWLEDGE CHECK QUESTIONS | Pg. 19
Notes: You may want to give participants a few minutes to answer the knowledge check questions on their own and then review as a group
A locality VSMP must be at least as stringent as what state permit?
Construction GP (9VAC25-870-106)
What plans must a locality’s ordinance require to be submitted and approved?
ESC plan and SWM plan

## Slide 18: Knowledge Check Questions
List three (3) violations for which a penalty may be imposed
  No state registration statement; no SWPPP; incomplete SWPPP; SWPPP not available for review; no approved erosion and sediment control plan; failure to install stormwater management BMPs or ESCs; stormwater BMPs or erosion and sediment controls improperly installed or maintained; operational deficiencies; failure to conduct required inspections; incomplete, improper, or missed inspections
3. | KNOWLEDGE CHECK QUESTIONS | Pg. 19
Notes: List three (3) violations for which a penalty may be imposed.
Any of the following: No state registration statement; no SWPPP; incomplete SWPPP; SWPPP not available for review; no approved erosion and sediment control plan; failure to install stormwater management BMPs or ESCs; stormwater BMPs or erosion and sediment controls improperly installed or maintained; operational deficiencies; failure to conduct required inspections; incomplete, improper, or missed inspections.

## Slide 19: Knowledge Check Questions
What is the maximum penalty a locality can impose under the stormwater act?
  $32,500 per violation per day
How long must a locality VSMP authority hold on to a registration statement?
  All registration statements must be documented and retained for at least three years from the date of project completion or state permit termination
3. | KNOWLEDGE CHECK QUESTIONS | Pg. 19
Notes: What is the maximum penalty a locality can impose under the stormwater act?
$32,500
How long must a locality VSMP authority hold on to a registration statement?
All registration statements must be documented and retained for at least three years from the date of project completion or state permit termination

## Slide 20: Knowledge Check Questions
How often must DEQ conduct program reviews?
  Once every five years
3. | KNOWLEDGE CHECK QUESTIONS | Pg. 19
Notes: How often must DEQ conduct program reviews?
DEQ is required to conduct a program review once every five years