## Slide 1: Module 4
Approval to Start Land Disturbance – portions included in the Administering a Stormwater Program Online Course

## Slide 2: Table of Contents
4a. Regulated LDAs – online course
4b. Application Package
4c. ESM Plan Submittal and Review
4d. Single-Family Detached Residential Structures – online course
4e. Construction General Permit Issuance
4f. Locality VESMP Authority Approval to Start Land Disturbance – online course
4. | TABLE OF CONTENTS| Pg. 1
Notes: a, d (some additional content here), f exclusively online
Learning objectives:
Explain what land-disturbing activities are regulated under the Stormwater Management Act
List the required components of a stormwater management plan
Describe the stormwater management plan review schedule
Determine, for a given project, the time limits of applicability for the Part II B and Part II C technical criteria and the time and conditions under which grandfathering can occur
Discuss alternatives and exceptions for meeting stormwater management technical criteria, including how and under which conditions requests can be made
Describe the locality VSMP authority permit and distinguish it from the Construction General Permit

## Slide 3: Module 4b.
Application Package
Notes: Skip ahead in PG to page 6…

## Slide 4: Application Package
Approved SWM plan
Approved ESC plan
Security for performance*
Fees*
Registration statement*
* If required
4b. | APPLICATION PACKAGE| Pg. 6
Approved ESM Plan
Notes: Skip ahead in PG to page 6…
Before starting a land-disturbing activity, an operator must submit an application package to the locality VESMP authority for review and approval. Land disturbance cannot begin until the proper permits have been issued.
- Good place to introduce the concept of “ESM plans” -> Erosion and Stormwater Management plans

## Slide 5: Application Package
As a program administrator…
Your role in the permit issuance process is to:
Ensure ESM plan review is completed within the required timeframe and proper notice is sent to the applicant
Verify application package is complete
Confirm registration statement information is accurate (ensure the correct operator is listed)
Enter registration statement into the Construction General Permit System
Ensure approval to start land disturbance is given at the correct time
4b. | APPLICATION PACKAGE| Pg. 6

## Slide 6: Module 4c.
ESM Plan Submittal and Review
Notes: Why are we talking about plan submittal and review? Isn't that for the plan reviewers to worry about???
As a Program Administrator, you need to know and understand the program requirements!
Questions you should be able to answer as an authority:
What's the time line for review?
Are projects grandfathered in the regulatory sense?

## Slide 7: ESM Plan Submittal & Review
ESM plan submitted
15 calendar days
Completeness review + written notification
60 calendar days from notification for technical review
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 7
Notes: The VESMP authority has 15 calendar days to determine the completeness of a stormwater management plan and notify the applicant (in writing) of its determination.
If the plan is not complete, the VESMP authority must notify the applicant in writing or electronically of the reason(s).
If a plan is complete and the applicant has been notified within 15 days of submission, the VESMP authority has 60 calendar days from the time of notification to review the plan.
After completeness has been communicated to the applicant within the 15 calendar days, the VESMP authority (plan reviewer) has 60 calendar days from the date of submission to review the plan and notify the operator in writing of the decision to approve or disapprove the plan. The reason for not approving must be included.

## Slide 8: ESM Plan Submittal & Review
Resubmittal
  VESMP authority has 45 calendar days from the date of resubmission to review a plan that was previously disapproved.
  This 45-day review period includes a new completeness review within the first 15 days.
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 8

## Slide 9: ESM Plan Submittal & Review
Modifications
  VESMP authority has 60 calendar days to respond in writing to plans that have been modified after approval with either an approval or disapproval. ESM plans modified or changed and submitted for review are treated as new submittals.
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 8
Notes: Perhaps a sediment trap needs to be changed to a sediment basin. Or if a post-construction stormwater BMP is changed to a different BMP, or eliminated all together.
Example: Modifications may occur due to a change in the nature of the project, or after an inspection an inspector finds that controls are not preventing sediment from leaving the site.

## Slide 10: SWM Plan Contents
Discharge information
1
Contact information
2
Narrative
3
General description of SWM facility O&M
4
SWM facility information
5
Hydrologic and hydraulic computations
6
Documentation for water quality & quantity compliance
7
Maps
8
Offsite options (if used)
9
Fee and form (if required)
10
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 8-10
Notes: Good place to stress that we’re now focusing specifically on the SWM plan portion of the ESM plan.
SWM plan must contain the following content in order to be considered administratively complete:
Information on the type of and location of stormwater discharges, and the features to which stormwater is being discharged
Contact information including name, address, telephone number, and email address of the owner, and Tax reference number and parcel number of the property or properties affected.
Narrative including: Description of current site conditions and final site conditions, or if allowed by the VSMP authority, the information provided and documented during the review process that address the current and final site conditions.
General description of the proposed stormwater management facilities and the mechanisms through which the facilities will be operated and maintained after construction is complete.
Information on the proposed stormwater management facilities
Hydrologic and hydraulic computations, including runoff characteristics
Documentation and calculations verifying compliance with the water quality and quantity requirements of the Regulations.
Map(s) of the site that depict the topography of the site
Letter of availability from the off-site provider if using off-site compliance options
Fee and form if required

## Slide 11: QuickPoll
Notes: How many days do VESMP Authorities have to review a newly submitted ESM/SWM plan?
60 days
15 days
45 days
30 days
Answer – a. 60 days after notifying the applicant of completeness. Or 60 days from submission, if not notifying the applicant.

## Slide 12: QuickPoll
How many days do VESMP Authorities have to review a newly submitted ESM/SWM plan?
60 days
15 days
45 days
30 days
Notes: Use partial screen view to respond to QuickPoll questions.
Ask participants to type in what page they found the answer

## Slide 13: SWM Plan
Time limits of technical criteria applicability
Initial permit coverage
Pt. V, Art. 4
7/1/09 – 6/30/14
1st 5-year renewal
Pt. V, Art. 4
2nd 5-year renewal
Pt. V, Art
New criteria
7/1/24 – 6/30/29
Permits issued before July 1, 2014
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 10-11
New criteria
Portions of projects not under construction must comply with the requirements of Pt. V, Art. 3 criteria
Notes: As discussed in Module 2, the ESM regulation includes technical criteria that must be met in the stormwater management plan to address water quality and water quantity.
There are two sets of criteria – Part V, Article 3 (which was covered in Module 2) and Part V, Article 4 (the “old” criteria). The following two sections explain how to determine which criteria to apply to a project.
Land-disturbing activities that obtained state permit coverage or started land disturbance before July 1, 2014, must meet the Part II C technical criteria. Such projects shall remain subject to the Part V, Article 4 technical criteria for two additional permit cycles (permit cycle is five years).
(Click – animation) ENDING July 1, 2024. This means NOW, no projects that were issued CGP coverage prior to July 1, 2014 should be currently conducting LDAs under the “old” criteria, unless they were under construction as of July 1, 2024.
After such time, portions of the project not under construction shall become subject to any new technical criteria adopted by the Board.

## Slide 14: SWM Plan
Time limits of technical criteria applicability
Initial permit coverage
Pt. V, Art. 3
7/1/14 – 6/30/19
1st 5-year renewal
Pt. V, Art. 3
2nd 5-year renewal
Pt. V, Art. 3
New criteria
7/1/29 – 6/30/34
Permits issued July 1, 2014 and after
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 11
7/1/24 – 6/30/29
Notes: Land-disturbing activities that obtained an initial state permit on or after July 1, 2014 must meet the Part II B technical criteria, with the exception of grandfathered projects. Land-disturbing activities conducted in accordance with the Part II B technical criteria shall remain subject to the Part II B technical criteria for two additional state permit cycles. After such time, portions of the project not under construction shall become subject to any new technical criteria adopted by the Board
Since we’re currently in the second five-year permit cycle of IIB, projects approved now will remain subject to IIB until 6/30/29

## Slide 15: SWM Plan
Grandfathering of technical criteria:
  No permit issued before July 1, 2014
  LDA didn’t start before July 1, 2014
  Land disturbance commenced prior to July 1, 2019
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 12
Notes: The grandfathering section of the Regulations lays out conditions for determining whether a land-disturbing activity that was neither permitted nor had started land disturbance before July 1, 2014 is able to meet the technical criteria in Part V, Article 4

## Slide 16: Grandfathering
Locality, state, and federal projects
1.
Obligation of locality, state, or federal funding before 7/1/12, or DEQ approved a SWM plan before 7/1/12;
2.
State permit wasn’t issued before 7/1/14; and
3.
Land disturbance didn’t start before 7/1/14
Grandfathered until construction is complete
4c. | SWM PLAN SUBMITTAL & REVIEW| Pg. 12
4.
Land disturbance commenced prior to 7/1/19
Notes: However if:
(Click) There has been an issuance of governmental bonding or public debt financing before July 1, 2012;
(Click) A state permit has not been issued prior to July 1, 2014; and
(Click) Land disturbance did not start before July 1, 2014.
(Click) These projects are grandfathered and there’s so specified time for completion

## Slide 17: Grandfathering
Locality, state, and federal projects
1.
Issuance of governmental bonding or public debt financing before 7/1/12;
2.
State permit wasn’t issued before 7/1/14; and
3.
Land disturbance didn’t start before 7/1/14
Part V, Article 4 – No time limit
4c. | SWM PLAN SUBMITTAL & REVIEW| Pg. 12
4.
Land disturbance commenced prior to 7/1/19
Notes: However if:
(Click) There has been an issuance of governmental bonding or public debt financing before July 1, 2012;
(Click) A state permit has not been issued prior to July 1, 2014; and
(Click) Land disturbance did not start before July 1, 2014.
(Click) These projects are grandfathered and there’s so specified time for completion

## Slide 18: Grandfathering
All other land-disturbing activities
1.
Proffered or conditional zoning plan, zoning with a plan of development, preliminary or final subdivision plat, preliminary or final site plan, or any document determined equivalent by the locality:
i.
Was approved by the locality before July 1, 2012
ii.
Provided a layout
iii.
Complies with the Part V, Art. 4 technical criteria, and
iv.
No modification that increases amount of P leaving each point of discharge and no increase in volume or rate of runoff
4c. | SWM PLAN SUBMITTAL & REVIEW| Pg. 12-13
Notes: All other land-disturbing activities shall be considered grandfathered by the VSMP authority and shall be subject to the Part II C technical criteria provided:
(Click) A proffered or conditional zoning plan, zoning with a plan of development, preliminary or final subdivision plat, preliminary or final site plan, or any document determined by the locality to be equivalent:
  (Click) Was approved by the locality prior to July 1, 2012,
  Provided a layout (a conceptual drawing sufficient to provide for the specified stormwater management facilities required at the time of approval,
  Complies with the Part II C technical criteria, and
  Has not been subsequently modified or amended in a manner resulting in an increase in the amount of phosphorus leaving each point of discharge, and such that there is no increase in the volume or rate of runoff;

## Slide 19: Grandfathering
4.
A state permit has not been issued prior to July 1, 2014; and
2.
Land disturbance did not start before July 1, 2014
Grandfathered until construction is complete
4c. | SWM PLAN SUBMITTAL & REVIEW| Pg. 12-13
3.
Land disturbance commenced prior to July 1, 2019
Notes: (Continued)
(Click) A state permit has not been issued prior to July 1, 2014; and
(Click) Land disturbance did not start before July 1, 2014
(Click) These projects are grandfathered until 6/30/2019. At that time, portions of the project not under construction shall be subject to any new technical criteria.
See the flow charts on pages 13+14

## Slide 20: Grandfathering
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 14-15
Modifications to a previously approved SWM plan may NOT result in an increase in P or water quantity discharging the site
Part V, Article 3 technical criteria

## Slide 21: Offsite Compliance Options
Operators may use offsite options to satisfy water quality criteria provided:
  Nutrient reductions are achieved before the start of land disturbance
  Phased projects – reductions are achieved before start of each phase
  Offsite options cannot be used in violation of local water-quality based limitations at the point of discharge
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 16
Notes: Operators may use offsite options to satisfy the Part V, Article 3 or 4 water quality criteria (discussed in Module 2) provided:
Offsite options must not be allowed unless the selected offsite option achieves (obtains) the necessary nutrient reductions before the start of land disturbance. In the case of phased projects, the operator MUST acquire or achieve offsite nutrient reductions before the start of each phase of land-disturbing activity in an amount sufficient for each phase. Phasing means the operator must submit a modification to their permit for each phase, as they obtain the credits.
Offsite options cannot be used in violation of local water quality-based limitations at the point of discharge based on an impaired waters plan, an MS4 program plan, or otherwise established or approved by the Board.
(For example, Prince William County prohibits offsite use because of the Occoquan Reservoir, Rockingham limits because of nutrient TMDLs, and Chesterfield limits because of the Swift Creek Reservoir)

## Slide 22: Offsite Compliance Options
Comprehensive stormwater management plan*
A locality pollutant loading pro rata share program*
Nonpoint nutrient offset program
Other offsite options
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 16
*Can be used to compliance with Water Quantity technical criteria requirements
Notes: Offsite options (discussed in more detail on following slides):
  (Click) Offsite controls utilized in accordance with a comprehensive stormwater management plan for the local watershed within which a project is located;
  (Click) A locality pollutant loading pro rata (in proportion) share program or similar local funding mechanism;
  (Click) Nonpoint nutrient offset program;
  (Click) Other offsite options approved by an applicable state agency or state board; and
  (Click) water quantity can be met with first two options
Offsite options 1+2 may be used to meet the requirements of the water quantity criteria

## Slide 23: Offsite Compliance Options
Comprehensive stormwater management plan*
  Locality VESMP authority may develop to meet water quality and/or water quantity criteria
  DEQ must approve the plan
  State and federal agencies may develop and may participate in locality-developed plans
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 17
Notes: A locality’s VESMP authority may develop a comprehensive- or commonly referred to as regional – stormwater management plan to meet the Part V, Art. 3 water quality and/or quantity criteria.
The plan must be approved by DEQ.
State and federal agencies may develop comprehensive stormwater management plans, and may participate in locality-developed comprehensive stormwater management plans where practicable and permitted by the locality VESMP authority.
(Example: Universities may build large stormwater facilities to accommodate future development)

## Slide 24: Offsite Compliance Options
A locality pollutant loading pro rata share program*
  Developers pay the locality the proportional cost of providing off-site stormwater management
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 17
Notes: Localities may have a pro rata share program established by ordinance, for developers to pay the locality the proportional cost of providing off-site stormwater management.
(Example: Henrico County)

## Slide 25: Offsite Compliance Options
Nonpoint nutrient offset program
  Must be from the same or adjacent fourth order subbasin
If no credits available within the fourth order subbasin, the VESMP or DEQ as the VSMP authority may allow the use of credits within the same tributary
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 17
Notes: A VESMP authority is authorized to allow the use of nutrient credits.
The credits must be from the same fourth order subbasin (similar to the previous regulation language of 8 digit HUC)
If no credits available within the fourth order subbasin, the VESMP or DEQ as the VSMP authority credits within the same tributary may be used.
(Examples: property owners can convert agricultural land from crop, hay or pasture to conserved open space, and stream restoration projects)

## Slide 26: Offsite Compliance Options
4c. | ESM PLAN SUBMITTAL & REVIEW|
Hydrologic Unit Geography (virginia.gov)
Notes: A VESMP authority is authorized to allow the use of nutrient credits.
The credits must be from the same fourth order subbasin (similar to the previous regulation language of 8 digit HUC)
If no credits available within the fourth order subbasin, the VESMP or DEQ as the VSMP authority credits within the same tributary may be used.
(Examples: property owners can convert agricultural land from crop, hay or pasture to conserved open space, and stream restoration projects)

## Slide 27: Offsite Compliance Options
Nonpoint nutrient offset program
  Nutrient credits must:
    Comply with 1:1 ratio of credits to required P reduction
    Achieve nutrient reductions before start of land disturbance
    Be documented for VESMP authority and DEQ
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 17
Notes: Nutrient credits must also:
Comply with a 1:1 ration of credits to the required phosphorus reduction;
Achieve necessary nutrient reductions before the start of land disturbance; and be
Be documented in a certification from the credit provider with the number of phosphorus nutrient credits acquired and the associated ratio of nitrogen nutrient credits at the credit generating entity. Documentation must be provided to the VSMP authority and DEQ. The stormwater management plan submittal must include a letter of availability. When DEQ is the VSMP authority, the affidavit of sale is required in order to receive CGP coverage. The Notice of Termination must include information about the final credits purchased.

## Slide 28: Nonpoint Source Nutrient Trading
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 18
Notes: Nutrient banking within the 4th order subbasins: (illustrative purposes mainly – map may not be the most up to date list of banks)
Nutrient credits cannot be used to:
Address water quantity control requirements; nor to
Violate local water quality-based limitations.
(On the map, the light blue outline represents the 8 digit HUCs. Trading can be done within the HUC or adjacent, as long as it’s in the same watershed (represented by the solid colors)

## Slide 29: Conditions When Offsite Options Must be Allowed
1.
Less than 5 acres of land will be disturbed; or
2.
Post-construction P requirement is less than 10 lbs./yr.; or
3.
Operator demonstrates all of the following:
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 19
Notes: A VESMP authority must allow an operator to utilize offsite options under any of the following conditions:
Less than five acres of land will be disturbed;
The post-construction phosphorus control requirement is less than 10 pounds per year; or
The operator demonstrates the following to the satisfaction of the VSMP authority:

## Slide 30: Offsite Compliance Options
i.
Alternative site designs have been considered that may accommodate on-site BMPs,
ii.
On-site BMPs are considered in alternative site designs
iii.
Appropriate on-site BMPs will be implemented
iv.
Full compliance with post-development P requirements cannot practicably be met on-site
If 75% required P reduction can be met, the applicant is considered to have met the above conditions
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 19
Notes:   Alternative site designs have been considered that may accommodate on-site best management practices,
  On-site best management practices have been considered in alternative site designs to the maximum extent practicable,
  Appropriate on-site best management practices will be implemented, and
  Full compliance with the postdevelopment nonpoint nutrient runoff compliance requirements cannot practicably be met on-site.
If an applicant demonstrates onsite control of at least 75% of the required phosphorus nutrient reductions, the applicant is deemed to have met the four requirements above and must be allowed to use offsite options

## Slide 31: Requesting an Exception
Request for exception from Part V, Article 3 or 4 may be submitted in writing to the VESMP authority
Exceptions may be granted if all of the following conditions are met:
  Exception is minimum necessary to afford relief
  Intent of Act and Regulations are preserved
  No special privileges given
  Conditions aren’t self-imposed or self-created
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 20
Notes: A request for an exception from the Part V, Article 3 or 4 technical criteria, including the reason for making the request, may be submitted in writing to the VESMP authority.
A VESMP authority may grant exceptions to the technical requirements of Part V, Article 3 or 4 provided all of the following conditions are met:
  (Click) The exception is the minimum necessary to afford relief;
  (Click) Reasonable and appropriate conditions shall be imposed so that the intent of the Act and Regulations are preserved;
  (Click) Granting the exception will not confer any special privileges that are denied in other similar circumstances; and
  (Click) Exception requests are not based upon conditions or circumstances that are self-imposed or self-created.

## Slide 32: Requesting an Exception
Exceptions must not be granted for:
  Economic hardship alone
  Obtaining required state permits
  BMPs not on BMP Clearinghouse or VSMH, except where allowed under Part V, Article 4
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 20
Notes: Exceptions must not be granted for:
  Economic hardship alone;
  Obtaining required state permits; or the
  Use of a BMP not found on the Virginia Stormwater BMP Clearinghouse, except where allowed under Part V, Article 4.

## Slide 33: Requesting an Exception
Exceptions to requirements for phosphorus reductions are not allowed unless offsite options have been considered and found not available.
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 20
Notes: Exceptions to requirements for phosphorus reductions are not allowed unless offsite options have been considered and found not available.

## Slide 34: Security for Performance
Before plan approval, locality VESMP authority may require a security for performance
If locality takes action and it costs more than the security, locality may collect difference
Security must be refunded within 60 days of completing the permit termination requirements
4c. | ESM PLAN SUBMITTAL & REVIEW| Pg. 20
Notes: Before plan approval, a locality VESMP authority may require an applicant, excluding state or federal entities, to submit a security for performance to ensure that measures could be taken by the locality VESMP authority at the applicant’s expense should they fail, after proper notice, to initiate or maintain appropriate actions that may be required by the permit.
If the locality VESMP authority takes action and it costs more than the security held, then the locality may collect the difference.
The security must be refunded within 60 days of completing the permit termination requirements (Module 5).

## Slide 35: Q&A
4c. | ESM PLAN SUBMITTAL & REVIEW |
Plan Submittal and Review
Offsite Compliance Options
Exceptions; Security for Performance
Part V, Art. 3&4; Grandfathering
Notes: (Pause for Q&A session)
Does anyone have questions about:
REMINDER THIS PPT WILL BE AVAILIBLE ON ELMS
Add your questions into the question box and the moderator will read them.

## Slide 36: Module 4d.
Single-Family Detached Residential Structures

## Slide 37: LDA sizes (875-20)
“Small construction activity”
  One acre to less than five acres’ disturbance
  SFDs require CGP coverage
    No registration statement needed
    Print copy of CGP from website to include in SWPPP
“Large construction activity”
  Five acres’ disturbance or more
  SFDs require CGP coverage
    Registration statement is required
    No permit fee
4d. | Single-Family| Pg. 21
Notes: NOT COVERED IN PG – VERY IMPORTANT
Bottom of page 19 content under CGP isn’t completely accurate. See Construction SWM website for more info (screenshot next slide)

## Slide 38: SFD Coverage Details
Notes: Do not need to teach from, just showing the content is outlined on the website, under the Construction Permitting Program accordion. Please review it yourself!

## Slide 39: Module 4e.
Construction General Permit Issuance

## Slide 40: Role of the Locality VESMP Authority
Plan review and approval
Confirm registration statement is complete and accurate
Enter registration statement info into Construction General Permit (CGP) System
4e. | CGP ISSUANCE| Pg. 22
Notes: The locality VSMP authority is responsible for plan review and approval
Confirm the registration statement is complete and accurate.
After both the erosion and sediment control plan and stormwater management plan have been approved, the program administrator will enter the information from the registration statement into the Construction General Permit System, a database that notifies DEQ to approve permit coverage.

## Slide 41: Registration Statement
4e. | CGP ISSUANCE| Pg. 23-28
Notes: By signing the registration statement, the operator is certifying they have prepared a SWPPP in accordance with the permit requirements.
Pages 1-3 of the RS

## Slide 42: Registration Statement Instructions
4e. | CGP ISSUANCE| Pg. 26
CGP - Page 4
Notes: Instructions for completing the registration statement are included on pages 4-6 of the RS

## Slide 43: Registration Statement Instructions
Section I: Operator/Permittee Information
  Confirm the certification in Section VI is signed by someone with signatory authority for the associated operator listed in Section I
4e. | CGP ISSUANCE| Pg. 29
Notes: The following items are of note:
Item 1: Construction Activity Operator
  General permit coverage will be issued to the operator listed. As a program administrator it is important to confirm the certification in Section VI is signed by someone with signatory authority for the associated operator listed in Section I.

## Slide 44: Registration Statement Instructions
4e. | CGP ISSUANCE| Pg. 29
If a site is found to be out of compliance, the operator listed on the registration statement is ultimately responsible.
Remember, the person/company who is assigned the permit is responsible until the permit is terminated or transferred.

## Slide 45: Registration Statement Instructions
Section II: Construction Activity Information
  Location and Site Map
    Limits of Disturbance
    Water bodies
    Aerial or topographic
  Acreage totals
    Total land area of development
    Primary estimated area to be disturbed
    Offsite estimated area to be disturbed
4e. | CGP ISSUANCE| Pg. 29-30
Notes: 2A and B
2C

## Slide 46: Registration Statement Instructions
Item I: Receiving Waters and 6th order HUC is used to determine if a site is discharging to:
  Surface waters identified as impaired in the 2022 §305(b)/303(d) Water Quality Assessment Integrated Report for Benthic Macroinvertebrates or PCBs
  Waterways with a TMDL wasteload allocation that was established and approved before July 1, 2024 for (i) sediment or a sediment-related parameter (i.e., total suspended solids or turbidity) or (ii) nutrients (i.e., nitrogen or phosphorus) or PCBs
  Exceptional waters
4e. | CGP ISSUANCE| Pg. 29-30
Notes: Item I in Section 2 on the registration statement asks for the name of the receiving water(s) and 6th order hydrologic unit code (HUC), which DEQ will use to determine if a site is discharging to:
Surface waters identified as impaired in the 2022 § 305(b)/303(d) Water Quality Assessment Integrated Report
Waterways with a TMDL wasteload allocation that was established and approved before July 1, 2024 for (i) sediment or a sediment-related parameter (i.e., total suspended solids or turbidity) or (ii) nutrients (i.e., nitrogen or phosphorus); or
PCBs – if it’s a demo of 10,000 square feet of a building built or renovated before July 1, 1980; or
Exceptional waters identified in 9VAC25-260-30 A 3 c
The name of the receiving waters, HUC, and latitude and longitude can be obtained by using DEQ’s GIS Mapping Application. Link provided in participant guide.
TMDL stream segments can be located at link in participant guide.

## Slide 47: Impaired Waters and Waters with TMDL Limitations
Notes: Remember, these are the impaired waters and waters with TMDL limitations

## Slide 48: Registration Statement Instructions
Section III: Offsite Support Activity Location Information
  Offsite support activity terminates when the permit terminates
  Does not serve multiple operations
  Does not cover industrial manufacturing facilities
  Excavated material transported offsite must have location identified
4e. | CGP ISSUANCE| Pg. 30
Notes: The permit also authorizes stormwater discharges from on-site and off-site support activities (e.g., concrete or asphalt batch plants, equipment staging yards, material storage areas, excavated material disposal areas, borrow areas). The total land area of the off-site support activity and the estimated area to be disturbed by the off-site support activity must be included Section II C. Additionally, appropriate control measures must be identified in a SWPPP and implemented to address discharges from the support activity areas.

## Slide 49: Registration Statement Instructions
Section IV: Other Information
  Used to record plan approval for ESC
  Tracks land disturbance for reissued permits
  Utilizing approved Standards and Specifications; attached S&S Entity form
  Nutrient Credit Use (per 9VAC25-875-580)
    Copy of the letter of availability from an appropriate nutrient bank provided
    DEQ, as the VSMP authority, requires an affidavit of sale
4e. | CGP ISSUANCE| Pg. 31
Notes: Report date of ESC approval if it’s a reissuance, and areas that have started LDA to track ending of IIC criteria
Billing if different than in Section 1

## Slide 50: Fees
Fees are required for state permit issuance, reissuance, modification, or transfer
Registration statements considered incomplete if fee is not paid
4e. | CGP ISSUANCE| Pg. 31
Notes: Applicants are required to pay fees for state permit issuance, reissuance, modification, or transfer. Registration statements will be considered incomplete if the proper fee is not paid and will not be processed until the fee is received.
A locality VSMP authority can change the fee schedule with approval by DEQ. However, the state portion of the fee schedule cannot be changed.
These fees are also independent of any erosion and sediment control fees.

## Slide 51: CGP Issuance
Locality VESMP authority collects the state portion of the permit fee
1st
VESMP authority confirms application is complete
2nd
VESMP authority enters information from registration statement into system
3rd
Email notifying receipt of registration statement sent to VESMP authority and DEQ
4th
DEQ issues permit coverage to the operator and locality authority upon receipt of a complete registration statement and payment, if applicable
4e. | CGP ISSUANCE| Pg. 33
Notes: (Click for each step)
VESMP authority confirms application is complete
Enters the information from the registration statement into the system,
Locality VESMP authority and DEQ receive an email notifying receipt of the submission.
Then DEQ issues Construction GP coverage and the operator receives an email with the coverage letter. The locality VESMP authority is copied on the email. If the operator has chosen not to receive information electronically, the notice of coverage letter will be sent via the US Postal Service.

## Slide 52: CGP Issuance
Locality VESMP authority does not collect the state portion of the permit fee
1st
VESMP authority confirms application is complete
2nd
VESMP authority enters information from registration statement into system
3rd
Email notifying receipt of registration statement sent to VESMP authority and DEQ
4th
Email notifying operator of their payment options sent
5th
Payment submitted
6th
DEQ issues permit coverage to the operator and locality authority upon receipt of a complete registration statement and payment, if applicable
4e. | CGP ISSUANCE| Pg. 34
Notes: (Click for each step)
VESMP authority confirms the application is complete
VESMP authority enters the information from the registration statement into the system,
VESMP authority and DEQ receive an email notifying receipt of the submission.
Then the operator receives an email from DEQ explaining their payment options:
  Credit card online (fastest method); or
  Check or money order.
Once the operator makes their payment,
DEQ issues Construction GP coverage and the operator receives an email with the coverage letter. The locality VESMP authority is copied on the email. If the operator has chosen not to receive information electronically, the notice of coverage letter will be sent via the US Postal Service.
Sample Notice of Coverage Letter is provided on the following two pages (33-35) in the PG.

## Slide 53: Q&A
4f. Locality approval to start - online
4a. Regulated LDAs - online
4. | APPROVAL TO START LAND DISTURBANCE
4b. Application package
4c. ESM plan submittal & review
4d. Single-family - online
4e. CGP issuance
Notes: 4a and f were covered in their entirety in the online course. We covered portions of b, c, d, and e here. Now on to the activity!
(Pause for Q&A session)
We covered a lot in this module!
4a. Regulated LDAs
4b. Application Package
4c. SWM Plan Submittal and Review
4d. Single-Family Detached Residential Structures
4e. Construction GP Issuance
4f. Locality VSMP Authority Approval to Start Land Disturbance
Add your questions into the question box and the moderator will read them.

## Slide 54: Knowledge Check Questions
What must permit applicants submit to the VSMP authority about permanent stormwater management facilities before the stormwater management plan can be approved?
  Initial terms of the long-term maintenance agreement (operations and maintenance plan)
What must permit applicants submit to the VSMP authority as part of the stormwater management plan if they are using one of the off-site compliance options?
  A letter of availability from the off-site provider
4. | KNOWLEDGE CHECK QUESTIONS| Pg. 38-39
Notes: (You may want to give participants a few minutes to answers these first before discussing)
What must permit applicants submit to the VSMP authority about permanent stormwater management facilities before the stormwater management plan can be approved?
Initial terms of the long-term maintenance agreement (operations and maintenance plan)
What must permit applicants submit to the VSMP authority as part of the stormwater management plan if they are using one of the off-site compliance options?
  A letter of availability from the off-site provider

## Slide 55: Knowledge Check Questions
If a determination of completeness is not communicated to the applicant within the required timeframe, how long does the VSMP authority have to review the stormwater management plan?
  60 days from the time the plan was submitted
If a project received permit coverage in May 2012, what technical criteria is the project subject to? How long is the project subject to the technical criteria?
  The project is subject to the Part II C technical criteria until June 30, 2024. After that time, any portion of the site not under construction is subject to any new technical criteria.
4. | KNOWLEDGE CHECK QUESTIONS| Pg. 38-39
Notes: If a determination of completeness is not communicated to the applicant within the required timeframe, how long does the VSMP authority have to review the stormwater management plan?
60 days from the time the plan was submitted
If a project received permit coverage in May 2012, what technical criteria is the project subject to? How long is the project subject to the technical criteria?
The project is subject to the Part II C technical criteria until June 30, 2024. After that time, any unfinished portion of the site is subject to any new technical criteria

## Slide 56: Knowledge Check Questions
What type of regulated land-disturbing activity requires coverage under the Construction GP but does not need to submit a registration statement?
  Single-family homes disturbing greater than or equal to one acre
What must an operator submit in order to receive a Construction GP?
  Approved stormwater management plan, approved erosion and sediment control plan, registration statement*, fees*, security for performance*
4. | KNOWLEDGE CHECK QUESTIONS| Pg. 38-39
Notes: What type of regulated land-disturbing activity requires coverage under the Construction GP, but does not need to submit a registration statement?
Single-family homes disturbing greater than or equal to one acre (§62.1-44.15:28).
What must an operator submit in order to receive a Construction GP?
Approved stormwater management plan
Approved erosion and sediment control plan
Registration statement*
Fees*
Security for performance*
* As required

## Slide 57: Knowledge Check Questions
When can a locality approve the start of land disturbance?
  After DEQ has issued the Construction GP
4. | KNOWLEDGE CHECK QUESTIONS| Pg. 38-39
Notes: When can a locality approve the start of land-disturbance?
A locality VSMP authority may only approve the start of land-disturbance after DEQ has issued the Construction GP