## Slide 1: Module 5
Inspection Requirements, Permit Termination & Post-Construction Inspections

## Slide 2: Table of Contents
5a. Construction inspection requirements
5b. Permit termination
5c. Post-construction inspection requirements
5 | INSPECTION REQUIREMENTS & PERMIT TERM.| Pg. 1
Notes: At the end of this module, you will be able to:
 Describe the VESMP authority inspection requirements
 List all the Construction General Permit termination requirements
 Describe the VESMP authority post construction inspection requirements

## Slide 3: Module 5a.
Construction Inspection Requirements

## Slide 4: Construction Inspections
VESMP authority inspections must review:
  Compliance with approved ESC plan
  Compliance with approved SWM plan
  Development, updating, implementation of P2 plan
  Development and implementation of additional control measures to address a construction-related TMDL (when required)
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 3
Notes: The VESMP authority must inspect a land-disturbing activity for:
Compliance with the approved erosion and sediment control plan;
Compliance with the approved stormwater management plan;
Development, updating, and implementation of a P2 plan; and
Development and implementation of any additional control measures necessary to address a TMDL.

## Slide 5: Inspection Frequency
During construction, periodic inspections are:
  During, or immediately following, initial installation of ESCs
  At least once every two weeks AND within 48-hours of a runoff-producing storm event
  At the completion of the project, prior to bond release
  or
  A DEQ-approved alternative inspection program
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 3
Notes: As discussed in ESC PA…

## Slide 6: Construction Inspections
Keep in mind, the Virginia Erosion and Stormwater Management Regulation requires both VESMP and VESCP authorities to inspect regulated LDAs during construction.
The contents of the VESMP authority’s inspections are broader.
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 3
Notes: VESMP authority inspections cover the Stormwater component and proper installation of those practices, so at times, this may require more frequent inspections.

## Slide 7: Inspection Frequency
As a program administrator…
It is important to know the inspection requirements so you can ensure your locality’s program meets the regulatory requirements.
You should read through and become familiar with the Construction General Permit Regulation (9VAC25-880).
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 3

## Slide 8: Inspection of Projects with Standards and Specifications
Programmatic inspections
  Similar to VESMP, or part of an alternative schedule
SWPPP inspection
  Inspection schedule in the CGP
DEQ inspections
  Randomly
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 4
Notes: State employees or contractors performing programmatic level inspections under standards and specifications (similar to inspections of private projects by locality VESMP authorities) must conduct periodic inspections to determine compliance with the stormwater program. Every 2 weeks and within 48 hours of rainfall
(Click) State employees or contractors performing SWPPP inspections under the Construction GP must follow the inspection schedule in the Construction GP (9VAC25-880-70 Part I B 4 and II F 2). This pertains to “qualified personnel”.
(Click) DEQ is required to randomly inspect state projects with standards and specifications.

## Slide 9: Right of Entry
Authorized under Act
  Reasonable times
  Reasonable
  circumstances
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 4
Notes: The Act authorizes DEQ, a VESMP authority, or a MS4 authority to, at reasonable times and under reasonable circumstances, enter establishments or properties for the purpose of obtaining information, conducting surveys or investigations necessary to enforce the Act.

## Slide 10: Modifications & Amendments to ESM Plans
Modifications to an approved plan must be reviewed by the VESMP authority
  How long does the plan reviewer have to review plan amendments?
    60 calendar days
Inspectors can require plan amendments to an approved plan to address deficiencies within a set timeframe
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 4
Notes: (Click) How long does the plan reviewer have to review plan amendments?
(Click) 60 calendar days
(Click) Based on an inspection, the VESMP authority may require amendments to the approved plan to address any deficiencies within a timeframe set by the VESMP authority.

## Slide 11: SWPPP Documentation
SWPPP requirements may be fulfilled by incorporating by reference other plans
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 5
Notes: The SWPPP requirements may be fulfilled by incorporating by reference other plans such as a spill prevention control and countermeasure (SPCC) plan.
All plans incorporated by reference into the SWPPP become enforceable under the Construction GP.
If a plan incorporated by reference does not contain all of the required elements of the SWPPP, the operator must develop the missing elements and include them in the SWPPP.

## Slide 12: SWPPP Documentation
1. General information
2. Approved ESC plan
3. Approved SWM plan
4. P2 plan
5. Impaired waters and TMDL requirements
6. PCB impaired waters and TMDL requirements
7. Exceptional waterways
8. Turbidity monitoring requirements
9. Qualified personnel
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 5
11. SWPPP signature
10. Duly Authorized Representative
12. SWPPP inspection records
Notes: (talk about each of these in next slides)

## Slide 13: SWPPP Documentation
1. General information
Signed copy of the registration statement
Copy of the notice of coverage letter
Copy of the Construction General Permit
Narrative description of the nature of the construction activity, including the function of the project
Legible map of the construction site
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 5-6
Notes: 1. General information
Signed copy of the registration statement
Copy of the notice of coverage letter
Copy of the Construction GP
Narrative description of the nature of the construction activity, including the function of the project (e.g., low density residential, shopping mall, highway)
Legible site plan

## Slide 14: SWPPP Documentation
2. Approved ESC plan
Describes structural and non-structural practices to be used during construction to keep sediment in place and capture any sediment that is moved by stormwater before it leaves the site
Approved by VESCP/VESMP authority
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 6
Notes: 2. Approved erosion and sediment control plan
(Review of previous content covered)

## Slide 15: SWPPP Documentation
3. Approved stormwater management plan
Describes methods to be used for controlling post-construction stormwater discharges
Approved by VESMP authority
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 6
Notes: 3. Approved stormwater management plan
(Review of previous content covered)

## Slide 16: SWPPP Documentation
4. Pollution prevention plan
Describes good housekeeping practices to minimize the discharge of pollutants from construction sites
Developed before land disturbance
Updated throughout construction
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 6
Notes: 4. Pollution prevention (P2) plan
(Review of previous content covered)

## Slide 17: SWPPP Documentation
5. Impaired waters + TMDL waters requirements
Identify impaired water(s), approved TMDL(s), and pollutant(s) of concern
Provide clear direction that:
  Stabilization applied to denuded areas within 7 days after final grade reached on any portion of site
  Nutrients properly applied
  SWPPP inspection schedule modified
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 6
Notes: 5. Additional requirements for discharges to impaired waters, surface waters with an applicable TMDL wasteload allocation and exceptional waters
Identify the impaired water(s), approved TMDL(s), pollutant(s) of concern, and exceptional waters
(Click) Provide clear direction that:
(Click) Permanent or temporary soil stabilization must be applied to denuded areas within seven days after final grade is reached on any portion of the site
(Click) Nutrients must be applied in accordance with manufacturer's recommendations or an approved nutrient management plan and must not be applied during rainfall events
(Click) A modified SWPPP inspection schedule shall be implemented in accordance with Part II G 2 a. of the CGP

## Slide 18: SWPPP Documentation
6. Impaired waters or TMDL waters with PCB WLAs
Demolition projects over 10,000 square feet which were renovated or constructed prior to January 1, 1980
  ESC plan implemented
  Comply with other additional TMDL requirements
  All federal, state, and local disposal requirements to be followed
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 6-7
Notes: 6. Additional requirements for discharges to impaired waters or surface waters with an applicable TMDL wasteload allocation for PCBs
Identify the impaired water(s), approved TMDL(s)
Comply with same requirements noted on previous slide:
  Permanent or temporary soil stabilization must be applied to denuded areas within seven days after final grade is reached on any portion of the site
  Nutrients must be applied in accordance with manufacturer's recommendations or an approved nutrient management plan and must not be applied during rainfall events
  A modified SWPPP inspection schedule shall be implemented in accordance with Part II G 2 a. of the CGP

## Slide 19: SWPPP Documentation
7. Exceptional waters requirements
Identify exceptional waters
Provide clear direction that:
  Stabilization applied to denuded areas within 7 days after final grade reached on any portion of site
  Nutrients properly applied
  SWPPP inspection schedule modified
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 7
Notes: 7. Additional requirements for discharges to exceptional waters
Identify exceptional waters
(Click) Provide clear direction that:
(Click) Permanent or temporary soil stabilization must be applied to denuded areas within seven days after final grade is reached on any portion of the site
(Click) Nutrients must be applied in accordance with manufacturer's recommendations or an approved nutrient management plan and must not be applied during rainfall events
(Click) A modified SWPPP inspection schedule shall be implemented in accordance with Part II G 2 a. of the CGP

## Slide 20: SWPPP Documentation
8. Turbidity monitoring requirements
Construction dewatering discharges to impaired, sediment-related TMDL or exceptional waters
All dewatering discharge locations identified
Daily monitoring required during dewatering operations
Three benchmark options for measurements
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 7
Notes: Dewatering discharges to Benthic Macroinvertebrate impaired, or exceptional waterways. Or a sediment related TMDL waterway

## Slide 21: SWPPP Documentation
9. Qualified personnel
Name, phone number and qualifications listed
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 8
Notes: 9. Qualified personnel
The name, phone number, and qualifications of the qualified personnel conducting inspections must be listed.
(Defined in #12)

## Slide 22: SWPPP Documentation
10. Duly Authorized Representative
Individuals or positions with delegated authority to sign inspection reports or modify the SWPPP
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 8
Notes: 10. Duly authorized rep
List the individuals or positions with delegated authority (from the operator), in accordance with 9VAC25-880-70 Part III K, to sign inspection reports or modify the SWPPP.

## Slide 23: SWPPP Documentation
11. SWPPP signature
Certification statement signed and dated by operator or duly authorized representative
Reports must also be signed by operator or duly authorized representative
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 8
Notes: 11. SWPPP signature
The SWPPP must be signed and dated by operator or duly authorized representative of the operator with the following certification (9VAC25-880-70 Part III K 4):
"I certify under penalty of law that I have read and understand this document and that this document and all attachments were prepared in accordance with a system designed to assure that qualified personnel properly gathered and evaluated the information submitted. Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete. I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations."
Reports, including inspection reports, must also be signed by the operator. The operator may be the same person that signed the registration statement, or that person may authorize a representative to sign on their behalf. The representative may be an individual or a position having responsibility for the overall operation of the regulated facility or activity.
Reports can be signed by:
Corporations – Responsible corporate officer
Partnership or sole proprietorship – General partner or the proprietor
Municipality, state, federal, other public agency – Principal executive office or ranking elected official

## Slide 24: SWPPP Documentation
12. SWPPP inspection records
Qualified personnel must conduct inspections
  Knowledgeable in ESC and SWM
  Can assess site conditions and effectiveness of ESC and SWM controls
  Add SWPPP inspection reports to SWPPP within 4 days
  Update SWPPP of changes as soon as possible, but no later than 5 business days
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 9
Notes: 12. SWPPP inspection records
(9VAC25-880-70 Part II F 2)
The operator must have a qualified person conducting inspections to ensure compliance with the SWPPP. A qualified person is defined as someone who is knowledgeable in the principles and practices of erosion and sediment and stormwater management controls who possesses the skills to assess conditions at the construction site for the operator that could impact stormwater quality and quantity and to assess the effectiveness of any sediment and erosion control measures or stormwater management facilities selected to control the quality and quantity of stormwater discharges from the construction activity (9VAC25-870-10).

## Slide 25: SWPPP Documentation
12. SWPPP inspection records
By July 1, 2025, to be qualified, personnel must have completed training and obtained either:
  Dual Inspector certification
  CGP Qualified Personnel Course Certificate
  Equivalent certification by EPA
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 9
Notes: 12. SWPPP inspection records
getting at how people are “knowledgeable in ESC and SWM”

## Slide 26: SWPPP Inspections
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 10
SWPPP Inspection Schedule (9VAC25-880-70 Part I B 4-6 and Part II G 2) | 
Discharges to impaired waters, surface waters with an applicable TMDL or exceptional waters | Standard Inspections
Inspections must be conducted either: At least once every 4 business days; or At least once every 5 business days and no later than 24 hours following a measurable storm event | Inspections must be conducted either: At least once every 5 business days; or At least once every 10 business days and no later than 24 hours following a measurable storm event
Notes: The qualified personnel must conduct inspections in accordance with the following:
(Click) If the project is discharging to impaired waters, surface waters with an applicable TMDL wasteload allocation or exceptional waters, then the qualified personnel must conduct inspections at the following frequency: (from slide)
(Click) If the project is discharging to a waterway without a limitation, then the qualified personnel must conduct inspections at the following frequency: (from slide)
Measurable storm event is defined as a rainfall event producing 0.25 inches of rain or greater over 24 hours

## Slide 27: Duty of the Operator to Provide Information
DEQ or VESMP authority
Permit applicant, permittee, anyone subject to Construction GP
Application materials, plans, specs, other info
Effect of discharge on quality of state waters
May require
To provide
To determine
5a. | CONSTRUCTION INSPECTION REQUIREMENTS| Pg. 11
Notes: DEQ or the locality VESMP authority may require every permit applicant, every permittee, or any person subject to state permit requirements to provide the following to determine the effect of the discharge on the quality of state waters:
  Application materials
  Plans
  Specifications
  Monitoring reports and other pertinent information

## Slide 28: Module 5b.
Permit Termination

## Slide 29: Permit Termination
1. Construction ends
2. Operator submits notice of termination to locality VESMP authority
3. Locality VESMP authority inspects site
4. Notice of termination entered into CGP System
5. Permit terminated by DEQ
6. Locality VESMP authority returns bonds or securities
7. Locality VESMP authority maintains documents and records
8. Post construction inspections
5b. | PERMIT TERMINATION | Pg. 12
Notes: 5b explains the process an operator has to follow to terminate permit coverage and the responsibilities of the program administrator in the permit termination process

## Slide 30: CGP Termination Requirements
Permit termination checklist
Permit termination requirements met
DEQ Notice of Termination form completed
  Confirmation long-term maintenance agreement(s) recorded in local land records (when applicable)
  Information on permanent control measures recorded (when applicable)
Construction record drawing(s) for permanent stormwater management facilities submitted to VESMP authority (when applicable)
5b. | PERMIT TERMINATION | Pg. 12
Notes: When an operator is ready to terminate their Construction GP coverage, they submit the DEQ Notice of Termination form to the VSMP authority. Before entering the information on the form into the CGP System, the VESMP authority should confirm the following has been completed: (from slide)
We’ll discuss each of these requirements in more detail

## Slide 31: Notice of Termination
N.O.T. must be submitted within 30 days of meeting one of the following permit requirements:
5b. | PERMIT TERMINATION | Pg. 13
Notes: The operator must submit the DEQ Notice of Termination form to the VSMP authority within 30 days of meeting one or more of the following conditions….

## Slide 32: Notice of Termination
Necessary permanent control measures included in the SWPPP for the site are in place and functioning effectively and final stabilization has been achieved on all portions of the site for which the operator is responsible (75% vegetative coverage with no significant bare areas).
  When applicable, long-term responsibility and maintenance requirements for permanent control measures must be recorded in the local land records before the submission of the Notice of Termination
5b. | PERMIT TERMINATION | Pg. 13
Notes: Typical situation when a permit is terminated…
“permanent control measures” is typically the BMPs

## Slide 33: Notice of Termination
Another operator has assumed control over all areas of the site that have not been fully stabilized and obtained coverage for the ongoing discharge
Coverage under an alternative VPDES or state permit has been obtained
5b. | PERMIT TERMINATION | Pg. 13
Notes: Maybe operator and owner had a falling out, and the owner has a new contractor/developer they’ve hired. Or the original operator went belly-up and the owner hired someone new.

## Slide 34: Notice of Termination
For residential construction only, temporary soil stabilization has been completed and the residence has been transferred to the homeowner*
5b. | PERMIT TERMINATION | Pg. 13
*Written notification to homeowner about the benefits of permanent stabilization must be recorded and kept with project records for 3 years
Notes: Maybe the new project is a car wash, and they’ll need another permit for that permanent discharge from the facility. They can terminate the CGP and move over to that longterm permit (not typical)
(Click) residential only…

## Slide 35: Notice of Termination
When receiving a complete N.O.T. form
  VESMP authority must act within 60 days
  Recommend termination to DEQ
5b. | PERMIT TERMINATION | Pg. 13
Notes: Authorities are required “to act” on complete NOTs within 60 days, by entering the info into the CGP System and submitting to DEQ that the permit should be terminated.
DEQ will then….

## Slide 36: Notice of Termination
5b. | PERMIT TERMINATION | Pg. 13
For all options: Authorization to discharge terminates, either:
  90 days following submittal of complete & accurate N.O.T.
  upon notification from DEQ,
OR
whichever occurs first
Notes: Once DEQ has been notified through the CGP System that the permit should be terminated….
Unless otherwise notified by the VESMP or DEQ

## Slide 37: Notice of Termination
As a program administrator…
You will be entering the information from the notice of termination forms into the Construction General Permit System.
5b. | PERMIT TERMINATION | Pg. 13

## Slide 38: Notice of Termination
Notes: There is a copy of the Notice of Termination form on pages 14-19 in your participant guide. It is the 2019 one. You can get the 2024, as shown here, from the Construction Stormwater webpage.

## Slide 39: Long-Term Maintenance Agreement
At a minimum, the agreement must:
  Be stated to run with the land
  Provide for all necessary access to the property for purposes of maintenance and regulatory inspections
  Provide for inspections and maintenance and the submission of inspection and maintenance reports to the VESMP authority
  Be enforceable by all appropriate governmental parties
5b. | PERMIT TERMINATION | Pg. 23
Notes: Run with the land means that when the property is sold, the new owner is aware of the facility and its maintenance requirements
Authority inspections
Owner required inspections and whether or not they should be submitted to authority

## Slide 40: Long-Term Maintenance Agreement
Proof of recordation must be provided with Notice of Termination
5b. | PERMIT TERMINATION | Pg. 23
Notes: Remember, if the operator is terminating their permit coverage because permanent control measures from the SWPPP have been installed and are functioning effectively and final stabilization has been achieved on all portions of the site for which the operator is responsible, then when applicable, the operator needs to have recorded a long-term maintenance agreement in the local land records before submitting the Notice of Termination

## Slide 41: Information on Permanent Control Measures
5b. | PERMIT TERMINATION | Pg. 23 | CGP-NOT Page 4 of 8
Notes: When applicable, the operator must include a list of on-site and off-site permanent control measures on the DEQ Notice of Termination form.
Multiple boxes provided on page 3 of 6 on the N.O.T.
Confirm accuracy of info with inspector before entering info into CGP system

## Slide 42: Construction Record Drawings
Required for permanent stormwater management facilities
Signed and sealed by a professional registered in Virginia
Completed per 9VAC25-875-535
5b. | PERMIT TERMINATION | Pg. 24
Notes: Once construction is complete, a construction record drawing for permanent stormwater management facilities must be submitted to the VSMP authority. The construction record drawing must be appropriately sealed and signed by a professional registered in the Commonwealth of Virginia, certifying that the stormwater management facilities have been constructed in accordance with the approved plan (or shows the variances from it).
Completed per requirements of a SWM plan
Remember, a VESMP authority may elect not to require construction record drawings for stormwater management facilities designed to treat stormwater runoff primarily from an individual residential lot on which they are located.

## Slide 43: Processing Permit Termination
Locality VESMP authority determines project is ready for permit termination
Program administrator enters information into CGP System
DEQ reviews and approves the termination
Operator receives termination letter via email (VESMP cc’d) or US Postal Service
5b. | PERMIT TERMINATION | Pg. 24
Notes: Once the locality VSMP authority determines a project is ready for permit termination, the program administrator finds the permit in the Construction GP System and enters the required information. Then DEQ reviews and approves the termination, and the operator is sent a termination letter via email or US Postal Service. The locality VSMP authority will also receive the email notification.

## Slide 44: Security for Performance
VESMP authority must return or terminate any bonds or securities within 60 days of completing permit termination requirements
60 days
5b. | PERMIT TERMINATION | Pg. 24
Notes: Within 60 days of completing the requirements of the permit conditions, the VESMP authority must return or terminate any bonds or securities provided by the operator at the onset of the project.

## Slide 45: Single-Family Detached Residential Structures
Localities may choose:
  Whether or not to require a long-term maintenance agreement
    Must still demonstrate future maintenance will be addressed through an enforceable mechanism
  No long-term maintenance agreement = no post-construction inspections
    Localities can also choose not to require construction record drawings
5b. | PERMIT TERMINATION | Pg. 25
Notes: Don’t need an NOT if they didn’t submit an RS, which is the case with small SFDs; large construction SFD over 5 acres would need a NOT
Future maintenance through an enforceable mechanism = HOA covenants???

## Slide 46: Quick Poll
Notes: How long does the authority have to return any bonds once the operator completes permit termination?
60 days – correct
90 days
6 months
1 year

## Slide 47: QuickPoll – Security for Performance
How long does the authority have to return any bonds once the operator completes permit termination?
60 days
90 days
6 months
1 year

## Slide 48: Module 5c.
Post-Construction Inspection Requirements

## Slide 49: Post-Construction Inspection Frequency
5 years
5c. | POST-CONSTRUCTION| Pg. 26
Notes: VESMP authorities must ensure stormwater management facilities are inspected by the VESMP authority or its designee at least once every five years. The inspections must be documented by records.

## Slide 50: Post-Construction Inspection Frequency
5c. | POST-CONSTRUCTION| Pg. 26
VESMP authority can use inspection reports from:
Licensed professional engineer, architect, landscape architect, or land surveyor
Someone working under the direction and oversight of a licensed professional
Certified SWM Inspector or Dual Inspector from DEQ
Notes: The VESMP authority may utilize the post-construction inspection reports of the owner of a stormwater management facility as part of its established inspection program if the inspection is conducted by:
A person who is licensed as a professional engineer, architect, landscape architect, or land surveyor;
or a person who works under the direction and oversight of the licensed professional;
or a person who holds an appropriate certification from DEQ (SWM Inspector).

## Slide 51: State Agency Standards and Specifications
5c. | POST-CONSTRUCTION| Pg. 26
Operation and maintenance stays with state agency
If sold, operation and maintenance transfers to new owner
State agency must inspect at least yearly or after certain storms
Notes: Responsibility for the operation and maintenance of stormwater management facilities must remain with the state agency and shall pass to any successor or owner. If portions of the land are to be sold, legally binding arrangements shall be made to pass the basic responsibility to successors in title. These arrangements shall designate for each state project the property owner, governmental agency, or other legally established entity to be permanently responsible for maintenance.
At a minimum, a stormwater management facility shall be inspected by the responsible state agency on an annual basis and after any storm which causes the capacity of the facility’s principal spillway to be exceeded.

## Slide 52: Quick Poll
Notes: How often must the VESMP authority ensure stormwater management facilities are inspected after construction?
Annually
At least bi-annually
At least once every five years – correct
Only if the site is redeveloped.

## Slide 53: QuickPoll – Post-Const. Inspections
How often must the VESMP authority ensure stormwater management facilities are inspected after construction?
Annually
At least bi-annually
At least once every five years
Only if the site is redeveloped.

## Slide 54: Q&A
Construction Inspections
Post Construction Inspections
Permit Termination
Notes: (Pause for Q&A session)
Does anyone have questions about:
Add your questions into the question box and the moderator will read them.

## Slide 55: Knowledge Check Questions
How often must a VSMP authority inspect a land-disturbing activity?
  Periodically
What must a VSMP authority inspect a land-disturbing activity for?
  Compliance with the approved erosion and sediment control plan and approved stormwater management plan; development, updating, and implementation of a P2 plan; and development and implementation of any additional control measures necessary to address a TMDL
5. |KNOWLEDGE CHECK QUESTIONS| Pg. 24
Notes: How often must a VSMP authority inspect a land-disturbing activity?
Periodically
What must a VSMP authority inspect a land-disturbing activity for?
Compliance with the approved erosion and sediment control plan;
Compliance with the approved stormwater management plan;
Development, updating, and implementation of a P2 plan; and
Development and implementation of any additional control measures necessary to address a TMDL

## Slide 56: Knowledge Check Questions
What must the operator submit to the VSMP authority before the Construction General Permit is terminated that certifies that the stormwater management facilities have been constructed in accordance with the approved stormwater management plan?
  Construction record drawing
How long does a locality VSMP authority have to return or terminate any bonds or securities?
  Within 60 days of meeting permit termination requirements
5. |KNOWLEDGE CHECK QUESTIONS| Pg. 24
Notes: What must the operator submit to the VSMP authority before the Construction General Permit is terminated that certifies that the stormwater management facilities have been constructed in accordance with the approved stormwater management plan?
Construction record drawing
How long does a locality VSMP authority have to return or terminate any bonds or securities?
Within 60 days of meeting permit termination requirements

## Slide 57: Knowledge Check Questions
How often must the VSMP authority ensure stormwater management facilities are inspected after construction?
  At least once every 5 years
5. |KNOWLEDGE CHECK QUESTIONS| Pg. 24
Notes: How often must the VSMP authority ensure stormwater management facilities are inspected after construction?
At least once every 5 years

## Slide 58
Course Completion Certificates and Survey in ELMS
Download the Candidate Information Booklet (CIB) from the Pearson Vue Website
Access PPTs on OTS Website under Course Materials page
Reach out to OTS Trainers for virtual “Office Hours”