## Slide 1: SWM Program Overview:
VESMP Process Activity
Review for Program Administrators
Notes: This activity is a review of the PG Modules 3 & 4: *Click*
Module 3: Administering a Stormwater Program
Module 4: Approval to Start Land Disturbance

## Slide 2: Directions:
| Regulated LDA | Exemption status |
As the local VESMP - Program Administrator:
Use the provided information to go through the VESMP process to determine if the land-disturbing activity in question should be REGULATED by the VESMP authority, OR if the activity in question falls under the status of an EXEMPTION
Determine follow-up procedures once Regulated/Exempt status is determined
Decide what actions a VESMP Program Administrator should take during the VESMP process

## Slide 3: Directions:
| Regulated LDA | Exemption status |
Establish the situation
Review all site information, including reports, photos, and correspondence
Decide the next course of actions
Determine if the activity in question is a Regulated LDA or if the activity falls under an Exemption status
Conclude next steps for VESMP Authority
Notes: *Click* (Directions will appear)

## Slide 4: Setting:
| Regulated LDA | Exemption status |
Chesapeake Bay Preservation Areas
  Localities with watersheds that discharge directly to the Chesapeake Bay or immediate tributaries
3A&B
Notes: Setup the situation: *click*
Our example takes place in Virginia, in a CBPA locality. *click*
So, some considerations here regarding discharge to the Ches Bay or its immediate tributaries …
Ask folks to consider this information: SWM-PA Mod. 3b. (Local Ordinances for Chesapeake Bay Preservation Act LDAs)
3A: More Stringent Ordinance
(There is a list of localities (Counties, Cities, and Towns) in Mod 3: on PG page 18)

## Slide 5
| Regulated LDA | Exemption status |
Local authority Inspector observes possible disturbance; mud on public road but tracks coming from private property
Situation – Potential Land-disturbing activity
5A
Notes: TELL THE STORY // Setup the situation:
The Local authority inspector was driving back from another inspection and notices some mud tracking onto a public road, but does not want to go onto private property to investigate.
*CLICK*
Make the point that Right to Entry (5A) does give VESMP authorities some recourse to go onto private property, but the inspector elects not to in this situation.
RANDOM CALL BACK TO : MS-17: Vehicular Tracking and Construction Entrances

## Slide 6: Situation – Potential Land-disturbing activity
| Regulated LDA | Exemption status |
The Inspector reviews some imaging of the area and finds a very recent aerial image
 Next Step?
Notes: Setup the situation:
Back in the field office, the inspector looks at aerial imaging of the mud tracking and finds potential disturbance up a private road.
(1.Click) First Red circle shows where the initial mud was tracked onto public road
(2.Click) Yellow arrow shows private road where tracking looks like it originated
(3.Click) Second Red circle shows where a potential disturbance may be and the source of the mud tracking
(4.Click) Ask what folks think the next step is.
NEXT STEPS  Quick-Poll
Fun Fact: The Real Estate Division of the Locality's Planning Department tend to find it fiscally beneficial to review annual aerial photography of their jurisdiction to ensure accurate property assessments and taxes can be collected.

## Slide 7: QuickPoll
Notes: Q: What’s the next course of action for the VSMP authority?
Get a road crew to clean up the road, and the main problem is addressed.
Look into who the land owner is, and contact them.
Prepare a Stop Work Order, and have the Inspector hand deliver to the site.
Assume the mud tracking came from local soybean farmers in the area and defer to VDACS for follow-up.
- VDACS = Va Dept. of Agriculture and Consumer Services
Looking for [B] as the correct answer.
Need to find out who owns the land and inquire as to the nature of the LDA.

## Slide 8: Q: What’s the next course of action for the VESMP authority?
| Regulated LDA | Exemption status |
Get a road crew to clean up the road, and the main problem is addressed.
Look into who the land owner is, and contact them.
Have the Inspector hand deliver a Stop Work Order to the site.
Assume the mud tracking came from local farmers in the area (not our problem).
Notes: Looking for [B] as the correct answer.
Need to find out who owns the land and inquire as to the nature of the LDA.

## Slide 9
| Regulated LDA | Exemption status |
Known Information:
Mud tracking coming from private property
Location of potential LDA
Parcel Information via GIS (or another database)
Notes: POST POLL: re-iterate the situation at hand and walk through the course of actions:
*Click*
We Look up the area in question via parcel information database.
Fun Fact: Localities will give some employees access to courthouse databases to be able to research and review deeds! Sales of property and etc are beneficial in enforcement research

## Slide 10: Situation: Contact Land Owner – LDA Inquiry
| Regulated LDA | Exemption status |
VESMP Authority emails Landowner: Inquiring about the nature of the disturbance
Requests an on-site inspection with Authority staff
5A
Notes: Once the owner is identified, we can contact the owner to inquire about the nature of the activity AND send our Inspector to the site (with owner permission) to assess the scope of the LDA.
*Click* REITERATE: MOD 5A: Right of Entry - P. 4  “for the purpose of obtaining information or conducting surveys or investigations necessary”

## Slide 11: Situation: Contact Land Owner – Response
| Regulated LDA | Exemption status |
Owner response: Claims service connection work Exempt – running water lines through property
Includes simple utility plan to show scope of work
Field verification needed
Notes: (Click) Email moves right.
Owner is claiming Exemption  Individual Service Connection.
(Click) Owner submits plan sheet showing utility work for an individual connection – Plat confirms the disturbance is under 1 acre, so are we done investigating the situation? No!!!
(Click) Field verification needed. Send your INSPECTOR OUT to confirm the claim!

## Slide 12: Service Connection Exemption
| Regulated LDA | Exemption status |
Private Property
Developer actively trenching of waterlines
LDA ~ quarter mile of linear excavation
Thoughts… check the regs
LDA: Regulated
-or- Exempt?
4A
Notes: Inspector field confirms: Mod 4A: Regulated LDA – Exemptions
*click* ( Information about our site in question appear on screen )
*Click* THOUGHTS: (remember we are in a CBPA)
Do we need a local E&S control LD permit?  If over 10,000 sqft, or stricter local ordinance threshold: YES
Is it part of a Common Plan of Development?
ASK folks, what page in the PG is Exemptions?  MOD 4: PG 4
  Is this enough information, are we satisfied with what we see to make that call? (flow into QP)
- *Last Click* LDA Regulated or Exempt  Launch Quick Poll

## Slide 13: QuickPoll
Notes: This is an Exempt activity. No further local authority action necessary.
This is NOT an Exempt activity. VESMP require an ESC plan.
Inquire for more project information.
This is NOT an Exempt activity. VESMP require CGP coverage.
Looking for [C] as the best answer. Given the snapshot of info we have at this point, it isn’t clear how we should regulate this LDA. Need dig deeper
VESMP should look further into the site; authority should dig a little deeper based on what little information has been provided for as an overall plan for the water line installation.
Based on the snapshot of info [A] could be correct. A good talking point.

## Slide 14: Q: Considering what the regs say about Exemptions, what’s a possible next step for the VESMP? (choose all that apply):
| Regulated LDA | Exemption status |
This is an Exempt activity. No further local authority action necessary.
This is NOT an Exempt activity. VESMP require an ESC plan.
Inquire for more project information.
This is NOT an Exempt activity. VESMP require CGP coverage.
Notes: Looking for [C] as the correct answer.
VESMP should look further into the site; authority should dig a little deeper based on what little information has been provided for as an overall plan for the water line installation.
Based on the snapshot of info [A] could be correct. A good talking point.

## Slide 15: Situation: Digging Deeper
| Regulated LDA | Exemption status |
Planning department received a building plat at that address for a SFD
Includes scope of construction to include LDA of about 30,000sqft.
Notes: *Click* Text and Plat appear
Locality received a building plat for a single-family dwelling to be built with service connection work
Implying that the service connection work MAY qualify as an exemption if it’s ONLY serving this one SFD.
*Click*
Text showing LDA is less than 1acre

## Slide 16: Single Family LDAs
| Regulated LDA | Exemption status |
 Thoughts…
Private Property
LDA < 1 acre (building plat)
ESC plan LDA Threshold * > 10,000 sqft
CBPA LDA Threshold * > 2,500 sqft
More stringent ordinance
* Water quantity compliance required
4D
Notes: Review LDA thresholds for folks, so we get an idea of the compliance requirements  Mod 4D
*CLICK* Water Quantity Compliance Threshold!
*CLICK*
Thoughts...
  See what folks think we should do next….looking for “get more info”
  We’re not done. Try and make the connection between the waterline install and the SFD.
ULTIMATE QUESTION NEEDS TO BE ASKED: is the individual service connection Exempt or is the scope of work larger than the Exemption allows for?

## Slide 17
| Regulated LDA | Exemption status |
Further Inspection
Preliminary grading plan submitted prior (not approved)
Separate developers moving forward with single lot builds
No utility infrastructure
…..yet
Notes: Site inspection reveals gravel road access to site with no evidence of utility infrastructure, raising the question of whether there is a more comprehensive plan that includes work to install better infrastructure.
After looking over the building plat, the VESMP Authority Plan Reviewer realizes that the lot is part of a larger plan that had been submitted, not approved, and the developer has yet to move forward with that plan. Rather, the developer has chosen to build lots individually.
So development is broken into separate plans but part of a related project. So, what is the connection, and is there an overall infrastructure plan?

## Slide 18
| Regulated LDA | Exemption status |
Further Inspection
Preliminary grading plan submitted prior (not approved)
Separate developers moving forward with single lot builds
No utility infrastructure
…..yet
Utility Dept. has preliminary infrastructure plan showing service connection to main water line excavation project
Notes: (CLICK) we know the landowner has some type of waterline plan.
(CLICK) Digger deeper, we find the Utility department has an overall utility plan showing

## Slide 19
| Regulated LDA | Exemption status |
Further Inspection
Utility Dept. has preliminary infrastructure plan showing service connection to main water line excavation project
1.3 linear miles of trench
~ roughly 3.5 acres of clearing/grading
Notes: (auto shift) show: 1.3 miles of trench, 3.5 acres of LD
(CLICK)

## Slide 20
| Regulated LDA | Exemption status |
Service Connection Review
Unpermitted land disturbance
LDA: Regulated
-or- Exempt?
Submitted building plat confirms SFD construction
No current utilities/service connections installed
Individual and a larger, overall waterline and infrastructure plan over 1 acre of disturbance
Notes: Review the Situation: a claim for an exemption for an individual service connection .
*5 CLICKS*
Regulated or Exempt?: based on all of our discussion and fact finding!!
Regulated; with a minimum requirement of an ESC land disturbing permit. Hence, Regulated and needing a Construction General Permit.

## Slide 21: QuickPoll
Notes: Q: Is the Single Family home construction detailed here an Exempt or Regulated LDA?
Exempt
Regulated
Looking for [B] as the correct answer.
Definitely REGULATED; however, we need to discuss HOW it will be regulated.
Regulated as part of an overall or CPOD?

## Slide 22: Q: Is the waterline construction detailed here an Exempt or Regulated LDA?
| Regulated LDA | Exemption status |
Exempt
Regulated
Notes: Looking for [B] as the correct answer.
Definitely REGULATED; however, we need to discuss HOW it will be regulated.
Regulated as part of an overall or CPOD?

## Slide 23
| Regulated LDA | Exemption status |
LDA: Regulated
-or- Exempt?
Under what conditions?
ESC Plan Reqs ONLY?
CBPA Regs; locality to require ESM plan?
Common Plan of Development = CGP?
Agreement in Lieu of a Plan?
Service Connection Review
Notes: Review previous points.
Regulated or Exempt?: Regulated; with a minimum requirement of an ESC land disturbing permit. With the submittal of an overall plan with individual lots sharing infrastructure, it seems that each parcel are actually part of a larger common plan of development, Hence, Regulated and needing a Construction General Permit.
ESC Plan ONLY – No
CBPA compliance – infrastructure work is over 2,500 sqft, so YES (at least)
CPOD – infrastructure work being done for the SFD construction, so YES (optional)
Agreement – maybe for the SFD (arguable) but not for the overall plan
CGP - > 1 acre, so YES

## Slide 24: QuickPoll
Notes: Q: How should the local authority proceed with the service connection LDA? Regulate under:
ESC Program reqs. ONLY
CBPA activity; locality’s choice
CPOD; SWM plan & CGP
Agreement in Lieu
Nope, it’s still Exempt

## Slide 25: Q: How should the local Authority proceed with the service connection LDA? Regulate under:
| Regulated LDA | Exemption status |
ESC Program reqs. ONLY
CBPA activity; locality’s choice
CPOD; ESM plan & CGP
Agreement in Lieu
Nope; it's still Exempt
Notes: Looking for [C] as the correct answer.
Definitely REGULATED:
- ESC, then the other choices would be required IN ADDITION TO ESC
- Regulate as a Common Plan. Infrastructure plan will be needed at some point. This will require a full ESM plan be submitted and reviewed, as well as Construction General Permit coverage from DEQ.

## Slide 26: Bonus Chat: Single Family Dwelling
| Regulated LDA | Exemption status |
 How do we regulate the SFD then?
Notes: Now that we’ve established the disconnection is part of larger plan serving multiple lots, and is a regulated activity:
do we need to do anything about the SFD construction as the VESMP authority???
NEXT SLIDE WILL DISCUSS SINGLE FAMILY EXEMPTION STATUS AGAIN

## Slide 27: Single Family Review
| Regulated LDA | Exemption status |
 Thoughts…
Private Property
LDA < 1 acre (building plat showing 30,000 sqft)
ESC plan LDA Threshold *> 10,000 sqft
CBPA LDA Threshold * > 2,500 sqft
More stringent ordinance
* Water quantity compliance required
QP
4D
Notes: Review LDA thresholds for folks, so we get an idea of the compliance requirements
*CLICK* Thoughts.  QP: How could the local Authority approach compliance requirements from the Owner/Developer?

## Slide 28: QuickPoll
Notes: This is a CBPA locality, so LDA threshold is at 2,500sqft, and the SFD LDA is 30,000sqft which triggers ESM plan submittal, but NOT CGP requirements.
Looking for [A] in terms of the rest of the activity, but there are options to compliance…………
[A] Maybe. Could be a compliance option, if the VESMP authority (Program Administrator) considers the SFD construction part of the overall development included in the infrastructure plan. This would be up to the VESMP authority.
[B] No, NOT Exempt. This is a difference from pre-July 2024
[C] No. Water quantity requirements are always a requirement in addition to ESC plan submittal.
[D] Yes. VESMP may enter into Agreements in Lieu w/ owners of SFDs under 1 acre.
[E] Yes. SFDs under 1 acre that are not covered with an Agreement in Lieu must submit an ESM plan for erosion and stormwater compliance, but the CBPA locality may choose whether to require water quality compliance.

## Slide 29: Q: How could the local Authority approach compliance requirements from the Owner/Developer? (select all that apply)
| Regulated LDA | Exemption status |
CPOD; require CGP coverage and full ESM plan submittal
Exempt, no Authority action needed
Require ESC plan submittal only
Accept an Agreement in Lieu of a plan
Require ESM plan but no water quality component
Notes: This is a CBPA locality, so LDA threshold is at 2,500sqft, and the SFD LDA is 30,000sqft which triggers ESM plan submittal, but NOT CGP requirements.
Looking for [A] in terms of the rest of the activity, but there are options to compliance…………
[A] Maybe. Could be a compliance option, if the VESMP authority (Program Administrator) considers the SFD construction part of the overall development included in the infrastructure plan. This would be up to the VESMP authority.
[B] No, NOT Exempt. This is a difference from pre-July 2024
[C] No. Water quantity requirements are always a requirement in addition to ESC plan submittal.
[D] Yes. VESMP may enter into Agreements in Lieu w/ owners of SFDs under 1 acre.
[E] Yes. SFDs under 1 acre that are not covered with an Agreement in Lieu must submit an ESM plan for erosion and stormwater compliance, but the CBPA locality may choose whether to require water quality compliance.

## Slide 30: SFD as part of a CPOD:
| Regulated LDA | Exemption status |
 Next Step?
Approved ESC Plan
Approved SWM Plan
SWPPP developed
Construction General permit coverage by DEQ
Registration Statement submitted
THEN, local authority approval to start land disturbance
4F
Notes: QP closes: *CLICK #1* (House image moves off screen, plan remains)
As the VESMP authority, what is the approval process for this regulated land disturbing activity to start land disturbance? PA participant guide Module 4f, page 38
*CLICK #2* Step 1: Get plans through the approval process!
*CLICK #3* Step 2: Now with approved plans, a registration state can be submitted to the State for review  meaning we are in the midst of building a SWPPP
*CLICK #4* Step 3” CGP coverage is permitted by DEQ
*CLICK #5* Step 4: THEN the local authority will grant approval for land disturbance

## Slide 31: Registration Statement
| Regulated LDA | Exemption status |
Required Information - Operator
Operator/permittee Information
Offsite support activity location(s)
Site Information:
  Disturbed area, including offsite
  Downstream waterways
  TMDL, Impaired, Exceptional
Construction activity location
Other information:
  SWPPP prepared
  ESC Plan Approved
  Approved Stds. & Specs
4E
Notes: What information does an Operator need to provide on the Reg. Statement?
What should a Program Admin be looking for when reviewing a Reg. Statement?
PA participant guide Module 4e, pages 22-31, ask for feedback from these pages in the Chat Box (or from live crowd).
***Note for Program Administrators: IF this was a SF home construction over 1 acre (and not part of a CPOD) it would not require a Registration Statement

## Slide 32: Registration Statement
| Regulated LDA | Exemption status |
Once the Registration Statement information has been put into the Construction GP system, what should the VESMP Authority ensure is obtained before the Operator begins land-disturbance??
Notes: Answer to the question: NOTICE OF COVERAGE LETTER

## Slide 33: Notice of Coverage Letter
| Regulated LDA | Exemption status |
Issued by DEQ
Copy should be posted near the entrance to the construction activity
Another copy should be placed in SWPPP
Time to send the Inspector out to the site to check these requirements…
Notes: Make 3 points on screen – Copy in the PG MOD 4 P. 35-37
BUT remind PAs that a SF home construction > 1 acre would need to download and print a standard Coverage Letter for SF homes, specifically.

## Slide 34: Single Family Dwelling
| Regulated LDA | Exemption status |
Review
SF home lot – < 1 acre
SF home lot was actually part of a larger common plan of development; Not Exempt
Regulated: LDA > 1 acre, so VESMA requirements applied
Registration Statement required; entered in CGP system by Program Admin.
DEQ issued Notice of Coverage letter; required on-site & in project SWPPP
Notes: Once we have the building plat confirming the disturbance is under 1 acre, are we done? Is the situation settled?
Do we need a local E&S control LD permit? (If over 10,000 sqft, or stricter local ordinance threshold)? YES
AND, is it part of a Common Plan of Development?
- (Last Click) Next Step. Quickpoll to see what folks think we should do next….

## Slide 35
| Regulated LDA | Exemption status |
Water line plan: Edgemont Subdivision Water Lines – Grantham & Associates, Inc. (gra-ce.net)
Water line excavator: commercial-water-line-installation - Pine Enterprises
Waterline excavation pipe: https://www.paletteplumbing.com/residential-services
Overall Utility plan: https://bes-engineer.com/index.php/civil-engineering-and-surveying-for-planning-water-sanitary-storm-and-detention/
Utility Profile: 12" Water Line Plan & Profile "A" - Austin, TX | Water line … | Flickr
Farm road: https://williammorfoot.co.uk/news/farm-track-construction/
Stream erosion: https://twitter.com/doee_dc/status/1078738838883840001
Lumber: https://www.mercari.com/us/item/m96009902379/?gclsrc=aw.ds&&utm_source=google&utm_medium=cpc&utm_campaign=12877497079&utm_content=t0&adgroup=120335190446&network=g&device=c&merchant_id=126358573&product_id=m96009902379&product_id=297362935391&gclid=CjwKCAiAzrWOBhBjEiwAq85QZ5z_LZ7Gh8j5bAMGOntcz6YWAeZB0x6oQ26sAwrC56hkIykKg8r-0xoCdGEQAvD_BwE
Rolloff dumpster: https://www.dumpstermaxx.com/construction-dumpster-rentals/
Single family home: https://www.globenewswire.com/en/news-release/2021/04/16/2211843/0/en/U-S-Housing-Starts-Surge-to-15-Year-High-Arizona-Builders-Poised-to-Meet-Demand.html
Email logo: http://www.differencebetween.net/technology/difference-between-email-and-gmail/
GIS Parcel data: https://www.esri.com/about/newsroom/arcnews/douglas-county-meets-growing-demand-for-parcel-maps/
Plat of survey: https://www.cdscapes.com/reading-property-surveys.html
Gravel Road: US Federal Roadways Gravel Road Maintenance Guide 2015
Mud on Road: https://www.motorcyclelawscotland.co.uk/why-choose-us/legal-information-centre/mud-on-the-road/
VA Map: https://www.virginia.org/maps/

## Slide 36
| Regulated LDA | Exemption status |
Farm road: https://williammorfoot.co.uk/news/farm-track-construction/
Stream erosion: https://twitter.com/doee_dc/status/1078738838883840001
Lumber: https://www.mercari.com/us/item/m96009902379/?gclsrc=aw.ds&&utm_source=google&utm_medium=cpc&utm_campaign=12877497079&utm_content=t0&adgroup=120335190446&network=g&device=c&merchant_id=126358573&product_id=m96009902379&product_id=297362935391&gclid=CjwKCAiAzrWOBhBjEiwAq85QZ5z_LZ7Gh8j5bAMGOntcz6YWAeZB0x6oQ26sAwrC56hkIykKg8r-0xoCdGEQAvD_BwE
Rolloff dumpster: https://www.dumpstermaxx.com/construction-dumpster-rentals/
Single family home: https://www.globenewswire.com/en/news-release/2021/04/16/2211843/0/en/U-S-Housing-Starts-Surge-to-15-Year-High-Arizona-Builders-Poised-to-Meet-Demand.html
Email logo: http://www.differencebetween.net/technology/difference-between-email-and-gmail/
GIS Parcel data: https://www.esri.com/about/newsroom/arcnews/douglas-county-meets-growing-demand-for-parcel-maps/
Plat of survey: https://www.cdscapes.com/reading-property-surveys.html
Gravel Road: US Federal Roadways Gravel Road Maintenance Guide 2015
Mud on Road: https://www.motorcyclelawscotland.co.uk/why-choose-us/legal-information-centre/mud-on-the-road/
VA Map: https://www.virginia.org/maps/