## Slide 1: Horsepen Creek, Little Roanoke Creek, and unnamed tributary to Spencer Creek TMDL Study
A water quality study for watersheds in Charlotte County
Aerin Doughty
TMDL Coordinator
January 15, 2025

## Slide 2: Our goals for today…
Share DEQ’s water quality improvement process
  Provide information on the streams of interest
  Define Total Maximum Daily Loads (TMDL)
  Discuss the stressor identification process
  Explore next steps and opportunities for engagement
Receive community feedback – I want to hear from you!

## Slide 3: Agenda
Background and TMDL Development
  Virginia Stream Condition Index
  Impairments
  TMDL
Benthic Stressor Analysis Overview
  Monitoring/Data
  Approach
  Conclusions
Wrap-up and Next Steps by DEQ Staff
  Public Comment Period
  Engagement
  Study/Modeling/Implementation
Questions

## Slide 4: Virginia’s Water Quality Process

## Slide 5: Background: Clean Water Act
The Clean Water Act requires that all waters meet water quality standards that promote healthy water use.
To meet the goals of the Clean Water Act, Virginia established water quality standards.

## Slide 6: Virginia’s Water Quality Standards
Water quality standards protect these six designated uses:
  aquatic life
  wildlife
  fishing
  shellfish
  swimming
  drinking water

## Slide 8: Why Benthic Macroinvertebrates?
Biological Indicators
Vary in their sensitivity to or tolerance of pollution
  Known pollution tolerance values (0-10)
  Respond to changes in water quality
Widespread, found in all aquatic environments
Limited mobility; spend 1-3 years in the water as larvae or nymphs
Biological monitoring gives a longer-term picture of water quality

## Slide 9: Aquatic life impairments are visible and quantifiable.

## Slide 10: Virginia Stream Condition Index (VSCI)
Benthic macroinvertebrates are collected, sorted, and identified
Each sample produces a score that is driven primarily by the types and diversity of organisms found
Pollution sensitivity affects the score

## Slide 11: Virginia Stream Condition Index (VSCI)
VSCI scores tell us that there is an impairment but not what the pollutant is…

## Slide 13: Horsepen Creek Biomonitoring Data Station: 4AHEN004.27
Low VSCI scores are driven by % Mayflies, % Stoneflies and Caddisflies, and % Scrapers

## Slide 14: Little Roanoke Creek Stations: 4ALRO010.18, 4ALRO010.68, 4ALRO010.88
Low VSCI scores are driven by % Mayflies, % Stoneflies and Caddisflies, and % Scrapers

## Slide 15: Unnamed tributary to Spencer Creek Stations: 4AXVO000.50, 4AXVO000.60
Low VSCI scores are driven by % Mayflies, % Stoneflies and Caddisflies, and % Scrapers

## Slide 16: What is a TMDL?
A Total Maximum Daily Load (TMDL) is the maximum amount of a pollutant that a waterbody can receive and still meet water quality standards.
A TMDL includes:
  Identifying sources of pollution causing impairments
    Aquatic Life Impairment
  Modeling their path to the stream
  Determining the reductions needed from each source to meet the standard

## Slide 17: TMDL? A kind of “Pollution Diet”
Pollutant load in the stream currently
Pollutant load the stream can accept and meet WQS
TMDL Endpoint

## Slide 18: TMDL? A kind of “Pollution Diet”
Pollutant load in the stream currently
Pollutant load the stream can accept and meet WQS
TMDL Endpoint
Water pollution is described by its source. There are two source types,
Point Sources and Non-Point Sources.
Pollution from a point source comes from a direct discharge (ie. effluent discharged to river through an overflow or pipe). Pollution from a non-point source comes from indirect contributions such as stormwater runoff, wind erosion, groundwater seepage, etc.
Pollution Load is the total pollutant from both sources being transported downstream by river flows.

## Slide 19: What pollutants may be leading to aquatic life impairments in Horsepen, Little Roanoke, and the unnamed tributary to Spencer Creek?

## Slide 20: Benthic Stressor Analysis
The goal of the benthic stressor analysis is to identify the pollutant(s) responsible for causing the benthic impairment.
Analysis is done using EPA’s Causal Analysis/Diagnosis Decision Information System (CADDIS) approach.
  Identify potential causes
  Analyze lines of evidence
  Determine the probable cause(s)

## Slide 21: Available Data
Stream Name | Station | Benthic Sampling |  | Water Quality Sampling | 
 |  | Monitoring Period | Samples Collected | Monitoring Period | Samples Collected
Horsepen Creek | 4AHEN004.27 | 2009-2022 | 15 | 2009-2022 | 32
Little Roanoke Creek | 4ALRO010.18 | 2012-2022 | 13 | 2012-2022 | 44
 | 4ALRO010.68 | 2007 | 2 |  | 
 | 4ALRO010.88 | 2022 | 2 | 2022 | 3
UT Spencer Creek | 4AXVO000.50 | 2012-2022 | 18 | 2012-2022 | 12
 | 4AXVO000.60 |  |  | 2019-2020 | 17
Reference Watershed Station |  |  |  |  | 
Reedy Creek | 4ARDD002.09 | 2020-2021 | 4 | 2020-2021 | 4
7 monitoring stations
54 benthic samples collected
95 water quality sampling events
Dataset from 2007-2022, 15 years of monitoring
1 local reference stream

## Slide 22: “Stressors” Analyzed
Physical Stressors: sedimentation and physical habitat
Water Chemistry Stressors: temperature, pH, dissolved oxygen, conductivity, total dissolved solids, and dissolved ions (sodium, potassium, chloride, sulfate)
Nutrient Stressors: nitrogen and phosphorus
Dissolved Metals: calcium, magnesium, arsenic, barium, beryllium, cadmium, chromium, copper, iron, lead, manganese, thallium, nickel, silver, zinc, antimony, aluminum, and selenium
Some of these candidates have direct negative effects on aquatic life, metal toxicity for example. Other candidates are factors that are byproducts or precursors of another candidate, low dissolved oxygen levels caused by nutrient enrichments leading to eutrophication for example.

## Slide 23: Evidence Examination
8 lines of Evidence were examined
  Ex. biological effect must be observed where the potential stressor is observed
  Ex. biological measurements characteristic of one or a few specific stressors
All the evidence is scored
Future modeling will look at even more evidence to develop the total maximum daily load equation

## Slide 24: Causal Analysis/Diagnosis Decision Information System (CADDIS) approach
ALL available data
Potential Stressors
Evidence Examination
Possible Stressors
Probable Stressors
Unlikely Stressors
TMDL

## Slide 25: Draft Results
Probable Stressors
TMDL
Horsepen Creek:
Phosphorus
Possible Stressors: Sediment, Dissolved Oxygen, Physical Habitat
Little Roanoke Creek:
Sediment and Dissolved Oxygen
Possible Stressors: Phosphorus
Unnamed Tributary to Spencer Creek:
Sediment
Possible Stressors: Physical Habitat and Phosphorus

## Slide 26: Some Supporting Lines of Evidence – Phosphorus

## Slide 27: Some Supporting Lines of Evidence – Sediment

## Slide 28: Some Supporting Lines of Evidence – Dissolved Oxygen

## Slide 29: Some Supporting Lines of Evidence – Physical Habitat

## Slide 30: Community Engagement Meeting or TMDL Advisory Group?
Community Engagement Meetings
  Open to the public
  Anyone in attendance can participate & advise DEQ on TMDL development
TMDL Advisory Group (TAG)
  Set-up upon request
  Replaces community engagement meetings
  Formal panel with approved membership that advises DEQ on TMDL development
    Cross-section of stakeholders
    Members commit to attend multiple meetings
  Open to the public but non-members may only attend as observers

## Slide 31: TMDL Development: The Study Continues
Identify Point Sources
  Permitted discharges
  Construction Permits
Identify Non-point Sources
  Land Use
  Natural hydrologic properties of the area

## Slide 32: TMDL Development: The Model & Reductions
Watershed
Inputs
Computer Model
Model Outputs
Adjust
Calibration
Parameters
Match Observed Data?
No
Yes
Meet TMDL Endpoints?
Yes
Revise Pollutant Reduction
Scenarios Until We Meet
TMDL Endpoints
No
TMDL
Complete

## Slide 33: TMDL Development: The Equation of the Pollution Load
WLA
LA
MOS
TMDL
Wasteload Allocation
Permitted/Point Sources
Load Allocation
Non-point Sources
Margin of Safety
Extra load to account for uncertainty
Total Maximum Daily Load

## Slide 34: What happens next…
EPA and SWCB Approval
Completed Benthic Stressor Analysis
First Public Meeting
Final Public Meeting
Public Comment Period
Public Comment Period
January 15, 2024
30 Days
Opportunity for you to participate
TMDL Development/
Community Engagement Meetings/TAG Meetings
*****February 14th, 2025*****
https://www.deq.virginia.gov/our-programs/water/water-quality/tmdl-development/tmdls-under-development

## Slide 35: For comments: aerin.doughty@deq.virginia.gov or 901 Russell Drive Salem, VA 24153 The 30-day public comment period ends February 14th, 2025. To learn more about TMDLs, visit DEQ’s website: https://www.deq.virginia.gov/our-programs/water/water-quality/tmdl-development To view the Stressor Analysis Document: https://www.deq.virginia.gov/our-programs/water/water-quality/tmdl-development/ tmdls-under-development
Comments, Thoughts, & Questions