## Slide 1: Tidal James River, Elizabeth River, and Tidal Tributaries PCB Water Quality (TMDL) Study:
Public Meeting
Mark Richards & Paige Haley
January 26, 2021

## Slide 2: Agenda
Welcome and Introductions
  Meeting Objectives
Overview of Water Quality Planning
Background PCB Information
Water Quality Impairment of the tidal James River watershed
Overview of the tidal James River watershed PCB TMDL
Next Steps
For Technical Support call 757.518.2153

## Slide 3: Overview of Water Quality Planning

## Slide 4: Water Quality Standards
Designated Uses
  All waters are designated for recreation, aquatic life, fish consumption, and wildlife
  Other uses applied locally as applicable (shellfish [tidal], public water supply, Chesapeake Bay, etc.)
Criteria
  To protect and maintain designated uses
  Numeric or narrative
Anti-degradation
  Protects and maintains existing water quality from being degraded

## Slide 5: Continuous Planning Process
VPDES Permit Limits
Assessment
TMDLs
Implementation Plan
Water
Quality Standards
Integrated Report
EPA
Monitoring
Public
Participation
Public
Participation
For Technical Support call 757.518.2153

## Slide 6: DEQ Fish Tissue Monitoring
Monitor to assess the “Fishable” Goal of the Clean Water Act - 305(b)
Target contaminants that accumulate in tissue
    “Lipophilic” or Fat loving
      PCBs, Pesticides, etc.
    Mercury
Compare to trigger values (protect human health)
    Listed on “dirty waters” / 303(d) report if exceeds

## Slide 7: VA Water Quality Criterion –Total PCBs
Agency | Fish Tissue Threshold (ng/g or ppb) | WQC (pg/L or ppq)
VDH | 100 (Fish Consumption Advisory) | - -
DEQ | 18 (Screening Value) | 640
DEQ’s Water Quality Assessment (Integrated Report)
  VDH - Consumption Advisory = impairment
  DEQ - two or more fish samples exceed screening value at a site or two water samples exceed criterion at a site = impairment
  From: DEQ’s 2022 (Draft) Water Quality Assessment Guidance Manual

## Slide 8: Total Maximum Daily Load (TMDL)
Pollution Budget
Addresses different pollution categories
PCB TMDL - Multi-media approach
  Air, Land, Water
Existing Load
TMDL
Pollutant Load
TMDL End Point
Margin of Safety
Load Allocations (WLA + LA)
Allocated Load
Goal = Reduce existing PCB load to restore the fish consumption use
TMDL = WLA + LA + MOS
Where:
WLA = Waste Load Allocation
LA = Load Allocation
MOS = Margin of Safety
For restoration the waterbody must meet two thresholds: 1) Numeric WQC [or site specific value] and 2) fish tissue threshold

## Slide 9: The TMDL Process
Identify Problem
Source Assessment
Identify sources
Estimate source loading
Link Sources to Targets
Assess linkages
Estimate total loading capacity
TMDL Allocations
Reduce loads from point sources
Divide remaining loads among
sources
TMDL = Sum of WLA + Sum of LA + MOS
Low Level PCB
Analysis
Fish Consumption Advisory
In Process
To be Completed
To be Completed
Notes: These components are not necessarily sequential steps, but are a guide and framework for TMDL development.
(1) Problem Identification: define key factors and background information for a listed waterbody that describe the nature and impairment. This is the guiding factor in development of the TMDL.
(2) Develop Numeric Targets: measurable indicators and target values that can be used to evaluate attainment of water quality standards in the listed waterbody.
(3) Source Assessment: identify sources of loading for bacteria
(4) Link Targets and Sources: this is necessary in order to develop the TMDL since the linkage defines the cause-and-effect relationship between the pollutant sources and the in-stream pollutant response and allows for an estimation of loading capacity. This relationship can vary seasonally, especially for nonpoint sources that are highly dependent on precipitation.
(5) Load Allocations: pollutant loadings that will not exceed the loading capacity and will lead to attainment of the water quality standard can be determined based on the target/source linkage. The loadings may be distributed or allocated among the significant sources.
(6) Follow-up Monitoring: An ongoing monitoring plan should be included to determine whether the TMDL has resulted in attaining water quality standards and to support any required revisions to the TMDL.

## Slide 10: PCB Background Information
For Technical Support call 757.518.2153

## Slide 11: Background: PCBs
Biphenyl molecule (1-10 chlorine atoms)
209 distinct PCB Compounds
Regulated by DEQ as Total PCB (tPCB) = 209 compounds summed
Referred to as PCB Aroclors (Monsanto tradename) = mixture of PCB compounds
  Examples 1248, 1254, 1260
For Technical Support call 757.518.2153

## Slide 12: Background: PCBs
Legacy Contaminant
  Estimated that > 1.5 Billion lbs. manufactured in the U.S. until 1977
Characteristics
  Very stable and heat resistant
  Persistent in the environment
Common uses:
  Transformers, capacitors, hydraulic fluids, circuit breakers, PVC Products, carbonless copy paper, caulking material, paints, and more!
For Technical Support call 757.518.2153

## Slide 13: Toxics Substances Control Act (TSCA)
1976 Law regulates PCBs
  Bans the manufacture, processing, use and distribution in commerce
  Non-PCB Transformer defined as containing < 50 ppm PCB
  Inadvertent manufacture of PCBs – products up to 50 ppm allowed to leave site as long as annual average is < 25 ppm
    Unintentional by-products of manufacturing processes
50 ppm compared to DEQ’s WQC - 6.4 X 10-7 ppm (0.00000064)
For Technical Support call 757.518.2153
Notes: Banned in 1979
PCB Regulations: Part 761 in Title 40 of the Code of Federal Regulations
https://www.epa.gov/pcbs/learn-about-polychlorinated-biphenyls-pcbs
Has list of federal notices
6 Sept 2012: changes made so that PCB regs matched RCRA regs (40 CFR 262, 263, 264)
TSCA Cleanup level of 1 ppm
9VAC20-81-630: wastes containing PCBs (effective 2011)

## Slide 14: PCBs in Municipal Products
Examples of other products tested
  Pennzoil SAE5W-30
  Valvoline Full Synthetic
  Road paint
March 2015

## Slide 15: Why PCBs Continue to be an Issue
Fish impairments based on human health concerns
  Fish consumption significant exposure pathway
    Suspected carcinogen (EPA)
      International Agency on Research for Cancer (WHO) upgraded to carcinogen
    Immunotoxicity, reproduction and
    development , hepatotoxicity (liver), etc.
Persistent, bioaccumulates at a low conc. (ppq or pg/L) & biomagnifies
Confirmed on-going releases
For Technical Support call 757.518.2153

## Slide 16: Site Specific PCB Endpoint
Explore the use of a site-specific Bioaccumulation Factor (BAF) endpoints
  Considers multiple exposure pathways
    Other pathways include sediment ingestion and Biomagnification
  Used in other VA PCB TMDLs - Potomac River, Roanoke River, New River and Levisa Fork
Existing WQC only considers a single exposure pathway (through fish gills)
1) Numeric water based value and 2) fish tissue concentration must be met for successful restoration
  Narrative WQS (i.e., control of toxic substances including those that bioaccumulate)
EPA Method (EPA-822-03-030, 2003)
For Technical Support call 757.518.2153

## Slide 17: Tidal James River, Elizabeth River, and Tidal Tributaries Water Quality Impairment
For Technical Support call 757.518.2153

## Slide 18: Tidal James River Watershed
For Technical Support call 757.518.2153

## Slide 19: James and Elizabeth River Watershed PCB Impairment Timeline
1993,1998, & 2000-2001: DEQ monitors fish tissue
2002: VA Department of Health issues fish consumption advisory for numerous species
2003: DEQ performed a source investigation in the upper tidal James River
2005, 2012 & 2016: DEQ completes additional fish tissue monitoring
2009-2020: DEQ performs water and sediment monitoring for PCB water quality study; initiated meetings
https://www.alamy.com/stock-photo/striped-bass.html
http://www.vdh.virginia.gov/environmental-health/public-health-toxicology/fish-consumption-advisory

## Slide 20: Problem Identification - VDH Fish Consumption Advisory
River basin | Water-body | Section | Locality | Contam-inants | Fish species | Advisory description
James River | James River | From I-95 James River Bridge in Richmond to Hampton Roads Bridge Tunnel, including tidal portions of tributaries | Richmond City, Henrico Co., Chesterfield Co., Charles City Co., Hopewell City, Colonial Heights City, Petersburg City, Dinwiddie Co., Prince George Co., Surry Co., James City Co., New Kent Co., Isle of Wight Co., Newport News City, Suffolk City, Portsmouth City, Hampton City, Norfolk City, Chesapeake City, Virginia Beach City | PCBs | Gizzard Shad, Carp, Blue Catfish ≥32 inches, Flathead Catfish ≥32 inches Blue Catfish <32 inches, Flathead Catfish <32 inches, Channel Catfish, White Catfish, Largemouth Bass, Bluegill Sunfish, American Eel, Quillback Carpsucker, Smallmouth Bass, Creek Chub, Yellow Bullhead Catfish, White Perch, Striped Bass, Bluefish, Croaker, Spot, Blueback Herring, Hickory Shad | Do Not Eat ≤ 2 meals/month
James River | Mill Creek | Entire Creek | City of Hampton | PCBs | Gizzard Shad | ≤ 2 meals/month
James River | Southern Branch | Southern Branch, including tributaries | Portsmouth City, Chesapeake City, Norfolk City | PCBs, Dioxin | Blue Crab | Do not eat crab's hepatopancreas ("mustard"). Crab meat is ok to eat.
http://www.vdh.virginia.gov/environmental-health/public-health-toxicology/fish-consumption-advisory/
Does not apply to swimming

## Slide 21: Tidal JR Fish Specis by year
2,024.9 ng/g
VDH Threshold
DEQ’s Screening Value

## Slide 22: Arithmetic Mean of tPCB Concentrations (ng/g) for the Lower James River Consumption Advisory Species by Year (1993-2016)
Chart: Arithmetic Mean of tPCB Concentrations (ng/g) for the Lower James River Consumption Advisory Species by Year (1993-2016)
| Blue Crab | Croaker | Striped Bass | Striped Bass | Bluefish | Croaker | Spot | Striped Bass | Blue Crab | Bluefish | Croaker | Spot | Blue Crab | Croaker | Gizzard Shad | Striped Bass | Croaker | Gizzard Shad | Mummichog | Spot | Croaker | Gizzard Shad | Striped Bass | 1993 | 1994 | 1996 | 2001 | 2005 | 2012 | 2016
Mean Total PCB Concentration (ng/g) | 39.92 | 84.5 | 2379.2 | 698.4 | 797.3 | 163.6 | 191.1 | 257.1 | 7.6 | 90.3 | 32.6 | 26.6 | 19.6 | 40.65 | 127.3 | 75.8 | 7.74 | 72.46 | 22.19 | 7.32 | 2 | 130.4 | 93
VDH Threshold
Lower JR segment begins east of Hog Island Wildlife Management Area

## Slide 23: tPCB conc. for consumption advisory fish in Elizabeth River watershed
Chart: Arithmetic Mean of tPCB Concentrations (ng/g) for all Consumption Advisory Fish Species in the Elizabeth River Watershed by Year (1993-2016) and Waterbody

## Slide 24: Arithmetic Mean of tPCB Concentrations (ng/g) for Gizzard Shad in the Elizabeth River Watershed by Year (1998-2016) and Waterbody
Chart: Arithmetic Mean of tPCB Concentrations (ng/g) for Gizzard Shad in the Elizabeth River Watershed by Year (1998-2016) and Waterbody
| DC | DC | SJ | EB | BC | WB | LR | SB | DC | SJ | EB | LR | SB | DC | SJ | PC | EB | BC | WB | DC | EB | WB | 2000 | 2001 | 2005 | 2012 | 2016
Mean Total PCB Concentration (ng/g) | 635.8 | 887.1 | 552.7 | 364.4 | 504.1 | 299.4 | 391.8 | 490.1 | 441.8 | 404.5 | 523.8 | 272.1 | 139.6 | 380.9358 | 631.1 | 133.7934 | 299.04 | 401 | 117.68 | 423.7153 | 791.6105 | 230.2

## Slide 25: Arithmetic Mean of tPCB Concentrations (ng/g) for Gizzard Shad in the Elizabeth River Watershed by Year (1998-2016) and Waterbody
Chart: Arithmetic Mean of tPCB Concentrations (ng/g) for the Mummichog in the Elizabeth River Watershed by Year (1998-2016) and Waterbody
| SB | DC | DC | SB | DC | SJ | EB | WB | LF | SB | DC | SJ | PC | EB | BC | WB | ER | LR | PC | BC | WB | 1998 | 2000 | 2005 | 2012 | 2016
Mean Total PCB Concentration (ng/g) | 25.6 | 258.8 | 273 | 92.9 | 235 | 105.5 | 117.2 | 69.3 | 81.7 | 43.8 | 76.8637 | 35.5 | 84.21 | 43.9 | 43 | 28.34 | 76.47 | 148.5 | 91.2949 | 50.13 | 30.35

## Slide 26: DEQ TMDL Sampling Approach
Source identification
TMDL model support
    Calibration/validation
2009-2012, 2016, 2020
Water column, sediment
    Water column grab samples: High and Base Flow (n >260)
    Sediment samples as needed

## Slide 27: Graph showing water data
Chart: Arithmetic Mean of tPCB Concentrations (pg/L) in Water Samples Collected During Dry and Wet Weather from the James River Mainstem (2009-2016)
| 2-JMS110.3 | 2-JMS087.01 | 2-JMS074.44 | 2-JMS069.08 | 2-JMS066.88 | 2-JMS057.69 | 2-JMS050.57 | 2-JMS042.92 | 2-JMS032.59 | 2-JMS021.04 | 2-JMS013.10 | 2-JMS006.68 | 2-JMS000.50
DW | 556.4 | 1412.7 | 211.8 | 429.4 | 254.4 | 666 | 451.5
WW | 406.59 | 671.2 | 588.13 | 596.3
NA | 282.8 | 634 | 448.2 | 668.7 | 559.18 | 392.8 | 323.2 | 342.8 | 182.06
Upper JR

## Slide 28: Arithmetic Mean of tPCB Concentrations (pg/L) in Water Samples Collected During Dry and Wet Weather from the Elizabeth River Watershed (2009-2020)
Chart: Arithmetic Mean of tPCB Concentrations (pg/L) in Water Samples Collected During Dry and Wet Weather from the Elizabeth River Watershed (2009-2020)
| 2-SBE008.40 | 2-SBE006.26 | 2-SBE001.53 | 2-SBE000.57 | 2-EBE008.25 | 2-EBE004.96 | 2-EBE000.40 | 2CNWB001.70 | 2-WBE006.18 | 2-WBE004.44 | 2-WBE002.11 | 2-ELI004.79 | 2-ELI003.52 | 2-ELI002.00 | 2-ELI000.68
DW | 391.07 | 523.2 | 876.6 | 522.4 | 0 | 1855.4 | 475.9 | 0 | 265.2 | 348 | 238.4 | 249.9 | 167.35 | 214.67
WW | 30434 | 41211 | 51372 | 1795 | 1790.93 | 63750 | 34327 | 446.9 | 579.8 | 643 | 905.7 | 510.4 | 427.1 | 437.75 | 366.09
30,434
34,327

## Slide 29: Arithmetic Mean of tPCB Concentrations (pg/L) in Water Samples Collected During Dry and Wet Weather from Tributaries in the Elizabeth River Watershed (2009-2020)
Chart: Arithmetic Mean of tPCB Concentrations (pg/L) in Water Samples Collected During Dry and Wet Weather from Tributaries in the Elizabeth River Watershed (2009-2020)
| 5BAAC007.85 | 2CBLM001.45 | 2-DEC000.58 | 2-STJ002.00 | 2-STJ000.81 | 2-PAR000.77 | 2-BRO001.35 | 2-IND000.98 | 2-LAF005.01 | 2-LAF001.15
DW | 681.8 | 972.3 | 1212.7 | 986.7 | 1158 | 2512.75 | 236
WW | 323.56 | 313.37 | 71499 | 1940.04 | 55907 | 5350.9 | 2506.15 | 2173.8 | 16294.77 | 0
16,294
5,351
55,907
DEQ’s WQC

## Slide 30: Monthly PCB concentrations at RM 4.79
Chart: Monthly Total PCB Concentrations (pg/L) in Water Samples Collected at Elizabeth River Station (RM 4.79) During 2011
| 40645 | 40673 | 40708 | 40736 | 40764 | 40799 | 40827 | 40855 | 40889 | 40918 | 40953 | 40981
Surface | 748.1 | 314.7 | 637.8 | 1094.9 | 1688.4 | 1239.25 | 687.9 | 270 | 221.6 | 84.2 | 267.3 | 251
Bottom | 513.7 | 393.3 | 1528.3 | 1684.5 | 1510.8 | 3659.35 | 780.2 | 348.4 | 290 | 63.7 | 365.2 | 969.4

## Slide 31: Graph os sediment in the James River
L-JR = Lower James River
Skif = Skiffes Creek
War = Warick River
Pag = Pagan River
Chuck = Chuckatuck Creek
Nan = Nansemond Creek
Mill = Mill Creek
Will = Willoughby Bay
For Technical Support call 757.518.2153

## Slide 32: Mean Total PCB Concentrations (ng/g) Detected in Sediment Collected in the Elizabeth River Watershed During 2001-2016
Chart: Arithmetic Mean Total PCB Concentrations (ng/g) Detected in Sediment Collected in the Elizabeth River Watershed During 2001-2016
| Mainstem | DC | SJ | PC | Mainstem | BC | Mainstem | Mainstem | LF | Southern Branch | Eastern Branch | Western Branch | ER Mainstem
 | 36.34 | 119.7 | 54.5 | 62.6 | 34.36 | 173 | 11.6 | 0.65 | 24
SB = Southern Branch ER
DC = Deep Creek
SJ = St. Juliens Creek
PC = Paradise Creek
EB = Eastern Branch ER
BC = Broad Creek
WB = Western Branch ER
ER = Mainstem ER
LR = Lafayette River
n = 8
n = 2
n = 4

## Slide 33: Tidal James River, Elizabeth River, and Tidal Tributaries PCB TMDL

## Slide 34: Sources considered in PCB TMDL
Non-point source
PCB Contaminated
Sediment
Wet Deposition
Dry Deposition
Air Emissions
Non-point source
Runoff
2
Contaminated Sites
1
6
5
MS4 SW Runoff
4
Point Source Effluent
Runoff
3
PCB
PCB
PCB
PCB
PCB
Requires Multi-Media Approach
(land, water, air)

## Slide 35: TMDL Source Category – Point Sources
VPDES Permitted facilities
  Municipal WWTP
  Industrial sources
    Selected based on Standard Industrial Classification (SIC)
      Individual Industrial Facilities
      Industrial Storm Water General Permitted Facilities
  Municipal Separate Storm Sewer System (MS4)
  Combined Sewer Overflow (CSO)
    Richmond

## Slide 36: TMDL Source Category – Point Sources
Upper and Middle Tidal James River (Piedmont Region) |  |  | 
Facility Type | # Permitted Facilities | Projected PCB Baseline Load (g/yr) | Projected WLA (g/yr)
Municipality | 11 | TBD | TBD
Industrial IP | 22 | TBD | TBD
Indus. SW GP | 112 | TBD | TBD
Lower James River and Elizabeth River Watershed (Tidewater Region) |  |  | 
Facility Type | # Permitted Facilities | Projected PCB Baseline Load (g/yr) | Projected WLA (g/yr)
Municipality | 6 | TBD | TBD
Industrial IP | 44 | TBD | TBD
Indus. SW GP | 127 | TBD | TBD
TBD = To Be Determined

## Slide 37: TMDL Source Category – MS4s
Upper and Middle Tidal James River (Piedmont Region) |  | 
MS4s | Projected PCB Baseline Load (g/yr) | Projected WLA (g/yr)
2 (Phase I – Large) 13 (Phase II - Small) VDOT | TBD | TBD
Lower James River and Elizabeth River Watershed (Tidewater Region) |  | 
MS4s | Projected PCB Baseline Load (g/yr) | Projected WLA (g/yr)
6 (Phase I – Large) 17 (Phase II – Small) VDOT | TBD | TBD
For Technical Support call 757.518.2153

## Slide 38: TMDL Source Category - Contaminated Sites
TSCA (PCB Clean-up Sites)
RCRA Corrective Action Facilities
CERCLA
Voluntary Remediation Sites
Landfills
Rail Yards/Spurs
Miscellaneous spill sites
  Pollution Response (PREP)
Electric Utility Transformer Pads
https://commons.wikimedia.org/w/index.php?curid=6092689
https://commons.wikimedia.org/w/index.php?curid=17503186

## Slide 39: TMDL Source Categories
Atmospheric Deposition (example)
Contaminated Sediment
Wet = 4.5 – 12% of total
Modes of Deposition
Rodenburg (Totten), L. A. et al., 2007. Rutgers University
For Technical Support call 757.518.2153

## Slide 40: Implementation Process
Implementation Process
Point sources
WLA---- PMP
Nonpoint sources
Source “Fingerprinting”
Deliberate Monitoring
Investigation
of Hotspots
Detect “uncharacterized sources”
Funding

## Slide 41: VPDES Point Sources Pollutant Minimization Plan
If existing (baseline) condition > WLA
Pollutant Minimization Plan
Submitted and Approved
Backtrack/Source ID
Re-evaluate baseline load
Remediation
/BMPs
Adaptive Implementation

## Slide 42: TMDL - Contaminated Sites
RCRA Corrective Action, TSCA, CERCLA
Clean-up standards for land based contaminated sites have no relationship to PCB water quality criterion
  The PCB clean-up level of 1 mg/kg is not adequate to protect the fish consumption use
What about PCB contaminated drainage that leaves the site?
  Contamination occurs when stormwater comes into contact with PCB contaminated soils (< 1 mg/kg) and migrates off-site (e.g., MS4, direct drainage to waterbody, etc.)
For Technical Support call 757.518.2153

## Slide 43: Point Source/Nonpoint Source: “Fingerprinting”
Objective: To identify a specific pattern or “fingerprint” of congeners that could be indicative of a pollution source
1. # of fingerprints in the system
2. Chemical composition in each fingerprint
3. contribution of each fingerprint in each sample

## Slide 44: Timeline - Tidal James & Elizabeth Rivers PCB TMDL Development

## Slide 45: Next Steps
Public Comment Period
  January 27th – February 26th
  Send Comments to:
  Paige Haley
  5636 Southern Blvd
  Virginia Beach, VA 23462
  Mary.Haley@deq.virginia.gov
DEQ will hold two Technical Advisory Committee meetings
  March 25th – Focus will be on areas of the Upper and Middle Tidal James River
    If interested in participating as a member, Contact Jennifer.Rogers@deq.virginia.gov
  March 30th - Focus will be on the Lower James and Elizabeth Rivers
    If interested in participating as a member, Contact Mary.Haley@deq.virginia.gov
Mark.Richards@deq.virginia.gov
Mary.Haley@deq.virginia.gov
For Technical Support call 757.518.2153

## Slide 46: Extra Slides

## Slide 47: VDH Threshold
In 2012 increased fish tissue PCB threshold from 50 ppb to 100 ppb
  Designed to protect public health when contamination has been identified.
  Risk Assessment calc. designed for known contamination in a finite geographical area (e.g., Superfund site).
VDH Changes -
- Increased body weight from 70 kg to 80 kg (176 lbs)
Changed life expectancy inc. from 70 yrs to 78 yrs & from 30 yrs
to 32 yrs a person would live in the same residence
- Decreased from four meals/month to two
Note: VDH is not required to go through administrative regulatory process to change threshold(s)

## Slide 48: VA Water Quality Criterion
VA PCB criterion based on EPA guidelines
Fish Screening Value basis of criterion
  Water concentration translated using a Bioconcentration Factor (BCF)
    Lab derived translator developed in the early 80’s
    Assumes fish only obtain PCBs through gills from the water column (ratio of PCB conc. in fish to that in water)
a
( = 2 meals/month)
Update: 80 kg (176)
Update: 22 g/d (1.5 lbs)