## Slide 1: PC/Laptop View
Android
Minimize the control panel
or maximize the control panel
Raise or lower your hand 
Mobile Devices View
Select audio method
*Phone call provides better quality audio
Enter questions then click send 
Enter Questions 
Raise  Lower Hand
 Click 3 dots to open Audio Options
iPhone
Raise  Lower Hand
Enter  Questions
Audio Options 
Mountain Run TMDL Public Meeting
For technical support 703-583-3906

## Slide 2: Mountain Run PCB Study:
First Public TMDL Meeting
Mark Richards & Rebecca Shoemaker
January 13, 2021
For technical support 703-583-3906

## Slide 3: Agenda
Welcome and Introductions
  Meeting Objectives
Overview of Water Quality Planning
PCB Background Information
Water Quality Impairment of Mountain Run
Overview of the Mountain Run PCB TMDL
Next Steps
Photo: October Greenfield, Friends of the Rappahannock

## Slide 4: Overview of Water Quality Planning

## Slide 5: Water Quality Standards
Designated Uses
  All waters are designated for recreation, aquatic life, fish consumption, and wildlife
  Other uses applied locally as applicable (shellfish [tidal], public water supply, Chesapeake Bay, etc.)
Criteria
  To protect and maintain designated uses
  Numeric or narrative
Anti-degradation
  Protects and maintains existing water quality from being degraded

## Slide 6: Continuous Planning Process
VPDES Permit Limits
Assessment
TMDLs
Implementation Plan
Water
Quality Standards
Integrated Report
EPA
Monitoring
Public
Participation
Public
Participation

## Slide 7: DEQ Fish Tissue Monitoring
Monitor to assess the “Fishable” Goal of the Clean Water Act - 305(b)
Target lipophilic or “fat loving” contaminants that accumulate in tissue
    PCBs, Pesticides, etc.
Compare to trigger values (protect human health)
    Listed on “dirty waters” report if exceeds - 303(d)

## Slide 8: VA Water Quality Criterion – Total PCBs
Agency | Fish Tissue Threshold (ppb) | WQC (pg/L)
VDH | 100 (Fish Consumption Advisory) | - -
DEQ | 18 (Screening Value) | 640
DEQ’s Water Quality Assessment (Integrated Report)
  VDH: Consumption Advisory = impairment
  DEQ: If two or more fish samples exceed screening value at a site or two water samples exceed criterion at a site = impairment
  From: DEQ’s 2020 Water Quality Assessment Guidance Manual

## Slide 9: Total Maximum Daily Load (TMDL)
Pollution Budget
Addresses different pollution categories
PCB TMDL - Multi-media approach
  Air, Land, Water
Existing Load
TMDL
Pollutant Load
TMDL End Point
Margin of Safety
Load Allocations (WLA + LA)
Allocated Load
Goal = Reduce existing PCB load to restore the fish consumption use
TMDL = WLA + LA + MOS
Where:
WLA = Waste Load Allocation
LA = Load Allocation
MOS = Margin of Safety
To be restored the waterbody must meet two thresholds: 1) Numeric WQC [or site specific value] and 2) fish tissue threshold

## Slide 10: The TMDL Process
Identify Problem
Source Assessment
Identify sources
Estimate source loading
Link Sources to Targets
Assess linkages
Estimate total loading capacity
TMDL Allocations
Reduce loads from point sources
Divide remaining loads among
sources
TMDL = Sum of WLA + Sum of LA + MOS
Low Level PCB
Analysis
Fish Consumption Advisory
In Process
To be Completed
To be Completed
Notes: These components are not necessarily sequential steps, but are a guide and framework for TMDL development.
(1) Problem Identification: define key factors and background information for a listed waterbody that describe the nature and impairment. This is the guiding factor in development of the TMDL.
(2) Develop Numeric Targets: measurable indicators and target values that can be used to evaluate attainment of water quality standards in the listed waterbody.
(3) Source Assessment: identify sources of loading for bacteria
(4) Link Targets and Sources: this is necessary in order to develop the TMDL since the linkage defines the cause-and-effect relationship between the pollutant sources and the in-stream pollutant response and allows for an estimation of loading capacity. This relationship can vary seasonally, especially for nonpoint sources that are highly dependent on precipitation.
(5) Load Allocations: pollutant loadings that will not exceed the loading capacity and will lead to attainment of the water quality standard can be determined based on the target/source linkage. The loadings may be distributed or allocated among the significant sources.
(6) Follow-up Monitoring: An ongoing monitoring plan should be included to determine whether the TMDL has resulted in attaining water quality standards and to support any required revisions to the TMDL.

## Slide 11: PCB Background Information

## Slide 12: Background: PCBs
Biphenyl molecule (1-10 chlorine atoms)
209 distinct PCB Compounds
Regulated by DEQ as Total PCB (tPCB) = 209 compounds summed
Referred to as PCB Aroclors (Monsanto tradename) = mixture of PCB compounds
  Examples 1248, 1254, 1260

## Slide 13: Background: PCBs
Legacy Contaminant
  Estimated that > 1.5 Billion lbs. manufactured in the U.S. until 1977
Characteristics
  Very stable and heat resistant
  Persistent in the environment
Common uses:
  Transformers, capacitors, hydraulic fluids, circuit breakers, PVC Products, carbonless copy paper, caulking material, paints, and more!

## Slide 14: Toxics Substances Control Act (TSCA)
1976 Law regulates PCBs
  Bans the manufacture, processing, use and distribution in commerce
  Non-PCB Transformer defined as containing < 50 ppm PCB
  Inadvertent manufacture of PCBs – products up to 50 ppm allowed to leave site as long as annual average is < 25 ppm
    Unintentional by-products of manufacturing processes
50 ppm compared to DEQ’s WQC - 6.4 X 10-7 ppm (0.00000064)
Notes: Banned in 1979
PCB Regulations: Part 761 in Title 40 of the Code of Federal Regulations
https://www.epa.gov/pcbs/learn-about-polychlorinated-biphenyls-pcbs
Has list of federal notices
6 Sept 2012: changes made so that PCB regs matched RCRA regs (40 CFR 262, 263, 264)
TSCA Cleanup level of 1 ppm
9VAC20-81-630: wastes containing PCBs (effective 2011)

## Slide 15: PCBs in Municipal Products
Examples of other products tested
  Pennzoil SAE5W-30
  Valvoline Full Synthetic
  Road paint
March 2015

## Slide 16: Why PCBs Continue to be an Issue
Fish impairments based on human health concerns
  Fish consumption significant exposure pathway
    Suspected carcinogen (EPA)
      Recognized as a carcinogen by the International Agency on Research for Cancer (IARC)
    Immunotoxicity, reproduction and
    development, hepatotoxicity (liver), etc.
Persistent, bioaccumulates at a low conc. (pg/L) & biomagnifies
Confirmed on-going releases

## Slide 17: Site Specific PCB Endpoint
Numeric water based value and fish tissue concentration must be met for successful restoration
  Narrative WQS (i.e., control of toxic substances including those that bioaccumulate)
Existing WQC only considers a single exposure pathway for PCBs (through fish gills)
  Other pathways include sediment ingestion and Biomagnification
Explore the use of a site specific Bioaccumulation Factor (BAF) for multiple exposure pathways
  Used in other VA PCB TMDLs - Potomac River, Roanoke River, New River and Levisa Fork
EPA Method (EPA-822-03-030, 2003)

## Slide 18: Water Quality Impairment in Mountain Run

## Slide 19: Mountain Run Watershed

## Slide 20: Mountain Run PCB Impairment Timeline
1999 & 2001: DEQ monitors fish tissue
2004: VA Department of Health issues fish consumption advisory for the American Eel (≤ 2 meals/month)
2006: 19.9-mile segment placed on VA’s impaired waters list
2006 & 2013: DEQ completes additional fish tissue monitoring
2013-2018: DEQ completes water and sediment monitoring to prepare for PCB study
2020: Impaired segment increased to 24.5 - miles
Photo: https://www.google.com/maps/place/Yowell+Meadow+Park/@38.4756743,-77.9990059
Photo: https://www.cfr.msstate.edu/wildlife/fisheries/pdf/AmericanEel.pdf

## Slide 21: Problem Identification VDH Fish Consumption Advisory
http://www.vdh.virginia.gov/environmental-health/public-health-toxicology/fish-consumption-advisory/
River basin | Waterbody | Section | Locality | Contaminants | Fish species | Advisory description
Rappahannock | Mountain Run | From rt. 15/29 bridge 19 miles to confluence with Rappahannock River | Culpeper | PCBs | American Eel | ≤ 2 meals/month
Does not affect swimming
Photo: Rick Browder, VADEQ

## Slide 22: Arithmetic Mean tPCB Concentrations (ng/g) for Mountain Run Fish Tissue by Species, Year (1999-2013) and Rivermile
Chart: Arithmetic Mean of tPCB Concentrations (ng/g) for Mountain Run Fish Tissue by Species, Year (1999-2013) and Rivermile
| American Eel | Bullhead Catfish | Fallfish | Redbreast Sunfish | Redhorse Sucker | Fallfish | Redbreast Sunfish | White Sucker | American Eel | Fallfish | Redbreast Sunfish | Rock Bass | Smallmouth Bass | Redbreast Sunfish | White Sucker | American Eel | Redbreast Sunfish | Yellow Bullhead Catfish | American Eel | White Sucker | Yellow Bullhead Catfish | American Eel | Sunfish species | Yellow Bullhead Catfish | American Eel | Green Sunfish | Yellow Bullhead Catfish | American Eel | Redbreast Sunfish | Sunfish species | Yellow Bullhead Catfish | American Eel | Green Sunfish | Redbreast Sunfish | Yellow Bullhead Catfish | 14.88 | 14.33 | 5.79 | 22.21 | 5.79 | 22.21 | 14.33 | Jonas Run | Flat Run | 5.79 | 0.59 | 1999 | 2001 | 2006 | 2013
Total PCB Concentration (ng/g) | 269.384 | 17.3174 | 15.7557 | 4.4671 | 2.9788 | 25.5066 | 20.5931 | 29.3152 | 202.2528 | 16.3918 | 12.7573 | 12.8605 | 20.9242 | 5.0973 | 0 | 184.01 | 8.37 | 33.2 | 149.6757 | 21.6524 | 20.13 | 254.73 | 22.2681 | 39.929 | 70.8 | 0 | 29.07 | 191.5512 | 7.6428 | 5.1471 | 22.7527 | 185.05 | 4.2489 | 6.5122 | 19.0551

## Slide 23: Arithmetic Mean of tPCB Concentrations in Mountain Run Fish
Chart: Arithmetic Mean of tPCB Concentrations (ng/g) for Mountain Run Fish Tissue by Species, Year (2006 - 2013) and Rivermile
| Redbreast Sunfish | White Sucker | American Eel | Redbreast Sunfish | Yellow Bullhead Catfish | American Eel | White Sucker | Yellow Bullhead Catfish | American Eel | Sunfish species | Yellow Bullhead Catfish | American Eel | Green Sunfish | Yellow Bullhead Catfish | American Eel | Redbreast Sunfish | Sunfish species | Yellow Bullhead Catfish | American Eel | Green Sunfish | Redbreast Sunfish | Yellow Bullhead Catfish | 22.21 | 5.79 | 22.21 | 14.33 | Jonas Run | Flat Run | 5.79 | 0.59 | 2006 | 2013
Total PCB Concentration (ng/g) | 5.0973 | 0 | 184.01 | 8.37 | 33.2 | 149.6757 | 21.6524 | 20.13 | 254.73 | 22.2681 | 39.929 | 70.8 | 0 | 29.07 | 191.5512 | 7.6428 | 5.1471 | 22.7527 | 185.05 | 4.2489 | 6.5122 | 19.0551
DEQ Screening Value

## Slide 24: DEQ TMDL Sampling Approach 2013 – 2015, 2018
Source identification
TMDL model support
    Calibration/validation
2013 – 2018 water column, sediment
    Water column grab samples: High and Base Flow (n = 63)
    Sediment samples as needed

## Slide 25: Water Column Arithmetic Mean Total PCB (tPCB) Concentrations (pg/L) by River Mile for Mountain Run (2013-2018)
Chart: Water Column Arithmetic Mean Total PCB (tPCB) Concentrations (pg/L) by River Mile for Mountain Run (2013-2018)
| 23.88 | 22.49 | 22.20 | 22.01 | 21.75 | 21.11 | 19.75 | 14.88 | 10.98 | 05.79 | 00.59
DW | 111.5 | 325.83 | 437.02 | 397.6 | 452.08 | 496.6 | 350.67 | 612.3 | 1962.12 | 381.3 | 402.1
WW | 89.4 | 1718.32 | 355.92 | 2261.4 | 4586.8 | 1618.31 | 1536.4 | 2680.68 | 1691.2 | 1933.9
DEQ’s WQC

## Slide 26: Water Column PCB Mean Concentration by Rivermile for Mountain Run
Unnamed Trib. (Spring St)
Balds Run
Hidens Branch
Jonas Run
Flat Run
DEQ’s WQC
Unnamed Trib. (Yancey St)

## Slide 27: Arithmetic Mean of Total PCB (pg/L) Water Concentrations in Mountain Run During Wet and Dry Flow Conditions
Chart: Arithmetic Mean of Total PCB (pg/L) Water Concentrations in Mountain Run During Wet and Dry Flow Conditions
| Dry Weather | Wet Weather
Lake Pelham Spillway Result Excluded | 581.762 | 2042.5478
WQS | 640
Mainstem Site Location (Rivermile) | Location Description | Sample Size (n) | Percent (%) Exceedence
23.88 | Spillway Below Lake Pelham | 4 | 0
22.49 | Rt 522 | 2 | 50
22.2 | Upstream of Old Brandy Rd | 2 | 0
22.01 | Old Brandy Rd | 5 | 40
21.75 | Upstream of RR Tracks | 1 | 0
21.11 | Rt 699 | 4 | 50
19.75 | Rt 29 (near By-pass) | 2 | 50
14.88 | Rt 633 (Stevensburg Rd) | 8 | 38
10.98 | Rt 669 | 2 | 100
5.79 | Rt 672 (Stones Mill Rd) | 7 | 29
0.59 | Rt 620 (Edward Shops Rd) | 6 | 17

## Slide 28: Total PCBs - Sediment
Chart: Total PCB (pg/g) Concentrations Detected in Sediment from Mountain Run and Tributaries
| 3-MTN024.05 | 3-XIH000.06 | 3-BLS000.08 | 3-HID000.22 | 3-MTN022.01 | 3-XEH000.10 | 3-XEH000.10 | 3-MTN014.88 | 3-MTN000.59
 | 1769.28 | 63145.02 | 515.49 | 7934.48 | 11456.57 | 796.13 | 691.74 | 27730.25 | 23301.52
Sediment Site Location (Rivermile) | Location Description
Lake Pelham (24.05) | Lake Pelham above Spillway
UT to Mtn Run (0.06) | End of Spring Street
Balds Run (0.08) | Colonel Jamerson Rd
Hidens Branch (0.22) | Rt 29 (Business)
Mountain Run (22.01) | Old Brandy Rd
UT to Mtn Run (0.10) | Rt. 667 (Nalles Mill Rd)
Mountain Run (14.88) | Rt 633 (Stevensburg Rd)
Mountain Run (0.59) | Rt 620 (Edward Shops Rd)

## Slide 29: Mountain Run PCB TMDL

## Slide 30: Sources considered in PCB TMDL
Non-point source
PCB Contaminated
Sediment
Wet Deposition
Dry Deposition
Air Emissions
Non-point source
Runoff
2
Contaminated Sites
1
6
5
MS4 SW Runoff
4
Point Source Effluent
Runoff
3
PCB
PCB
PCB
PCB
PCB
Requires Multi-Media Approach
(land, water, air)

## Slide 31: TMDL Source Category – Point Sources
VPDES Permitted facilities
  Municipal WWTP
  Industrial sources
    Selected based on Standard Industrial Classification (SIC)
      Individual Industrial Facilities
      Industrial Storm Water General Permitted Facilities
  Municipal Separate Storm Sewer System (MS4)

## Slide 32: TMDL Source Category - VPDES Permitted Facilities
Facility Type | PCB Impaired Waterbody | Facility Name | Permit ID
Municipal WWTP |  |  | 
 | Mountain Run | Town of Culpeper WWTP | VA061590
Industrial Stormwater |  |  | 
 | Mountain Run. UT | TE Connectivity - Culpeper Plant | VAR050855
 | Mountain Run. UT | Bingham and Taylor Corp | VAR050900
 | Mountain Run. UT | Culpeper Municipal Power Plant | VAR051573
 | Mountain Run | Wise Services and Recycling LLC | VAR051878
 | Jonas Run, UT | Culpeper Recycling | VAR051928
 | Mountain Run | Culpeper Towing and Salvage Incorporated | VAR051952
 | Jonas Run, UT | AMRF Incorporated | VAR052293
Industrial Individual Permit |  |  | 
 |  | Not Applicable | 

## Slide 33: TMDL Source Category - Contaminated Sites
TSCA (PCB Clean-up Sites)
RCRA Corrective Action Facilities*, CERCLA
  Former Manufacturing Facilities (EPA Emergency Response)
Voluntary Remediation Sites*
Landfills
Rail Yards/Spurs*
Miscellaneous spill sites*
Electric Utility Transformer Pads*

## Slide 34: Railyards/Railway Spurs & Electrical Substations

## Slide 35: TMDL Source Categories
Atmospheric Deposition (example)
Contaminated Sediment
Wet = 4.5 – 12% of total
Modes of Deposition
Rodenburg (Totten), L. A. et al., 2007. Rutgers University
Chart: Sediment tPCB (pg/g) Concentrations Detected in Mountain Run and Tributaries
| 3-MTN024.05 | 3-XIH000.06 | 3-BLS000.08 | 3-HID000.22 | 3-MTN022.01 | 3-XEH000.10 | 3-XEH000.10 | 3-MTN014.88 | 3-MTN000.59
 | 1769.28 | 63145.02 | 515.49 | 7934.48 | 11456.57 | 796.13 | 691.74 | 27730.25 | 23301.52
For technical support 703-583-3906

## Slide 36: Mountain Run PCB TMDL PCB Fate and Transport Modeling

## Slide 37: Implementation Process
Implementation Process
Point sources
WLA---- PMP
Nonpoint sources
Source “Fingerprinting”
Deliberate Monitoring
Investigation
of Hotspots
Detect “uncharacterized sources”
Funding

## Slide 38: VPDES Point Sources Pollutant Minimization Plan
If existing (baseline) condition > WLA
Pollutant Minimization Plan
Submitted and Approved
Backtrack/Source ID
Re-evaluate baseline load
Remediation
/BMPs
Adaptive Implementation

## Slide 39: Point Source/Nonpoint Source: “Fingerprinting”
Objective: To identify a specific pattern or “fingerprint” of congeners that could be indicative of a pollution source
1. # of fingerprints in the system
2. Chemical composition in each fingerprint
3. contribution of each fingerprint in each sample

## Slide 40: Mountain Run PCB TMDL Project Timeline

## Slide 41: Next Steps
Public Comment Period
  January 14, 2021 – February 16, 2021
  Written comments may be sent to:
  Rebecca Shoemaker
  Northern Regional Office 13901 Crown Court, Woodbridge, VA 22193
  Rebecca.Shoemaker@deq.Virginia.gov
Technical Advisory Committee
  1-2 more meetings
  To participate please provide:
    Name, address, phone #, email address, organization (if applicable) with comments
Final public meeting (July 2021)
Mark.Richards@deq.virginia.gov
Rebecca.Shoemaker@deq.virginia.gov

## Slide 42: Extra Slides

## Slide 43: VDH Threshold
In 2012 increased fish tissue PCB threshold from 50 ppb to 100 ppb
  Designed to protect public health when contamination has been identified.
  Risk Assessment calc. designed for known contamination in a finite geographical area (e.g., Superfund site).
VDH Changes -
- Increased body weight from 70 kg to 80 kg (176 lbs)
Changed life expectancy inc. from 70 yrs to 78 yrs & from 30 yrs
to 32 yrs a person would live in the same residence
- Decreased from four meals/month to two
Note: VDH is not required to go through administrative regulatory process to change threshold(s)