## Slide 1: Tidal James River, Elizabeth River, and Tidal Tributaries PCB Study Area
Welcome! Please enter your name and affiliation in the chat box
For Technical Support call 757.518.2153

## Slide 2: Getting Familiar with GoToMeeting
For Technical Support call 757.518.2153

## Slide 3: Introductions
Mark Richards
DEQ Central Office
Dr. Jian Shen
Res. Prof. of Marine Science
Jen Rogers
Piedmont Regional Office
Paige Haley
Tidewater Regional Office
For Technical Support call Kristie Britt at 757.518.2153
Notes: Intro Myself
Jen P, planning Team Lead at Piedmont and is serving as technical support for this meeting
Rob Breeding from CO on questions
Warren Smigo and Mike Shaver- our Piedmont Regional Biologists- they are the ones out collecting bugs and providing tons of data for the study. They are on the call tonight to help with questions as they are the experts when it comes to all things biology- They also provided many of the photos for this presentation
We also are teaming with Katie Shoemaker at Wetland Studies and Solutions, Inc and Dr. Robert Brandt from JMU who are the contractors working on this project.
Also want to acknowledge Matt Carter, Garth Jenkins and Andrew Kirk on the water monitoring crew who help collect lots of data for use in this project

## Slide 4: Tidal James River, Elizabeth River, and Tidal Tributaries PCB Water Quality (TMDL) Study:
Technical Advisory Subcommittee Meeting (Tidewater Regional Office)
Mark Richards & Paige Haley
March 30, 2021

## Slide 5: Meeting Agenda
Meeting objective and Technical Advisory Committee’s Role
TMDL Development Process
Overview of the TMDL Sources
PCB Fate and Transport Model - VIMS
Point Source Load Calculations
TMDL Endpoint
Source: James River Association
For Technical Support call 757.518.2153

## Slide 6: Meeting Objective and Technical Advisory Subcommittee Role
For Technical Support call 757.518.2153

## Slide 7: Role of Technical Advisory Subcommittee Members
To play an advisory role on technical aspects of the TMDL to:
  Keep the TMDL:
    Realistic
    Reasonable
    Reflective of local conditions
Examples of things TAC members have influence over:
  Model assumptions (hydrology condition used for TMDL)
  Identification of missing sources
  TMDL site-specific endpoint concentrations
  Allocations of the TMDL to the different sources
For Technical Support call 757.518.2153
Notes: RECORD

## Slide 8: Technical Advisory Subcommittee
Due to spatial size of watershed, the Technical Advisory Committee is split into two Subcommittees
  Piedmont Regional area (meeting March 25th)
  Tidewater Regional area (meeting March 30th)
If a decision is made at one of the tidal James River Subcommittee meetings, a follow-up TAC meeting will be held to ensure collective awareness.
Every effort will be made to keep the meetings consistent.
For Technical Support call 757.518.2153

## Slide 9: Overview of TMDL Development Process
For Technical Support call 757.518.2153

## Slide 10: Continuous Planning Process
VPDES Permit Limits
Assessment
TMDLs
Implementation Plan
Water
Quality Standards
Integrated Report
EPA
Monitoring
Public
Participation
Public
Participation
For Technical Support call 757.518.2153

## Slide 11: VA Water Quality Criterion –Total PCBs
Agency | Fish Tissue Threshold (ng/g or ppb) | WQC (pg/L or ppq)
VDH | 100 (Fish Consumption Advisory) | - -
DEQ | 18 (Screening Value) | 640
DEQ’s Water Quality Assessment (Integrated Report)
  VDH - Consumption Advisory = impairment
  DEQ - two or more fish samples exceed screening value at a site or two water samples exceed criterion at a site = impairment
  From: DEQ’s 2022 (Draft) Water Quality Assessment Guidance Manual
For Technical Support call 757.518.2153

## Slide 12: Problem Identification - VDH Fish Consumption Advisory
River basin | Water-body | Section | Locality | Contam-inants | Fish species | Advisory description
James River | James River | From I-95 James River Bridge in Richmond to Hampton Roads Bridge Tunnel, including tidal portions of tributaries | Richmond City, Henrico Co., Chesterfield Co., Charles City Co., Hopewell City, Colonial Heights City, Petersburg City, Dinwiddie Co., Prince George Co., Surry Co., James City Co., New Kent Co., Isle of Wight Co., Newport News City, Suffolk City, Portsmouth City, Hampton City, Norfolk City, Chesapeake City, Virginia Beach City | PCBs | Gizzard Shad, Carp, Blue Catfish ≥32 inches, Flathead Catfish ≥32 inches Blue Catfish <32 inches, Flathead Catfish <32 inches, Channel Catfish, White Catfish, Largemouth Bass, Bluegill Sunfish, American Eel, Quillback Carpsucker, Smallmouth Bass, Creek Chub, Yellow Bullhead Catfish, White Perch, Striped Bass, Bluefish, Croaker, Spot, Blueback Herring, Hickory Shad | Do Not Eat ≤ 2 meals/month
James River | Mill Creek | Entire Creek | City of Hampton | PCBs | Gizzard Shad | ≤ 2 meals/month
James River | Southern Branch | Southern Branch, including tributaries | Portsmouth City, Chesapeake City, Norfolk City | PCBs, Dioxin | Blue Crab | Do not eat crab's hepatopancreas ("mustard"). Crab meat is ok to eat.
http://www.vdh.virginia.gov/environmental-health/public-health-toxicology/fish-consumption-advisory/
Does not apply to swimming

## Slide 13: Problem Identification PCB Impairments Included in 305(b)/303 (d) Integrated Report
*Does not affect swimming
Affected Water Body | Listing Year | Square Miles
Upper James River & Tributaries (tidal fresh) | 2002, 2006, 2008, 2012 | 34.2
Middle James River & Tributaries (Oligohaline) | 2004 and 2006 | 53.8
Lower James River & Tributaries (Mesohaline) | 2004 & 2006 | 143.1
Elizabeth River & Watershed | 2004 & 2006 | 17.0
Source: Rick Browder, DEQ
For Technical Support call 757.518.2153

## Slide 14: Tidal James River Impaired Watershed
For Technical Support call 757.518.2153

## Slide 15: Contaminant of Interest - PCBs
Legacy Contaminant
  Estimated that > 1.5 Billion lbs. manufactured in the U.S. until 1977
Characteristics
  Very stable and heat resistant
  Persistent in the environment
Common uses:
  Transformers, capacitors, hydraulic fluids, circuit breakers, PVC Products, carbonless copy paper, caulking material, paints, and more!
For Technical Support call 757.518.2153

## Slide 16: Total Maximum Daily Load (TMDL)
Pollution Budget
Addresses different pollution categories
PCB TMDL - Multi-media approach
  Air, Land, Water
Existing Load
TMDL
Pollutant Load
TMDL End Point
Margin of Safety
Load Allocations (WLA + LA)
Allocated Load
Goal = Reduce existing PCB load to restore the fish consumption use
TMDL = WLA + LA + MOS
Where:
WLA = Waste Load Allocation
LA = Load Allocation
MOS = Margin of Safety
For restoration the waterbody must meet two thresholds: 1) Numeric WQC [or site specific value] and 2) fish tissue threshold
For Technical Support call 757.518.2153

## Slide 17: The TMDL Process
Identify Problem
Source Assessment
Identify sources
Estimate source loading
Link Sources to Targets
Assess linkages
Estimate total loading capacity
TMDL Allocations
Reduce loads from point sources
Divide remaining loads among
sources
TMDL = Sum of WLA + Sum of LA + MOS
Low Level PCB
Analysis
Fish Consumption Advisory
In Process
To be Completed
To be Completed
For Technical Support call 757.518.2153
Notes: These components are not necessarily sequential steps, but are a guide and framework for TMDL development.
(1) Problem Identification: define key factors and background information for a listed waterbody that describe the nature and impairment. This is the guiding factor in development of the TMDL.
(2) Develop Numeric Targets: measurable indicators and target values that can be used to evaluate attainment of water quality standards in the listed waterbody.
(3) Source Assessment: identify sources of loading for bacteria
(4) Link Targets and Sources: this is necessary in order to develop the TMDL since the linkage defines the cause-and-effect relationship between the pollutant sources and the in-stream pollutant response and allows for an estimation of loading capacity. This relationship can vary seasonally, especially for nonpoint sources that are highly dependent on precipitation.
(5) Load Allocations: pollutant loadings that will not exceed the loading capacity and will lead to attainment of the water quality standard can be determined based on the target/source linkage. The loadings may be distributed or allocated among the significant sources.
(6) Follow-up Monitoring: An ongoing monitoring plan should be included to determine whether the TMDL has resulted in attaining water quality standards and to support any required revisions to the TMDL.

## Slide 18: DEQ TMDL Sampling Approach
Source identification
TMDL model support
    Calibration/validation
2009-2012, 2016, 2020
Water column, sediment
    Water column grab samples: High and Base Flow (n >260)
    Sediment samples as needed

## Slide 19: Sources Considered in the PCB TMDL Development Study
For Technical Support call 757.518.2153

## Slide 20: Sources considered in PCB TMDL
Non-point source
PCB Contaminated
Sediment
Wet Deposition
Dry Deposition
Air Emissions
Non-point source
Runoff
2
Contaminated Sites
1
6
5
MS4 SW Runoff
4
Point Source Effluent
Runoff
3
PCB
PCB
PCB
PCB
PCB
Requires Multi-Media Approach
(land, water, air)
For Technical Support call 757.518.2153

## Slide 21: TMDL Source Category – Point Sources
VPDES Permitted facilities
  Municipal WWTP (6)
  Industrial sources (171)
    Selected based on Standard Industrial Classification (SIC)
      Individual Industrial Facilities
      Industrial Storm Water General Permitted Facilities
  Municipal Separate Storm Sewer System (MS4; 23 + VDOT)
  Combined Sewer Overflow (CSO)
    Richmond
For Technical Support call 757.518.2153

## Slide 22: TMDL Source Category – MS4s
Upper and Middle Tidal James River (Piedmont Region) |  | 
MS4s | Projected PCB Baseline Load (g/yr) | Projected WLA (g/yr)
2 (Phase I – Large) 13 (Phase II - Small) VDOT | TBD | TBD
Lower James River and Elizabeth River Watershed (Tidewater Region) |  | 
MS4s | Projected PCB Baseline Load (g/yr) | Projected WLA (g/yr)
6 (Phase I – Large) 17 (Phase II – Small) VDOT | TBD | TBD
For Technical Support call 757.518.2153
Non-MS4
Tidewater Area MS4 tPCB Data | 
Land Use | Uncensored tPCB (pg/L)
100% single familiy residential | 791.7
100% commercial | 650.6
High density residential | 1,487.5
100% Commercial | 3,382.5
100% Commercial | 1,703.3
100% Commercial | 2,840.0
Residential | 89.3
Light industrial | 626.5

## Slide 23: TMDL Source Category - Contaminated Sites
TSCA-PCB Clean-up Sites (0)
RCRA Corrective Action (9)
CERCLA (11)
Voluntary Remediation/Brownsfield (9)
Landfills
Rail Yards/Spurs
Miscellaneous spill sites
  Pollution Response (PREP)
Electric Utility Transformer Pads
https://commons.wikimedia.org/w/index.php?curid=6092689
https://commons.wikimedia.org/w/index.php?curid=17503186
For Technical Support call 757.518.2153

## Slide 24: TMDL Source Categories
Atmospheric Deposition (example)
Contaminated Sediment
Wet = 4.5 – 12% of total
Modes of Deposition
Rodenburg (Totten), L. A. et al., 2007. Rutgers University
24
For Technical Support call 757.518.2153

## Slide 25: PCB TMDL Fate and Transport Model
For Technical Support call 757.518.2153

## Slide 26: James River PCB TMDL Study
Jian Shen
Virginia Institute of Marine Science
March 30, 2021
For Technical Support call 757.518.2153

## Slide 27: Outline
PCB Transport Processes
Loading estimation
Preliminary model results
Estuarine Model
TMDL Study
For Technical Support call 757.518.2153

## Slide 28: PCB Transport Processes in Watershed
For Technical Support call 757.518.2153

## Slide 29: PCB Transport Processes in Estuary
Ground
water
Transport
Upstream due to stratification
Sorbed to
POC & algae
Sorbed
to DOC
PCB
Settling and
Resuspension
Dissolved
Sorption/desorption
Diffusion
Burial
Atmospheric
deposition
Air-sea
exchange
Runoff
Discharge
Transport downstream
For Technical Support call 757.518.2153

## Slide 30: Estuarine Model
Water
Water column model
Sediment model
Biochemical Reaction
Transport in & out
Loading
Atmospheric exchange
Watershed model
Nonpoint
sources
Point sources
Precipitation
Determine Loading reduction based WQS
TMDL
For Technical Support call 757.518.2153

## Slide 31: Estuarine Model (biochemical processes)
It is a organic carbon-based (sorption/desorption) modeling framework
It couples water column and the bottom sediment
It models exchanges of PCB between Bay water and atmosphere
For Technical Support call 757.518.2153

## Slide 32: Estuarine Model Elements
Tide, Temperature, Salinity, TSS, Meteorological forcing (wind, atm. pressure, dry & wet temperature, cloud cover, solar radiation)
Surface elevation
Current
Temperature
Salinity
Suspended sediment
Dynamic
Model
Carbon
Model
Particulate organic carbon
Algal particulate organic carbon
Dissolved carbon
PCB
Model
Dissolved carbon
Particulate organic carbon
POC bound
Algae bound PCB
DOC bound PCB
Dissolved PCB
Dissolved PCB
POC sorbed
PCB
DOC sorbed
PCB
Loading
Loading
Water column
Sediment
Water column
Sediment
Burial
ATM
Bay
For Technical Support call 757.518.2153

## Slide 33: PCB Model Sorption Processes
Equilibrium model assumes:
Cd
v
v = PCB concentration on the solid / carbon (ng/g)
Cd =dissolved concentration (ng/L)
Dissolved carbon
Particulate carbon
Algae
Dissolved PCB
PCB
The relationships between total PCB, dissolved PCB, particulate carbon bound PCB, algal bound PCB, and dissolved carbon bound PCB are:
fx = fraction of each component
C = total PCB
Partition coefficient differs for different homolog
For Technical Support call 757.518.2153

## Slide 34: Storm Water Measurements
For Technical Support call 757.518.2153

## Slide 35: Simulate PCB based on Selected Homologs
Water tPCB (ng/L)
For Technical Support call 757.518.2153

## Slide 36: Loading estimation
Upstream loading
Atmospheric deposition
Lateral loading
Contaminated sites
Point source/MS4
CSOs
For Technical Support call 757.518.2153

## Slide 37: Atmospheric Deposition
The measured atmospheric deposition on the watersheds in the Chesapeake Bay ranges from 1.6 and 16.3 μg/m2/year (CBP, 1999)
Total PCB wet and dry depositions were 1.1 and 1.0 kg/year, respectively for the James River below the fall line (CBP, 1999).
The estimated total PCB atmospheric deposition rate is 3.08 (μg/m2/year).
An approximate 1-2% deposited PCB on watershed will discharge to the estuary (Totten et al. 2006, Delaware River )
The estimated loading is about 569 g/yr (assuming 2% runoff) below the fall line
Direct PCB deposition on the surface of Estuary is about 1,056 g/year
Current net transport between atmosphere and water is out (loss PCB to atmosphere)
  Total PCB gaseous concentrations is about 330 pg/m3 (0.3 pg/l). Mean PCB concentration is about 15,560 pg/l
For Technical Support call 757.518.2153

## Slide 38: Upstream Loading Estimation
Assuming atmospheric deposition rate is 3.08 ug/m2/year, 2% runoff, the estimated loading are 1,051 g/year
Regression estimation are 1,027 (low) and 2,327 (high) g/year, respectively from 2005-2014. Model input using high estimation based on regression
For Technical Support call 757.518.2153

## Slide 39: Watershed Model Approach
The watershed model will be used to simulate non-point sources loadings based on land uses below fall-line
Watershed is divided into multiple segments
Major pollutant sources
  Contamination sites
  MS4/Storm water
  Background source (land use)
For Technical Support call 757.518.2153

## Slide 40: Watershed model: Using land use
For Technical Support call 757.518.2153

## Slide 41: Contaminated and Remediated Sites
11 sites have PCB concentration (total 48)
Using watershed modeled flow and area, the loading can be estimated assuming PCB concentration is constant
For sites without concentration, mean concentration will be used
Estimated loads are 19.3 and 983 g/year using median and mean concentrations, respectively
Final loading will be adjusted based watershed model and observations
For Technical Support call 757.518.2153

## Slide 42: CSOs (Richmond)
Loadings Derivation Current Condition
  Utilize monthly average flows (10 yr. period) and mean PCB concentration is 11,906.7 pg/L.
64,367 pg/L
938 pg/L
For Technical Support call 757.518.2153

## Slide 43: Watershed model: Point Sources
Upper JR for PRO mtg ~ 145 facilities; Lower JR and Eliz River ~ 177 facilities
Combined point source
(~322)
Loading is estimated based on drainage area, measured flow and typical concentration
For Technical Support call 757.518.2153

## Slide 44: MS4 Loading Estimation
Use watershed model to simulate loadings from urban land uses
Adjust loading based on observations for different land uses
For Technical Support call 757.518.2153

## Slide 45: Preliminary model results
Location of Observations for model calibration
For Technical Support call 757.518.2153

## Slide 46: Preliminary model results: Example
For Technical Support call 757.518.2153

## Slide 47: PCB budget
Combine model simulations and loading estimation to estimate the PCB budget and determine load reduction
Shen et al., 2012
For Technical Support call 757.518.2153

## Slide 48: TMDL Study
Use water quality standards (WQS) to conduct TMDL with target source reduction (point, nonpoint, MS4, contaminated sites etc)
Large portion of PCB is from the bottom sediment deposition. It will take time for the water quality condition of the estuary to meet the WQS
TMDL simulation
  Using representative flows (high, mean, low) to run model for a sufficient time (advantage: including resuspension, deposition processes)
  Using harmonic flow (advantage: mean condition)
Mean tPCB in Baltimore harbor
(Shen et al. 2012)
For Technical Support call 757.518.2153

## Slide 49: Flow Distribution
Harmonic flow (2010)
Select 3-year flow
For Technical Support call 757.518.2153

## Slide 50: Proposed Procedure for Loading Allocation
Allocate loads (WLA (MS4) and LA) for each jurisdiction
  City, county, federal land, VDOT, and other specific units (e.g. university)
  WLA for point source is estimated based on permitting
The regulated area for each jurisdiction is determined by the GIS layer for each city, or county, or federal land
  Regulated area includes both pervious and impervious lands
  VDOT is excluded from City/County GIS layer
  Federal lands are excluded from City/County GIS layer
Estimate loading for each Jurisdiction
  Option I:
    Compute the percentage of regulated area to total jurisdiction area for each modeled sub-watershed
    Use the percentage to partition the total loading for each sub-watershed
    Sum loads for all sub-watershed
  Option II:
    Same as option I, but estimate loading based on land use and partition the loading based on percentage of the land use for each jurisdiction area
    This method is more difficult, but it does not provide better estimation as we don’t have very good data set to calibrate loading for each land use
For Technical Support call 757.518.2153

## Slide 51: Climate Change Consideration
Sea-level rise (0.22 cm, and 0.86 psu) at James River mouth
Increase of salinity intrusion
Change in estuarine circulation
Changes in discharge
Change in residence time
Increase temperature (~0.9-1.2 C)
Increase growth rate
Increase respiration rate
Change in grazing
Transport processes
For Technical Support call 757.518.2153

## Slide 52: Temperature Effect on Growth and Respiration Rates
Testing cases
Reduced respiration
Revised curve for diatom
Use 2 curves for summer green
Use Eppley curve
Change grazing
Respiration rate changes faster than growth rate when temperature increase.
The temperature increases in summer due to climate change ranges from 1-2 Co, and the growth rate does not increase fast enough and Chl-a could decrease.
If a high growth rate is used, the model calibration is not satisfactory in the James River
For Technical Support call 757.518.2153

## Slide 53: Evaluation Impact due to Transport or Temperature
Change in transport
Change in temperature
Blue lines are current condition and red lines are under changed condition
For Technical Support call 757.518.2153

## Slide 54: Climate Change Consideration
Minor changes in Chl a and organic carbon
Increase depth (volume increase will reduce concentration)
Increase salinity and gravitational circulations
It is not expected Climate change will impact on PCB TMDL significantly
Model simulation of algae and carbon for James River Chl a project provides all the dynamics and organic carbon results. We can conduct similar simulations if it is needed.
For Technical Support call 757.518.2153

## Slide 55: VPDES Load Calculations
For Technical Support call 757.518.2153

## Slide 56: General Approach to Point Source Loads
Applicable to:
  Municipal Wastewater Treatment Plants
  Industrial Stormwater General Permits
  Industrial Individual Permits
Existing loads and wasteload allocations (WLAs) are calculated on a spreadsheet outside of the TMDL model
  Integrated into the TMDL model
Calculated in a standard fashion for all PCB TMDLs
  Provides for consistency and certainty
  Clearly communicates the assumptions of the TMDL WLA
Load = concentration * flow
For Technical Support call 757.518.2153

## Slide 57: PCB Concentrations Used for Establishing Point Source Loads
“Existing Condition” load
  Preference to use Permittee generated PCB data
    Corrected in accordance with TMDL GM 14-2004
  In lieu of available PCB data, default concentration used
    Derived from statewide PCB data using Standard Industrial Classification (SIC)
Waste Load Allocation (WLA)
  Utilize TMDL endpoint PCB concentration
    Applicable sub-watershed
For Technical Support call 757.518.2153

## Slide 58: Point Source Flow Matrix
Wastewater Type |  | PCB Conc. and Discharge Flow (Used for Calculation of Baseline Loads & WLAs)
Municipal |  | Design Flow (Used for WLA)
 |  | Eight Years Monthly Ave Flow (Used for Baseline Load)
* Industrial Storm Water General Permits (ISWGPs) |  | Flow calculated from inputs including industrial activity acreage and impervious acreage acreage
*Individual Industrial | Process Water | Baseline Load uses Mean of DMR monthly average flow WLA = Mean of DMR daily max flow
 | Comingled (process water can’t be separately measured from SW) | 
 | Storm Water | Acreage applicable to outfall drainage area (industrial activity acreage and impervious acreage)
*A single baseline load and WLA is calculated from each applicable facility regardless of the number of outfalls.
For Technical Support call 757.518.2153

## Slide 59: TMDL Endpoints
For Technical Support call 757.518.2153

## Slide 60: State Water Quality Standards Has Two Values
 | Fish Tissue Threshold (ppb) | WQC (ppq)
VDH | 100 (Fish Consumption Advisory) | - -
DEQ | 18 (Screening Value) | 640
DEQ’s Water Quality Assessment (Integrated Report)
  VDH - Consumption Advisory = impairment
  DEQ - two or more fish samples exceed screening value at a site or two water samples exceed criterion at a site = impairment
TMDL has two endpoints
TMDL must be consistent with the WQS, not the VDH threshold
For Technical Support call 757.518.2153
Notes: VDH value also contains Exposure Duration Factor in the numerator = Life expectancy/expected time lived in a single location
Consumption rate
  DEQ = 22 g/day
    Updated by EPA in 2015 based on the Exposure Factors 2011 handbook.
    90th percentile consumption rate of fish from inland and nearshore waters for adults 21 year and older (2003-2010)
  VDH = 15 g/day
    (227 g/meal) 2 meals a month 30 days in a month

## Slide 61: Narrative WQS
For Technical Support call 757.518.2153

## Slide 62: Biannual Water Quality Assessment Guidance
Guidance memo developed for each Assessment Cycle
  Appendix E-1 Contains Fish Tissue Values for Non-Carcinogen and Carcinogen Criterion Based Tissue Values (TV)
  2016 (GM No. 16-2005) – 9/6/2016
  2018 (GM No. 16-2005) – 3/5/2018
  2020 (GM No. 19-2001) – 7/12/2019
    [footnote] These fish tissue values have been calculated based on the Water Quality Standards that are associated with the latest Triennial Review criteria proposals as adopted by the State Water Control Board in October 2008.
  2022 (GM No. XXX ) –
  Undergoing final internal (DEQ) review
    Public noticed January 19th – February 18th (2021)
Forthcoming Triennial Review
  From 0.00064 ug/L to 0.00058 ug/L
PCB Total/congeners | 1336-36-3 |  | 20
PCB Total/congeners | 1336-36-3 |  | 20 18
For Technical Support call 757.518.2153

## Slide 63: VA Water Quality Criterion
VA PCB criterion and Fish Screening Values based on EPA guidelines
Fish Screening Value basis of criterion
  Water concentration translated using a Bioconcentration Factor (BCF)
    Lab derived translator developed in the early 80’s
    Assumes fish only obtain PCBs through gills from the water column (ratio of PCB conc. in fish to that in water)
      What about other exposure pathways?
For Technical Support call 757.518.2153

## Slide 64: PCBs and Water Partitioning
Homolog | Midpoint Kow
Mono+Di | 47,315
Tri | 266,073
Tetra | 1,011,579
Penta | 3,349,654
Hexa | 5,370,318
Hepta | 17,179,084
Octa | 39,810,717
Nona | 82,224,265
Deca | 151,356,125
Kow values of PCB homolog groups
More Hydrophobic i.e., less Dissolved
For Technical Support call 757.518.2153

## Slide 65: Bio magnification
0.001
1
1,000
10,000
20,000
x1000
x100
x10
x2
Biomagnification
Concentration (parts per trillion)
PCBs
H2O
For Technical Support call 757.518.2153

## Slide 66: PCB Endpoints
Bioaccumulation and Bioconcentration Concepts
  Bioaccumulation refers to “the uptake and retention of a chemical by an aquatic organism from all surrounding media (e.g., water, food, sediment).”
  Bioconcentration refers to “the uptake and retention of a chemical by an aquatic organism from water only.”
“For some chemicals (e.g., highly persistent and hydrophobic), the magnitude of bioaccumulation by aquatic organisms can be substantially greater than the magnitude of bioconcentration.”
“…EPA encourages States and authorized Tribes to derive BAFs that are specific to certain regions or waterbodies, where appropriate.”
For Technical Support call 757.518.2153

## Slide 67: Average Fish Tissue Concentration vs. Average Water Concentrations
Chart: Elizabeth River Zone
 | 1
 | 640
Chart: Lower James River (RM 21 - 0 ) Zone
| 19.550776513522674 | 75.848145113849995 | 40.651933211260001 | 127.31747653017001 | 7.7385403575952223 | 72.459143315167992 | 22.185350725559744 | 14.640831149290641 | 61.918183941470005 | 1.99897561806341 | 130.34930017112183 | 37.661012569700006 | 34.991551105619997
 | 393 | 393 | 323 | 323 | 323 | 323 | 323 | 323 | 218 | 218 | 218 | 218 | 218
 | 1
 | 640
Average H2O tPCB (pg/L)
Quadrant | Water | Fish
A | Fail | Pass
B | Fail | Fail
C | Pass | Pass
D | Pass | Fail
B
A
D
C
A
C
D
B
For Technical Support call 757.518.2153

## Slide 68: Bioaccumulation Factors (BAFs)
EPA Method (EPA-822-03-030, 2003)
Utilize site specific data (i.e., water data) to reflect exposure of fish and their food
  Pathways of PCB exposure includes through gills, from food, and indirect ingestion of contaminated sediment
More realistic
Precedent (PCB TMDLs)
  Potomac River
  Roanoke River
  Levisa Fork
  New River
For Technical Support call 757.518.2153

## Slide 69: BAF Process in a Nutshell
BAF values are calculated for each fish species in a TMDL watershed
The TMDL endpoint is based on some average of selected fish species BAF values
For each fish species: Ratio of Water PCBs and Fish Tissue PCBs
Within the home range of a fish species
Within a TMDL watershed
For each fish species: Normalized for freely dissolved PCBs and fish tissue lipid content
For each fish species: The median of home range values
For each fish species: Normalized by median fish lipid content and freely dissolved PCBs
For each fish species: Normalized values divided by fish tissue threshold value
(18 ppb)
For Technical Support call 757.518.2153

## Slide 70: BAF Endpoint Selection
BAFs are calculated for each fish species in the four TMDL watershed sections
  Upper tidal JR, middle tidal JR, lower tidal JR, and Elizabeth River
  If select a site-specific endpoint, would be based on recreational/commercial interest, fish advisory, or as an example, use arithmetic mean of species
Upstream reductions from the James, Jackson, Maury River PCB TMDL will likely impact the fall-line load in upper tidal JR
  Different modeled scenarios can be run to assist with endpoint selection
DEQ exploring a draft endpoint revision based on comments received
  Appropriate fish cutoff (year fish collected)
  Changes in analytical methods
For Technical Support call 757.518.2153

## Slide 71: Anticipated TAC Meeting Timeline
2021 2022
1st Public Meeting
(Feb. ‘21)
1st Technical Advisory Subcommittee Meeting
(Mar. ’21)
2nd Technical Advisory Subcommittee Meeting
(Summer ’21)
3rd Technical Advisory Subcommittee Meeting
(Winter ’21)
Final Public Meeting
(Winter ‘22)
Sources and Endpoints
Draft TMDL Allocations
Draft TMDL Report
For Technical Support call 757.518.2153

## Slide 72: Next Steps
Public comment responses
TAC contact list
Watershed Modeling
  Spring/Summer 2021
Anticipated future TAC meetings
  TAC 2 - Summer 2021
  TAC 3 - Winter 2021
Meeting Feedback
  Virtual Meeting Comment Form
Overall: Mark.Richards@DEQ.Virginia.gov
Piedmont: Mary.Haley@DEQ.Virginia.gov
For Technical Support call 757.518.2153